## Slide 1: WP PWIE ADC KOM introduction S. Brezinsek and G. Calabro

## Slide 2
WP PWIE STRUCTURE

## Slide 3
WP PWIE => DEMO input
Initial ADC modelling and engineering assessment by 2022
(max. 2024 under discussion / include WP TE results about AUG top divertor
After divertor decision strategy: transfer to WP DES (DCT) and WP DIV to next level of optimisation
PWIE studies in TSVV7 with input from ADC / TE in charge of experiment exploitation
I-DTT => divertor selection by the end of the year if present ENEA timeline prevails

## Slide 4
Compare the merits of different ADC solutions to show a “gain” vs. reference SD (SND)
Proposal: utilise a spider diagram
Identify most critical
  Physics Quantities
  Engineering Quantities
Quantification type
  Hard numbers (e.g. impurity concentration)
  Soft information (e.g. RH compatibility)
Comparison
  Always reference to SD
  Direct comparison between ADCs
No real numbers – concept only
Outcome: Comparison of ADC solutions along a
clear set of criterions (if modelling available)

## Slide 5
Plasma Modelling Activities for DEMO I
Abandon in the moment development/tests of turbulence code => back to TSVV and TE (review end 2022)
Focus on SOLPS-ITER usage + Optimisation tool
Best explored advanced configurations: SD, XD, SXD
SOLPS-ITER so far only with fluid neutrals and standard grid option:
Update of SOLPS-ITER regarding wide-grid option and kinetic option (EIRENE)
  Benchmark against old „best case“ for SD, XD, SXD => first input to TSVVs as case
  Benchmark experiments and modelling within WP TE
Comparison of neutral modules regarding impact of neutrals and calculation speed (SD, XD, SXD)
  full fluid (improved)
  hybrid kinetic/fluid
  full kinetic options (same cases as above)
Hand-over options to DIVGAS for pumping assessment
Outcome:
Clarification regarding missing x-point radiaton in fluid kinetic simulations
Confidence in existing modelling (large matrix) => new runs with time/precision optimum
SOLPS with EIRENE as input for PWI studies in TSVV 7

## Slide 6
Plasma Modelling Activities for DEMO II
Moderate exploration of hybrid configuration solutions / optimisation procedures between SD, XD, SXD
Best suited SOLPS-ITER version (fluid neutrals?) to study configuration hybrid solutions:
small matrix of runs: Ar / D2 scan | check if physics benefits remain
  Hybrid between SN and XD (no existing)
  Hybrid between SN and SXD (exist / same inner target / different outer target)
Outcome:
Optimisation with respect to baseline solution at low cost in change, but high impact
Qualification of optimisation tool which can be applied to other ADC designs
Apply iterative SOLPS-ITER optimisation technique to identify optimum solution regarding power handling and magnetic configuration realisation: target tile shaping, leg length, and magnetic shape (KU LEUVEN)
  Test run with target shaping SN or XD (separate)
  Test run with leg length between SN and SXD
  Test run with all optimisations combined
Best cases could be analysed regarding engineering properties
  envelope already given / focus on optimisation (control power / vertical stability)

## Slide 7
DN / DND
Less explored configuration regarding experiment / modelling
Optimise modelling with improved SOLPS-ITER ? Include lessons learned from challenging experience with existing SOLPS-ITER runs for DND in EAST
Clarify how to compare with other single divertor configurations regarding exhaust improvement?
  2 identical divertors / oscillation?
  Comparison with existing experiments essential to assess (no) benefit found in first DEMO runs
Assess control and stability issues for DEMO?
Can the divertor be split and inner divertor remain for wall lifetime in? Outer divertor leg exchange separate?
WEST as available European benchmark facility to gain data and experience? EAST /DIII-D / TCV?
Combine experimental studies with control questions in long-pulse operation
Currently physics issues as device with equivalent divertors (shape / pumping) rare
Potential collaboration with new EAST W divertor experiments under revised EU-CHN partnership?
Next step ADSDEX Upgrade … COMPASS-U … DTT?
Requires WP TE and human resources on experimental and modelling side
Dedicated project activity? Funding? Timescale

## Slide 8
Less explored configuration regarding modelling
SOLPS-ITER modelling seems very challenging for DEMO runs in SF
Can we expect improvements with new SOLPS-ITER?
TCV as available European benchmark facility with a lot of data
Test with new SOLPS-ITER version for TCV or SOLPS-ITER predictions for ASDEX Upgrade
Return to DEMO predictions if successful and stable (KU Leuven)
Parallel on engineering side: clarify if there is any chance of realisation regarding control and coils
Requires WP TE and human resources on experimental and modelling side
Dedicated project activity? Funding? Timescale
SFD / SF+ / SF-

## Slide 9
I-DTT timeline and divertor selection …
The given timeline for the first divertor in I-DTT is (in my view) currently not compatible with the plan to test the BEST ADC solution for DEMO (within the EUROfusion program)
Potential compromises / solutions
a) The first I-DTT divertor – if DTT in time - could be selected out of the “mature SD, XD, SXD” group
  SD would mean a conventional divertor, but maybe with advanced PFC/M concepts (other then ITER)
  A hybrid solution between SD and XD or SXD might be an option to follow with the first divertor
  showing some benefit over the SD (optimisation tool via SOLPS-ITER could be used)
  Validate the improvement and tools / not necessary the best DEMO solution
  This option rules out SFD and DN
b) The first I-DTT divertor CONCEPT – if DTT in time - could be a DN solution utilising an upper and lower divertor out of the “mature SD, XD, SXD” group or hybrids between them.
  One could use a SN reference lower divertor and an optimised upper hybrid SD-XD or SD-SXD divertor
  Allows to compare directly different divertor solutions and benefits including DN
  Note upper and lower divertor could be splitted in time for installation if we say it is a DN test
  This option rules out the SFD
c) The first I-DTT divertor – if delayed - could be selected out of a wider portfolio of concepts including SFD
  Which one to choose and when?
  What do we want to test for DEMO? Concept? PFCs? Stability? Scheme? Engineering?

## Slide 11
Feature | Potential benefit | Configuration
Longer connection length | Larger collisionality and hence easier access to high-radiation and detached regimes, lower Ttarget, more room for radial transport. | SXD; XD; SFD
Larger poloidal flux expansion | Passive stabilization of detachment front (via different mechanisms), increased connection length and wetted area. | SXD (difficult in DEMO); XD
Larger toroidal flux expansion |  | SXD
Multiple X-points | Splitting of energy and particle fluxes to multiple targets, Stabilization of the radiation front outside the core, in SFD increased connection length, in DND topological separation of the inner divertor. | DN; SFD
Status

## Slide 12
DN:
show simultaneous control of two detached divertors (best, but not necessary: symmetric pumping and geometry, probably not by controlling drsep) at relevant heat flux in experiments
devise modelling scheme that gives reliable comparison to SND and others (not really the case so far(?)) and quantify physics gain
engineering: quantify (dis)advantages (vertical stability, TBR…)
SFD:
Get a converged code run to compare operational window
Is it ruled out due to control problems (both SF+ and SF-)? Or deferred infinitely?
SXD:
Is there physics value to combine it with an XD (flux expansion at target)? What would be the impact on engineering (coils)?
Strategy to validate the predicted gain in operational space (theory & experiments)?
Disscusion from Joint Meeting of FTD and FSD
(Zohm/Federici/Naulin/Brezinsek/Neu/Wischmeier/Wiesen/Maviglia …):
ADC configuration issues (summarised by Hartmut):