## Slide 1
Plans for 2021-2022
E. Nardon, TSVV9 Progress Meeting, 06/05/21
Finalize and submit for publication my work on post-TQ injection (SPI or other) to deplete small RE seeds https://arxiv.org/abs/2007.01567
Participate in developments and tests of JOREK
  2 temperature (Ti/Te) model
  Particle-based impurity model relaxing coronal equilibrium assumption
  Solve/understand energy conservation issues and mysterious/suspicious flow patterns associated to MGI
  Model families…
Continue JOREK simulations of Ar MGI in JET 85943
  Apply new models (Ti/Te, particle-based impurity model)
  Test improvements to solver (→ faster simulations / better resolution?)
  Try to run into the CQ! (and observe reconstruction of flux surfaces…)
Animate/coordinate work on disruptions with JOREK
  Monthly meetings with a growing team of disruption modellers
  Supervise Sarah Sadouni (postdoc at CEA): investigations on current profile relaxation (3D or equivalent 2D with hyper-resistivity, including for JET 85943)

## Slide 2
Further investigate pure H2 SPI in ITER with JOREK
  Assess consistency with DREAM and INDEX simulations
  Use a better description of background impurities
  Simulate 2nd (Ne) SPI
  Use test particles to check that hot tail generation is negligible (when improved collision model ready)
  Note:
    Effect of pre-existing islands planned being investigated by F. Wieschollek at IPP Garching
      On ASDEX Upgrade sims. so far
      ITER sims. planned, to be confirmed
    Validation work ongoing by Mengdi Kong for JET and Sang-Jun Lee for KSTAR