## Slide 1: Overview and status of SOLPS DEMO activities within the DEMO Central Team
S. Wiesen
May 11th 2021

## Slide 2: DEMO physics in EU Framework Programme 9 (FP9, 2021-25/27)
Transport F. Köchl
S. Wiesen | TSVV-7 KoM | May 11th , 2021| Page 2

## Slide 3: Plasma System Division (PSD) WPDES - Exhaust
Divertor Design studies
Core-edge coupling
Wall models
Time-dependent SOL/edge models
ADC (WP-PWIE)

## Slide 4: Employment of SOLPS-ITER: from ITER to DEMO
ITER design changed in 2013 to full-metal walls, now completed
Design required considering the most severe target loading conditions for engineering specifications (PSOL = 100 MW, D(T) plasmas with impurity seeding)
Since 2014: New SOLPS-ITER code for divertor design
ITER: Emphasis is to widen the existing simulation database to other operational scenarios (low-power plasmas, limiter phase start-up, H/He plasmas, seeding…) and including refinements of the underlying physics model (wide grids, drifts, currents, transport models, possible systematic errors, …), i.e. features not originally in SOLPS4.3  SOLPS-ITER

## Slide 5: Revised ITER Divertor Design studies: metal wall & SOLPS-ITER
R.A. Pitts, E. Kaveeva, V. Rozhanski, S. Wiesen, X. Bonnin et al, NME 2019
PSOL=100MW

## Slide 6: Early assessment for DEMO
SOLPS4.3, Kukushkin Pacher 2007-2009
D/He/Be +
Ne-seeding
PSOL = 300MW
Density control by Core + Gas fuelling

## Slide 7: Early assessment for DEMO
SOLPS4.3, Kukushkin, Pacher 2007-2009
Full detachment of inner divertor restricts pPFR
Criterion: max Te at inner target falls below certain minimum, i.e. < 5eV
For DEMO: pPFR,max = 18.6 Pa

## Slide 8: Re-assessment with new SOLPS-ITER
Work only started in FP8: F. Subba EU-DEMO  WPDES
SOLPS-ITER model parameters
  Input power into edge: 150 MW
  D-puff: 1e23 atoms/s (~ 200 Pa m3 s-1)
  Minor D pellet volumetric source: 7e21 (s-1)
  D+He+Ar plasma
  Ar puff: 1.5e19 atoms/s
Zeff ~1.9 in the core
HFS
LFS
HFS deeply detached
Low temperatures; <1eV at max particle flux/density
Negligible heat flux ~ 1MW/m2
LFS partially detached
temperature low @ strike-line < 1.5eV
Heat-flux max 2MW/m2
Assessment of several control parameters, together with satisfying a number of constraints (e.g. power loading and core He density or radiation)  establishment of DEMO operational windows and SOLPS-ITER based scalings
Extension towards EU-DEMO design: e.g. include XPoint radiation (demonstrate validaity of model first, e.g in WPTE!), Add physics: inclusion of drifts, line emission opacity, neutral buffering, etc
later include also high candidate ADCs (e.g. DDN)

## Slide 9: Plasma System Division (PSD) WPDES - Exhaust
Divertor Design studies
Core-edge coupling
Wall models
Time-dependent SOL/edge models
ADC (WP-PWIE)

## Slide 10: Previous ASTRA/SOLPS4.3 coupling
Core & pedestal:
ASTRA/ICPS model
MMM/Weiland models, shear stabilised; JET/AUG
Edge:
SOLPS4.3 setup as in ITER – but no direct coupling
Provide ASTRA with ni/Ti,e DT/He fluxes at spx
Derived scalings for point-of-detachment, i.e.:
H.D. Pacher, G.W. Pacher, A.S. Kukushkin, G. Janeschitz DEMO conceptual study EFDA TW6-TRP-002

## Slide 11: Numerical assessment of integrated DEMO operational space
H.D. Pacher, G.W. Pacher, A.S. Kukushkin, G. Janeschitz DEMO conceptual study EFDA TW6-TRP-002
DEMO operating window, I=21 MA, Ne seeding feedback
Review ASTRA/SOLPS-ITER coupling: functionality and code-implementation (e.g. same functionality as in ASTRA/SOLPS5.0 coupling), versioning
Interface requirements: Assess overlapping computational region between SOLPS-ITER (2D) and ASTRA (1D); identification of an improved scheme to couple; improved pedestal model (i.e. including core radiation)

## Slide 12: Plasma System Division (PSD) WPDES - Exhaust
Divertor Design studies
Core-edge coupling
Wall models
Time-dependent SOL/edge models
ADC (WP-PWIE)

## Slide 13: CX and photon fluxes on (ITER) first wall components
Breakdown of problem: ITER
Also: photons and radiation loads possible
Collaborative work WPDC, W. Biel

## Slide 14: CHERAB DEMO First Wall Estimated Loads
Calculations on TQ mitigated Disruptions (or VDEs)
Assessment of active mitigation techniques
Initial thermal energy Wth=1.3GJ: 20% radiated @ pre-TQ at MGI/SPI  1GJ remaining
Analysis including averaging techniques
Some relevant differences observed:
  More uniform load distribution
  Estimated peak load appears smaller by about 33%
  Higher accuracy
F. Maviglia, IAEA-TM 2020
Prad=800GW
Collaboration WPPWIE & TSVV-7
Continuation requires SOLPS-ITER w/extended wall option (not validated yet); comparison with other models (e.g. SOLEDGE2D)
Development of numerical diagnostics for heat-fluxes in DEMO: CX and photon fluxes on walls (energy spectra, angular distribution)
Comparison CHERAB vs EIRENE; (disruptions/VDEs)  RACLETTE finalization of off-normal radiation loads task
3D field line tracing codes to estimate charged particle HF (PFCflux – SMARDDA) Later: kinetic models of 3D structures (e.g. toroidal/poloidal gap analysis
Long term: Towards numerical optimization of first wall, steady-state & transients (e.g. disruptions/VDEs), impact on wall, W droplets (MEMOS-U)

## Slide 15: Plasma System Division (PSD) WPDES - Exhaust
Divertor Design studies
Core-edge coupling
Wall models
Time-dependent SOL/edge models
ADC (WP-PWIE)

## Slide 16: Example: Re-attachment in DEMO
The maximum tolerable steady-state HF on the current DEMO SN divertor plate is 10 MW/m2. This value can be achieved only in detached plasma conditions (with seeded impurities).
In case of accidental divertor reattachment, the divertor reaches burn-out (leading to an in-vessel LOCA) in about 3 sec.
Divertor sweeping (to be activated only in emergency cases) to allow the divertor surviving while the current is ramped down [Maviglia, FED 2016]. Needs the presence of IVC.
Siccinio, NF 2019, RACLETTE

## Slide 17: Advanced Fluid Neutral Model application to ITER
TSVV-5
Re-attachment/re-detachment studies; requires input from WPTE expts
Time-dependent option in SOLPS-ITER: issue: explicit-implicit coupling of plasma-fluid and neutral Monte-Carlo
Exploit advanced fluid-models in SOLPS-ITER for time-dependent simulations (without EIRENE); integration with core-codes (e.g. ASTRA)
Interaction related ETASC TSVVs (flight simulators, scenario integration) and ENRs on model reduction (e.g. generative neural-networks) as alternative model

## Slide 18: Plasma System Division (PSD) WPDES - Exhaust
Divertor Design studies
Core-edge coupling
Wall models
Time-dependent SOL/edge models
ADC (WP-PWIE)

## Slide 19: ADC
Mainly covered by WPPWIE/ADC and WPTE (physics)
Extension of FP8 activities (c.f. F. Militello et al, ADC report 2021, WP-DTT1 and WP-DTT1/ADC) - SOLPS-ITER
Requires speed up and/or validated reduced physics models
Extension of WPDES activities towards ADC scenarios, e.g. DN, SXN. Later on
Cyclic monitoring of DCT into WPPWIE/WPTE activities: focus on demonstration of ADC being a possibility for DEMO  input gate review 2024
Work with groups who work on advanced fluid models (e.g. TSVV-5) and numerical divertor optimisation techniques (e.g. Univ. Leuven, adjoint optimisation techniques)  WPPWIE (possible combined PWIE-DES EEG)
Later: assessments of engineering limits for ADCs: transients and configurations (e.g. sweeping etc)

## Slide 20: Summary
Divertor Design studies
Core-edge coupling
Wall models
Time-dependent SOL/edge models
ADC (WP-PWIE)

## Slide 21: backup

## Slide 22: Lessons learned ITER divertor design
SOLPS4.3 has been the main workhorse for the ITER divertor design studies since 20+ years
Physics operating mode for the ITER divertor is to a large extent based on plasma boundary simulations conducted over ~15 years with the SOLPS-4.3 code (B2-Eirene)  mostly C targets!
  A. S. Kukushkin et al. J. Nucl. Mat. 290-293 (2001) 887
  A. S. Kukushkin et al. Nucl. Fusion 42 (2002) 187
  A. S. Kukushkin and H. D. Pacher, PPCF 44 (2002) 931
  H. D. Pacher et al. J. Nucl. Mat. 313-316 (2003) 657
  A. S. Kukushkin et al. Nucl. Fusion 43 (2003) 716
  A. S. Kukushkin et al. Fus. Eng. Design 65 (2003) 355
  A. S. Kukushkin et al. Nucl. Fusion 45 (2005) 608 A. S. Kukushkin et al. J. Nucl. Mat. 337-339 (2005) 17
  A. S. Kukushkin et al. Nucl. Fusion 47 (2007) 698
  A. S. Kukushkin et al. J. Nucl. Mat. 363-365 (2007) 308
  G. W. Pacher et al. Nucl. Fusion 48 (2008) 105003
  H. D. Pacher et al. J. Nucl. Mat. 390-391 (2009) 259
  A. S. Kukushkin et al. Nucl. Fusion 49 (2009) 075008
  A. S. Kukushkin et al., J. Nucl. Mat. 415 (2011) 2011
  H. D. Pacher et al. J. Nucl. Mat. 415 (2011) S492
  G. W. Pacher et al. Nucl. Fusion 51 (2011) 083004
  A. S. Kukushkin et al. Fus. Eng. Design 86 (2011) 2865
1996
2001
2009

## Slide 23: Early assessment for DEMO
SOLPS4.3, Kukushkin, Pacher 2007-2009

## Slide 24: Erosion vs Deposition on the ITER port-plug faces
V. Kotov NF 2016

## Slide 25: Hierarchy of neutral models
TSVV-5

## Slide 26: What else can cause a loss of detachment?
Well, many things…
Fluctuations in the separatrix density.
Fluctuations in the separatrix power (e.g. pellet induced transient a-particle heating)
Combinations thereof.
Technical failure (e.g. impurity puff valve).
Control failure.
…others…
[Wiesen, NF 2017]
Impurity radiation control required
ITER/JINTRAC

## Slide 27: ITER exaple: pellet induced re-attachment
High density
Short bursts of re-attachment during pellet ablation
Such simulations help to predict and mitigate impact of unavoidable transients in HF  ITER & DEMO divertor engineering and operational design

## Slide 28: Issue of particle balance / explicit-implicit coupling  long convergence times
A. S. Kukushkin et al. Fus. Eng. Design 86 (2011) 2865

## Slide 29: W droplets lifetime in DEMO – preliminary results
ITER vessel geometry with a full W wall, ITER mitigated VDE profiles with late Ne gas injection during the current quench
Isotropic W droplet injection from the plasma-wall contact point during a 4 ms window after the thermal quench, with initial radii 10-150 µm and initial speeds 0-70 m/s
 Out of the injected droplet MASS, roughly 40% vaporizes, 40% re-solidifies into dust and 20% ends up as liquid splash on wall