## Slide 1: UQ, SDTrim-activities and Ravetime
Udo von Toussaint
TSVV7 Kick-off meeting, May 2021-05-11
UQ
SDTRIM
Ravetime
Notes: 1

## Slide 2: TSVV…
T heory
S imulation
V erification
V alidation

## Slide 3
Interplay of Simulation – Verification - Validation
physical model of system -
Theory
mathematical model
numerical model
computer
simulation
validation
Simulation-based decision making
e.g. design, control, operations,
material selection, planning
scalable algorithms & solvers
data/observations
(actual )
(multiscale) models
advanced geometry &
discretization schemes
- parameter inversion
- data assimilation
- model/data error
control
- uncertainty
quantification
visualization
data mining/science
optimization
stochastic models
uncertainty quantification
verification
approximation / error control

## Slide 4
Typical challenges in simulation based models:
Aleatoric and epistdemic uncertainties
Medium to large number of uncertain inputs
Non-linear interactions possible / likely
    Uncertainty (Reliability) of results?
Increasing awareness of importance: cf. transport shortfall
UQ-methods for computer models
Validation
Notes: So, if you don’t know the solution, how do you test?

## Slide 5: Methods in Uncertainty Quantification
Common Approaches to Uncertainty Quantification
  Sampling (Monte Carlo methods) : simple, too expensive, lack of higher order info
  Spectral Expansion (Polynomial Chaos Expansion)
    Non-Intrusive Approach
    Intrusive Approach: complete code rewrite
  Surrogate models (eg. Gaussian processes)

## Slide 6: Methods in Uncertainty Quantification
Spectral Expansion (Polynomial chaos expansion)

## Slide 7: Sensitivity Assessment
Polynomial chaos expansion: Sensitivity to input variables
Once the Polynomial Chaos expansion is available, the full set of Sobol indices are obtained for free

## Slide 8: Validation requires UQ
How to realize UQ within project?
PCE requires multiple code runs at dedicated parameter settings
  Attempts for dedicates libraries & framworks exists : most are hampered by code complexity & ressources
  However, IMAS needs/requires this capability anyway
Establish UQ capability (massiv # of parallel runs) at a generic level
  Requires early contact with responsible ACHs
  Identification of pilot project
Notes: 8

## Slide 9: SDTrimSP in a nutshell (1)
How does it work / what can it do?
Can describe particle bombardment of targets based on binary collision approximation [1,2]
Applicable in eV – MeV range
Widely used to simulate sputtering, backscattering, transmission, damage distributions
Dynamic target composition, arbitrary particle energy / energy distribution
Well suited for sequential and parallel architectures
Provides input for ERO, SOLPS, Transport models etc.  Modelling of PWI
[1] W. Eckstein, Computer Simulation of Ion-Solid Interactions, Springer Series in Material Science, Vol. 10,1991
[2] A. Mutzke, R. Schneider, W. Eckstein, R. Dohmen, SDTrimSP Version 5.0 IPP Report 12/8, Garching, (2011)
Notes: 9

## Slide 10: SDTrimSP 2D & 3D
SDTrimSP has been expanded to include 2D / 3D targets
Angle / energy distribution of sputtered particles
Fluence-dependent surface morphology / composition
Fluence-dependent sputter yield
Length [Å]
20
40
60
80
0
20
Length [Å]
-10
-5
5
10
0
0
-5
-10
5
10
[W, Ar+, 500 eV]
Notes: 10

## Slide 11: Dynamic simulations
10×1020 Ar/m² ?
fluence 5 · 1020 m-2
20×1020 Ar/m² ?
30×1020 Ar/m² ?
50×1020 Ar/m² ?
initial
5×1020 Ar/m² ?
10×1020 Ar/m² ?
30×1020 Ar/m² ?
5×1020 Ar/m² ?
20×1020 Ar/m² ?

## Slide 12: Ta – 45° incidence, 15° rotation
500 nm
6.2×1020 Ar/m²
SDTrimSP-3D Ta columns eroded by 5 keV Ar under 45° incidence, 15° rotation

## Slide 13: SDTrim 1D-3D
Intended project work
IMAS-interface
  Sample description
  Data extraction
Data base for simulation framework

## Slide 14: RAVETIME
RAVETIME:
Finite Volume code for Reaction-Advection-Diffusion for Transport in Matter
Key points:
  A class of Riccati-type differential equations describes
    Fill-level dependent trapping
    Most surface- and interface processes (site-saturation, binary molecule formation)
  Operator splitting allows
    Massive parallel computation  fast
      Handling of 3D geometries
      UQ-approaches
Status: verification successful, IMAS compatible parallelization pending

## Slide 15: Conclusions & Outlook
Thank you for your attention
Any questions?
(*) SDTRIM-
slides are courtesy
of
Rodrigo Arredondo
4 µm
(*)

## Slide 16: SDTrimSP 2D & 3D
SDTrimSP has been expanded to include 2D / 3D targets
(essentially, parallelized SDTrimSP)
Instead of layers, now we have 3D cubes
Important: Requires small enough cell resolution (nm)
Drawback: Computation time (scales with Ny x Nz )
1D 5 keV Ar+  Si 50×1020 Ar/m²
dx = 2.5 nm
Processors: 32 Time: 0.25 h
3D 5 keV Ar +  Si 50×1020 Ar/m²
dx = dy = dz = 2.5 nm 100 x 100 x 200 nm
Processors: 32 calculation-time: 52 h
STEM  Å
AFM  nm
CLSM  sub-µm
Notes: 16

## Slide 17: Ta – 45° incidence, 15° rotation
6.2×1020 Ar/m²
X - Cut
1 µm
1 µm
(3)
X
SDTrimSP-3D Ta columns eroded by 5 keV Ar under 45° incidence, 15° rotation