## Slide 1: Summary of current status of EIRENE with AMJUEL and H2VIBR for vibrationally excited molecules
Mathias Groth, Andreas Holm

## Slide 2: Underlying AM databases in EIRENE is AMJUEL, HYDHEL and H2VIBR
AMJUEL is tabulated rates of H2 molecular dissociation, ionization, recombination, charge-exchange and excitation, and H0 and helium ionization, recombination, charge exchange, and excitation
  Fundamental data and their sources from Sawada and Fujimoto, J. Appt. Phys. 78 (1995) 2913
  Single (electron-impact) and double (proton-impact) polynomial fits (electron temperature and test-particle/beam energy) of cross-sections and rates.
  Double-polynomial fits (electron temperature and density) of effective rates (MAR/MAD/MAI, populations coefficients, etc) based Sawada/Fujimoto 1995 CRM.
HYDHEL are fitted cross-section and rates based on Janev et al., “Elementary Processes in Hydrogen-Helium Plasmas”, Springer 1987
  Fundamental data from experiments
  Parent database for AMJUEL ⇒ in EIRENE, H+ + H0 CX and helium rates preferentially taken from HYDHEL

## Slide 3: Underlying AM databases in EIRENE is AMJUEL, HYDHEL and H2VIBR
H2VIBR contains vibrationally resolved H2 rates, calculated by rescaling ground-state rates
  Source of fundamental data?
  Rescaling?
EIRENE has been used with ADAS data for atomic reaction

## Slide 4: EIRENE internal post-processing has been used for more comprehensive comparison to experiments than ADAS
EIRENE tracks molecules and atoms on (triangular) grid for given background plasma
  Reactions with molecular ions are included (in each cell), but molecular (positive and negative) ions are assumed instantaneously destroyed → EIRENE - Kinetic Ion Transport (Friedrich Schluck → Derek Harting)
EIRENE tallies (cell) volume-averaged particle, momentum and energy sources and sinks → coupling to plasma codes, post-processing of relevant processes
AMJUEL reduced population coefficients for atomic lines and vibrationally unresolved molecular bands:
  Molecular reactions resulting in excited hydrogen atoms
  Electronically excited molecules → Lyman, Werner and Fulcher bands

## Slide 5: Development of CRUMPET for training purpose and inclusion in edge fluid code UEDGE
CRUMPET development part of Andreas’ Fulbright with Lawrence Livermore National Lab (July 2019 – July 2020)
  CRUMPET is a Python CRM tool for constructing and evaluating CRMs
  Constructs a system of ODEs based on A&M data (reads and uses AMJUEL, H2VIBR, ADAS, Einstein-coefficients, etc)
  Time-dependent evaluation of the ODE using Python solver
  Constructs a Greenland-style CRM and calculates effective rate coefficients
Verification of UEDGE molecular model, including vibrationally excited molecules, against UEDGE-EIRENE predictions
Re-activation of 2000 H2(v) model (original B2/EIRENE cases from 1998, Ursel’s JNM 2001) and tests in simple slab and well-diagnosed JET geometry (L-mode plasmas)
Standalone EIRENE ⇒ SOLPS-ITER

## Slide 6: Cross-checks of AMJUEL against YACORA database ⇒ desired EIRENE post-processing
Comparison of YACORA vs AMJUEL post-processing (impact of evaluating full CRM vs piecewise calculated effective rates)
Scaling of vibrationally dependent rates (e.g., H2VIBR)
Isotopologue rescaling vs. CR modelling with first-order data (e.g. impact "temperature scaling” and Franck-Condon factors)
YACORA processing of measured H2 and D2, (T2 and D-T) spectra with local ne, Te measurements (e.g., Fantz & Heger, PPCF 1998 and Fantz, Plasma Sources Sci. Technol. 2006)
…

## Slide 7: (Some) open questions
Potential need for self-consistent CRM for molecules inside EIRENE (for each cell)?
(Total) molecular radiation in the energy balance, to be returned to plasma code
CX processes between electronically excited atoms with plasma ions?
Status of HYDKIN (tool)? (removed from eirene.de website)

## Slide 8: Notes and minutes of meeting
Options for H2 CRM in support of EIRENE
  Detlev’s Sawada code (using AMJUEL, HYDHEL, H2VIBR)
  Andreas’ CRUMPET (using AMJUEL, HYDHEL, H2VIBR)
  Dirk’s/Ursel’s YACORA
Preference for YACORA as code with the most developed and up-to-date AM data (see Dirk’s presentation)
Current YACORA:
  Started with Sawada datasets → latest MCCC data, Curtin University connection, formatted ASCII input for isotopologues
  Integration of equations rather than linearization as in Greenland ⇒ non-linear effects, optical thickness
  Mock-up of transport effects through diffusion ⇔ EIRENE transport
  Surface effect, release/reflection of excited molecules

## Slide 9: Notes and minutes of meeting
Start with cross-comparison of EIRENE output using AMJUEL and YACORA
  Andreas’ 1-D slab ⇒ realistic MAGNUM-PSI and JET L-mode cases
  Start with YACORA on the Web → training in executing YACORA as project progresses, sharing of executable to be discussed when ready
  Discussion of making YACORA part of EIRENE when determined beneficial
  Start with hydrogen case, then move to deuterium, tritium, DT
MDAS (Molecular ADAS) could potentially replace AMJUEL (for cross-sections and rates), but running up-to-date CRM necessary to verify and validate models; to address multidimensionality of parameters (past ne and Te dimensions)
JKU?
Dmitriy/Mathias to get in contact with Jorge Gonzalez-Munoz/Egbert Westerhoff for SOLPS-ITER, Ivo Classen for AM spectroscopy at MAGNUM-PSI

## Slide 10: Notes and minutes of meeting
Mathias to summarize JET L-mode measurements (W target)
  H2 vs D2 (T2 and DT) → Fulcher band measurements
  Comparison cases for H2 and D2 DIII-D L-mode cases with HR-UV (potentially, Lyman-Werner bands), Fulcher band, Divertor Thomson Scattering → carbon target = resurrect previous knowledge
Next steps:
  Andreas to provide EIRENE profiles and analyses based on 1D hydrogen slab
  Comparison of AMJUEL and YACORA input data and post-processing of EIRENE output ⇒ need prioritized list of input/output data
  Smaller-circle Zoom meeting by mid-June 2021, Andreas to visit IPP Garching (probably, hopefully) in September 2021
  Summary of activities to TSVV-5 group in October/November 2021