## Slide 1: DIFFER contributions to SP-X1
Ivo Classen, Hennie van der Meiden, Jordy Vernimmen, Jonathan van den Berg

## Slide 2: Deliverables
Near target measurements:
  CTS on Magnum: Velocity
  TS on Magnum and UPP: Accurate power loads
Passive VUV spectroscopy on Magnum
TALIF on Magnum
  Diagnostic development
  First step towards VUV-LIF

## Slide 3: Magnum-PSI
up to 5 eV
= 1019 – 1021 m-3
up to 1025 m-2s-1
q up to 50 MWm-2
Pulses: up to 20eV and 1GWm-2
Differential pumping:
neutrals: 0.3 Pa during plasma

## Slide 4: Section A
Near target ion/electron properties (TS/CTS)
Plasma velocity measurements

## Slide 5
CTS / TS at Magnum-PSI
Simultaneous TS and CTS
Careful stray radiation suppression
Measurements up to 3mm from target

## Slide 6: Results so far
At

## Slide 7: In 2021: Measurements under variety of target angles (90, 60, 45, 30 degrees)

## Slide 8: Section B
Passive VUV spectroscopy
Coming soon to a linear device near you!
(collaboration with Comenius Institute)

## Slide 9: Section C
Active spectroscopy on Magnum-PSI
Now: TALIF (atoms)
Future: CARS / VUV-LIF (molecules)

## Slide 10: Motivation
10
The ro-vibrational distribution plays a major role: MAR rate can vary multiple orders of magnitude
Direct measurement difficult, but H2(r,n) distribution previously successfully measured in both linear plasmas and tokamaks (no current set-ups)
 Build new diagnostic on Magnum-PSI (divertor relevant plasmas) based on proven methods: VUV-LIF and CARS (TU/e, Plexis)
Grant application running at Dutch Scientific Organization (NWO)
From Vankan et al.

## Slide 11: Active spectroscopy: 3 methods
11
VUV-LIF based on Stimulated anti-Stokes Raman scattering (population  >2,J)
Coherent anti-Stokes Raman spectroscopy (CARS):
(population  ≤2,J)
Two photon Absorption Laser Induced Fluorescence (TALIF)
(density H atoms in ground state)

## Slide 12: VUV-LIF principle
VUV LIF spectroscopy of H2 ground state
Excite ground state ro-vib level to electronically excited state
Measure fluorescence signal
Scanning the laser wavelength excites different ro-vib states
110 to 165 nm for n=0 to n=14

## Slide 13: Planned VUV-LIF setup
13
Laser in VUV range (down to ~ Ly a)
 Raman cell (SARS)
In vacuum
VUV monochromators
Vacuum window transmission (>120 nm) prevents measuring lower vibrational states (n>2)

## Slide 14: Complementary techniques: CARS
14
Lower vibrational states (n<=2) can be measured with CARS
Same lasers as VUV-LIF
No vacuum needed
CARS:
4-wave mixing process
660-700 nm probe beam
532 nm pump beam

## Slide 15: In 2021: Start with TALIF
TALIF:
  Density of atomic H density Also applicable to N
  Excitation: 205.14 nm (for Ly b absorption with 2 photons)
  Fluorescence: Ha
Independent of national funding
TU/e student project starting in September
Laser setup before end of 2021
First measurements first half 2022

## Slide 16: Thank you for your attention!