## Slide 1: SOLPS-ITER activities within the DEMO Central Team – development needs
S. Wiesen
September 17th 2021

## Slide 2: Overview
DEMO Divertor Design studies
Core-edge coupling
Transients & divertor re-attachment
Wall models
ADCs

## Slide 3
DEMO divertor design studies

## Slide 4: Early assessment for DEMO
SOLPS4.3, Kukushkin Pacher 2007-2009
D/He/Be +
Ne-seeding
PSOL = 300MW
Density control by Core + Gas fuelling

## Slide 5: Early assessment for DEMO
SOLPS4.3, Kukushkin, Pacher 2007-2009
Full detachment of inner divertor restricts pPFR
Criterion: max Te at inner target falls below certain minimum, i.e. < 5eV
For DEMO: pPFR,max = 18.6 Pa

## Slide 6: Lessons learned ITER divertor design
SOLPS4.3 has been the main workhorse for the ITER divertor design studies since 20+ years
Physics operating mode for the ITER divertor is to a large extent based on plasma boundary simulations conducted over ~15 years with the SOLPS-4.3 code (B2-Eirene)  mostly C targets!
  A. S. Kukushkin et al. J. Nucl. Mat. 290-293 (2001) 887
  A. S. Kukushkin et al. Nucl. Fusion 42 (2002) 187
  A. S. Kukushkin and H. D. Pacher, PPCF 44 (2002) 931
  H. D. Pacher et al. J. Nucl. Mat. 313-316 (2003) 657
  A. S. Kukushkin et al. Nucl. Fusion 43 (2003) 716
  A. S. Kukushkin et al. Fus. Eng. Design 65 (2003) 355
  A. S. Kukushkin et al. Nucl. Fusion 45 (2005) 608 A. S. Kukushkin et al. J. Nucl. Mat. 337-339 (2005) 17
  A. S. Kukushkin et al. Nucl. Fusion 47 (2007) 698
  A. S. Kukushkin et al. J. Nucl. Mat. 363-365 (2007) 308
  G. W. Pacher et al. Nucl. Fusion 48 (2008) 105003
  H. D. Pacher et al. J. Nucl. Mat. 390-391 (2009) 259
  A. S. Kukushkin et al. Nucl. Fusion 49 (2009) 075008
  A. S. Kukushkin et al., J. Nucl. Mat. 415 (2011) 2011
  H. D. Pacher et al. J. Nucl. Mat. 415 (2011) S492
  G. W. Pacher et al. Nucl. Fusion 51 (2011) 083004
  A. S. Kukushkin et al. Fus. Eng. Design 86 (2011) 2865
1996
2001
2009
▬ 1996 (ITER physics basis 1999)
▬ 2003 (neutral-viscosity added)
▬ 2004 (refined molecular collision kinetics added)
▬ 2005 (Lyman radiation trapping)

## Slide 7: Rationale for inclusion of a DEMO divertor liner
Current design
Introduced to reduce radiative and neutronic load into the pump duct
Shape and arrangement of the target / reflector / liner is as such that it is expected a large quantity of neutrals and scattered particles impinging on the almost unprotected parts:
- between the reflectors and the back of liner, - the liner supply tubes, - the supports.
Efficiency of pumping potentially reduced (incl. He-ash)
Post-design modelling in preparation with SOLPS-ITER  assess load specification, pumping efficiency, etc

## Slide 8: Issue of particle balance / explicit (EIRENE sources)-implicit (B2.5) coupling  long convergence times
A. S. Kukushkin et al. Fus. Eng. Design 86 (2011) 2865
Pumping in ITER (and DEMO) amounts to only about 1% or less of the recycling flux.  to resolve the effect of pumping and fuelling on the solution, the accuracy of the particle balance in the code must be much better than 1%  big challenge for a hybrid code such as SOLPS to reach convergence
Numerical noise induced at time-step t+dt  correction factors ~1 required

## Slide 9: DEMO divertor assessment with new SOLPS-ITER
Work only started in FP8: F. Subba EU-DEMO  WPDES
SOLPS-ITER model parameters (no drifts/currents)
  Input power into edge: 150 MW
  D-puff: 1e23 atoms/s (~ 200 Pa m3 s-1)
  Minor D pellet volumetric source: 7e21 (s-1)
  D+He+Ar plasma
  Ar puff: 1.5e19 atoms/s
Zeff ~1.9 in the core
HFS
LFS
HFS deeply detached
Low temperatures; <1eV at max particle flux/density
Negligible heat flux ~ 1MW/m2
LFS partially detached
temperature low @ strike-line < 1.5eV
Heat-flux max 2MW/m2

## Slide 10: Revised ITER Divertor Design studies: metal wall & SOLPS-ITER
R.A. Pitts, E. Kaveeva, V. Rozhanski, S. Wiesen, X. Bonnin et al, NME 2019
PSOL=100MW
Assessment of several control parameters, together with satisfying a number of constraints (e.g. power loading and core He density or radiation)  During FP9, establishment of DEMO operational windows and SOLPS-ITER based scalings (F. Subba, L. Aho-Mantila, WPDES)
Extension towards EU-DEMO design: assume validity of model first, e.g. through FSD experiments, and scoping (e.g. w. advanced fluid or hybrid models) Add physics: inclusion of drifts/currents, improved impurity & A&M models, neutral buffering/conductances, Lyman opacity effects, large frad (e.g. XPR) etc Add constraints: divertor shape, field geometry, engineering limits, cost  towards an optimized DEMO divertor configuration ( WPDIV, WPTFV)

## Slide 11
Core-Edge coupling

## Slide 12: Previous DEMO ASTRA/SOLPS4.3 coupling
Core & pedestal:
ASTRA/ICPS model
MMM/Weiland models, shear stabilised; JET/AUG
Edge:
SOLPS4.3 setup as in ITER – but no direct coupling
Provide ASTRA with ni/Ti,e DT/He fluxes at spx
Derived scalings for point-of-detachment, i.e.:
H.D. Pacher, G.W. Pacher, A.S. Kukushkin, G. Janeschitz DEMO conceptual study EFDA TW6-TRP-002

## Slide 13: Numerical assessment of integrated DEMO operational space
H.D. Pacher, G.W. Pacher, A.S. Kukushkin, G. Janeschitz DEMO conceptual study EFDA TW6-TRP-002
DEMO operating window, I=21 MA, Ne seeding feedback
Review of reduced integrated models: e.g. T. Luda et al: coupling of ASTRA/MISHKA w/ Kallenbach multi-point model of SOL  calibration of reduced SOL model (based on SOLPS-ITER, w/ or w/o neutral kinetics – fast models reqd), collaboration with WPTE RT02/RT13
Review ASTRA/SOLPS-ITER coupling: functionality and code-implementation setup of revised EU-DEMO reference scenario
Also: Coupled JETTO-SANCO/SOLPS-ITER simulations: IMAS coupling of core code to SOLPS-ITER foreseen (collaboration w/ IO)
Interface requirements for improved scenario integration: Assess overlapping computational region between SOLPS-ITER (2D) and ASTRA (1D); identification of an improved scheme to couple: improved pedestal model (i.e. including core radiation), H&CD models etc

## Slide 14
Transients – Divertor re-attachment

## Slide 15: What else can cause a loss of detachment?
Well, many things…
Fluctuations in the separatrix density.
Fluctuations in the separatrix power (e.g. pellet induced transient a-particle heating)
Combinations thereof.
Technical failure (e.g. impurity puff valve).
Control failure.
…others…
[Wiesen, NF 2017]
Impurity radiation control required
JETTO-EDGE2D
ITER

## Slide 16: Fuelling Pellet induced re-attachment
High density
Short bursts of re-attachment during pellet ablation
Such simulations help to predict and mitigate impact of unavoidable transients in HF  ITER & DEMO divertor engineering and operational design
[Wiesen, NF 2017]
JETTO-EDGE2D
ITER

## Slide 17: Re-attachment in DEMO
The maximum tolerable steady-state HF on the current DEMO SN divertor plate is 10-20 MW/m2. [J.H. You, G1 review mtg] This value can be achieved only in detached plasma conditions (with seeded impurities).
In case of accidental divertor reattachment, the divertor reaches burn-out (leading to an in-vessel LOCA) in about 3 sec.
Divertor sweeping (to be activated only in emergency cases) to allow the divertor surviving while the current is ramped down [Maviglia, FED 2016]. Needs the presence of IVC.
Siccinio, NF 2019
RACLETTE: 10s HF ramp 10..70 MW/m2

## Slide 18: Re-attachment in DEMO
What about “fast termination”?
A fast plasma shutdown (like in ITER) at full current would pose unacceptable risks on the machine integrity [Maviglia, NME 2021],[Lehnen, IAEA 2016].
In parallel, the current cannot be ramped down faster than ~0.2 MA/s without losing vertical stability control. (the increase of ramp down rate with the use of IVC is presently being investigated)
[Siccinio, FED 2020]
ITER
DEMO
[Lehnen, IAEA 2016]

## Slide 19: The (provisional) solution
Diagnostics able to detect reattachment before it happens (e.g. spectroscopy following the radiation front) [Biel, FED 2019].
Divertor sweeping (to be activated only in emergency cases) to allow the divertor surviving while the current is ramped down [Maviglia, FED 2016]. Needs the presence of IVC.
[Maviglia, NME 2021]
[Siccinio, NF 2019]
10s HF ramp 10..70 MW/m2

## Slide 20: Advanced Fluid Neutral Model application to ITER
TSVV-5
Re-attachment/re-detachment studies; requires input from WPTE expts
Time-dependent option in SOLPS-ITER: issue: explicit-implicit coupling of plasma-fluid and neutral Monte-Carlo
Exploit advanced fluid-models in SOLPS-ITER for time-dependent simulations (without EIRENE); integration with core-codes (e.g. ASTRA)
Interaction related ETASC TSVVs (flight simulators, scenario integration) and ENRs on model reduction (e.g. generative neural-networks) as alternative model

## Slide 21
Wall models

## Slide 22: CX and photon fluxes on (ITER) first wall components
Breakdown of problem: ITER
Also: photons and radiation loads possible
Collaborative work WPDC, W. Biel

## Slide 23: Erosion vs Deposition on the ITER port-plug faces
V. Kotov NF 2016

## Slide 24: CHERAB DEMO First Wall Estimated Loads
Calculations on TQ mitigated Disruptions (or VDEs)
Assessment of active mitigation techniques
Initial thermal energy Wth=1.3GJ: 20% radiated @ pre-TQ at MGI/SPI  1GJ remaining
Analysis including averaging techniques
Some relevant differences observed:
  More uniform load distribution
  Estimated peak load appears smaller by about 33%
  Higher accuracy
F. Maviglia, IAEA-TM 2020
Prad=800GW
Collaboration WPPWIE & TSVV-7
Continuation requires SOLPS-ITER w/extended wall option (not validated yet); comparison with other models (e.g. SOLEDGE2D)
Development of numerical diagnostics for heat-fluxes in DEMO: CX and photon fluxes on walls (energy spectra, angular distribution)
Assessment of 2nd Xpoint and PWI in upper plane (SN) (R. Osawa, WPDES)
3D field line tracing codes to estimate charged particle HF (PFCflux – SMARDDA) Later: kinetic models of 3D structures (e.g. toroidal/poloidal gap analysis, Firdaouss, Gerardin, WPDES)
Long term: Towards numerical optimization of first wall, steady-state & transients (e.g. disruptions/VDEs), impact on wall, W droplets (MEMOS-U, Ratynskaja)

## Slide 25
ADCs

## Slide 26: ADC
Mainly covered by WPPWIE/ADC and WPTE (physics)
Extension of FP8 activities (c.f. F. Militello et al, ADC report 2021, WP-DTT1 and WP-DTT1/ADC) - SOLPS-ITER
Requires speed up and/or validated reduced physics models
Cyclic monitoring of DCT into WPPWIE/WPTE activities: focus on demonstration of ADC being a possibility for DEMO  input gate review 2024
Extension of WPDES activities towards ADC scenarios, e.g. DN, SXN (later on); start with advanced fluid or hybrid neutral model (L. Aho-Mantila, WPDES)
Work with groups who work on advanced fluid models development (i.e. TSVV-5) and numerical divertor optimisation techniques (e.g. Univ. Leuven, adjoint optimisation techniques)  call for combined PWIE-DES EEG, closed & proposals in place
Later: assessments of engineering limits for ADCs: transients and configurations (e.g. sweeping in ADC, seeding, etc)

## Slide 27: Overview
DEMO Divertor Design studies
Core-edge coupling
Transients & divertor re-attachment
Wall models
ADCs
All topics would be exploiting the newly developed features in the NGM of TSVV-5