## Slide 1: ITER views on further EIRENE development
X. Bonnin
ITER Organization
with inputs from S. Pinches, O. Hoenen, R. Pitts, S. Lisgo, D. Coster (IPP) and N. Rivals (CEA)

## Slide 2: Context
EIRENE is the dominant Neutral Gas Module (NGM) used in the fusion community and by the IO, for example in:
  SOLPS-ITER (B2.5-Eirene)
  EMC3-Eirene
  SOLEDGE3X (SOLEDGE2D+TOKAM3X+Eirene)
  JINTRAC (EDGE2D-Eirene)
  OSM-DIVIMP-Eirene
The IO has therefore a strong interest in the continued improvement of the EIRENE code: physics fidelity, accuracy and robustness, validation, and adherence to good community development standards
The IO welcomes the opportunity it is given to participate in the shaping of future EIRENE code developments while recognizing that EIRENE is IP from FZJ

## Slide 3: EIRENE developments in IO’s interest
Software development:
  Use of standard Interface Data Structures (IDSs) for input/output (sometimes called “IMAS-ification”)
  Lowering barrier to use through better documentation and worked-out examples
  Performance improvements, e.g. through further parallelization
  Improved distributed development
New physics capabilities and improvements:
  Corrections to treatment of molecular “test” ions
  Revival of radiation transport options
  Species-specific source rescaling scheme
  Extensions to wall and surface chemistry models

## Slide 4: IMAS-ification of EIRENE
Long-term goal, but the most important one for the IO.
All IO-used software must eventually interface with IMAS. For an NGM, this means:
  Ability to obtain its input from a combination of the equilibrium, wall, edge_profiles, and edge-transport IDSs, plus a limited number of code-specific parameters in a dedicated input file
  Ability to provide its output as edge_profiles, edge_sources, edge_transport, radiation, and summary IDSs
    Allows use in different workflows, e.g. for synthetic diagnostics (spectroscopy, bolometry, etc.)
    Dedicated radiation tallies already exist in the SOLPS-ITER branch for this purpose
  Ability to use reaction data from the AMNS package
  Use of Generalized Grid Description (GGD) geometrical objects
  Contribute to evolution of IMAS Data Dictionary to provide all quantities of interest and participate in definition of relevant new quantities when the need arises

## Slide 5: Improvements to test ion treatment
Many issues were discovered when H2+ ions were included in SOLEDGE3X simulations of the ITER sub-divertor volume and the same issues are expected to crop up when using the extended grids version of SOLPS-ITER
  Test ions must be followed to avoid large sinks and the magnetic field must be smoothly interpolated for that purpose (already possible)
  Correction to the test ion following routine were necessary for Fokker-Planck collisions and when crossing periodicity boundaries
  Collisions of test ions with surfaces also needed changes with respect to sheath potential calculation and cell indexing
These changes already exist in the SOLEDGE branch and should be examined by the FZJ team for inclusion in the general Eirene distribution

## Slide 6: Species-specific rescaling scheme
Correct particle source rescaling is essential to maintain proper particle balance for cases with cross-species reactions such as CX between fuel ions and impurities or in a D-T mixture.
Such a scheme has been implemented in SOLPS-ITER
  Works well for standard cases, when statistics are sufficient
  Reverts to the traditional scaling scheme when treating very rare events
  Rather clumsy solution still in need of generalization and may not be practical for very large grids as in EMC3-Eirene
  Requires further discussion with other developers to decide on implementation choices if pursued as a generalized Eirene feature

## Slide 7: Radiation transport and opacity
Radiation transport and opacity calculations in Eirene are essential to obtain a correct description of the plasma in remote areas, such as under the ITER dome umbrella:
  We know the plasma there will be maintained by photo-ionization
  Plasma parameters in the sub-divertor will determine pumping and fueling efficiency
  Part of S. Wiesen’s and D. Reiter’s ISFN work programmes
Correct spectrum calculations critical to properly interpret spectroscopic signals like Lyman and Balmer lines, as demonstrated on JET
Such capabilities were demonstrated ~10 years ago by Kotov & Kukushkin, but need to be revived and modernized

## Slide 8: Improvements to wall models
Extension of the wall model to allow for surface chemistry, wall temperature evolution, surface erosion/deposition, and hydrogen inventory calculations:
  A prototype wall evolution model already exists in a SOLEDGE2D version
  A very basic surface chemistry model for Nitrogen currently being tested in SOLPS-ITER (probability of N recycling as either N2 or NH3 varying according to surface conditions)
  Include a thermal model to self-consistently determine the wall temperature
  Ability to track surface deposits and/or erosion of wall material
  Ability to specify and treat non-elemental wall compositions

## Slide 9: Further code improvements
Consider GPU parallelization, particularly for very large 3-D grids
Possibility to obtain internal, not total, energy sources from Eirene
Splitting of Eirene sources by reactions, or at least by reaction type
Bringing back the various repository forks in better agreement with each other
Providing instructions on how to compile the code in the Eirene manual from the files in the repository
Providing worked out examples and sets of recommended reactions for various standard use cases, including synthetic diagnostics and time-dependent runs
Recommended boundary conditions and surface models for fictitious wall boundaries

## Slide 10: Concluding remarks
The IO has very limited manpower resources but stands ready to assist EIRENE and other NGM developments and welcomes the TSVV-5 initiative
The IO encourages voluntary contributions from the ITER Member States by means of the ISFN, IPAs, and Visiting Researcher programmes
The IO has limited budget for contractual work on new simulations and/or code development, when these are in direct pursuance of the ITER project goals and would not be done at all or on the necessary time scale via voluntary contributions
The IO must work within the legal constraints of the terms of the ITER Agreement (i.e. licensing, distribution outside public institutions within the ITER Member States, etc…)