## Slide 1: TSVV3 – ACH EPFL workplan SOLEDGE3X workplan
P. Tamain

## Slide 2: Overview
SOLEDGE3X concerned by support through 3 of the ACH tasks
  Optimization of elliptic solvers => not specific to SOLEDGE3X, generic discussion in this meeting
  Optimization of kinetic neutrals treatment via coupling to EIRENE
  Code-dependent optimization

## Slide 3: Elliptic solvers in SOLEDGE3X
SOLEDGE3X makes use of 2 elliptic implicit solvers:
  Parallel heat conduction terms:
    2D thanks to flux-surface aligned grid (1 matrix by flux surface)
    Embarrassingly parallel on flux-surfaces
    Direct solver quite efficient but scalability questionable and difficulties to exploit parallelization (core pinning) with the libraries we use
  Electrostatic potential:
    3D (strong specificity vs other codes), extremely badly conditioned
    Tried many different solvers from direct to AMG
    Until recently main bottleneck of code for computing time (>95% for large cases), memory and scalability

## Slide 4: SOLEDGE3X points of interest for elliptic solvers
Strong progress on both aspects through usage of PETSC
  Natural scalability recovered for heat conduction solver
    Most probably due to better ability to manage core pinning
  Huge gain obtained on potential solver which is not any the dominant part of the code
    Key aspect = re-use of preconditioner
  But usage of PETSC not ideal because of pure MPI parallelization (vs hybrid for rest of code)
Key points of interest on elliptic solvers:
  Find a way to exploit hybrid parallelization in elliptic solvers (moving away from PETSC or adding threads somehow)
  Strong interest in surveying and testing methods used in other codes
Ideal
SOLEDGE3X weak strong scaling on TCV case [courtesy H. Bufferand]

## Slide 5: Kinetic neutrals in SOLEDGE3X: status
SOLEDGE3X coupled to EIRENE through STYX interface
  Takes care of EIRENE setup and data exchange between plasma solver and EIRENE
  Already used in 3D turbulence cases with TOKAM3X [Tamain PSI 2018], currently tested only in 2D in SOLEDGE3X
SOLEDGE3X:
Plasma 3D flux-driven turbulence Plasma up to sheath entrance
EIRENE:
Neutral transport and interactions
Quasi-neutral plasma
Neutrals
ni, ui,
Ti, Te
Sn, SE
 TOKAM3X-EIRENE
 TOKAM3X-EIRENE
STYX
But 2 issues:
  STYX has not been optimized nor parallelized properly (initially designed for 2D solver)
    Computing and memory bottle neck for large 3D case
  STYX not conceived as separate module => for the moment usable only in SOLEDGE3X

## Slide 6: Kinetic neutrals in SOLEDGE3X: workplan
ACH support requested to:
  Perform first profiling and optimization/parallelization of STYX
  Achieve separation (modularization) between SOLEDGE3X and STYX in order to make STYX-EIRENE readily available for any edge code

## Slide 7: SOLEDGE3X optimization: workplan
SOLEDGE3X partly written in replacement of TOKAM3X following recommendations of profiling
  Strong improvement in terms of computing time evident on test cases
  But no exhaustive profiling ever performed since then on SOLEDGE3X, partly because computing time ultra-dominated by elliptic potential solver
Now that this bottleneck has been solved, strong need for:
  Exhaustive profiling: algorithmic efficiency, salability (…) of the various parts of the code
    Take advantage to setup automatic tools for CI/CD
  Identify issues and propose solutions
  Implement and test them in the code