## Slide 1: Exhaust and Detachment
S. Wiesen
with support by M. Siccinio, M. Wischmeier, et al

## Slide 2: Overview
DEMO Divertor Design studies
Core-edge coupling
Transients & divertor re-attachment
Open points (from FTD-DCT perspective)

## Slide 3
DEMO divertor design studies

## Slide 4: Early assessment for DEMO
SOLPS4.3, Kukushkin Pacher 2007-2009
D/He/Be +
Ne-seeding
PSOL = 300MW
Density control by Core + Gas fuelling

## Slide 5: Early assessment for DEMO
SOLPS4.3, Kukushkin, Pacher 2007-2009
Full detachment of inner divertor restricts pPFR
Criterion: max Te at inner target falls below certain minimum, i.e. < 5eV
For DEMO: pPFR,max = 18.6 Pa

## Slide 6: Lessons learned ITER divertor design
SOLPS4.3 has been the main workhorse for the ITER divertor design studies since 20+ years
Physics operating mode for the ITER divertor is to a large extent based on plasma boundary simulations conducted over ~15 years with the SOLPS-4.3 code (B2-Eirene)  mostly C targets!
  A. S. Kukushkin et al. J. Nucl. Mat. 290-293 (2001) 887
  A. S. Kukushkin et al. Nucl. Fusion 42 (2002) 187
  A. S. Kukushkin and H. D. Pacher, PPCF 44 (2002) 931
  H. D. Pacher et al. J. Nucl. Mat. 313-316 (2003) 657
  A. S. Kukushkin et al. Nucl. Fusion 43 (2003) 716
  A. S. Kukushkin et al. Fus. Eng. Design 65 (2003) 355
  A. S. Kukushkin et al. Nucl. Fusion 45 (2005) 608 A. S. Kukushkin et al. J. Nucl. Mat. 337-339 (2005) 17
  A. S. Kukushkin et al. Nucl. Fusion 47 (2007) 698
  A. S. Kukushkin et al. J. Nucl. Mat. 363-365 (2007) 308
  G. W. Pacher et al. Nucl. Fusion 48 (2008) 105003
  H. D. Pacher et al. J. Nucl. Mat. 390-391 (2009) 259
  A. S. Kukushkin et al. Nucl. Fusion 49 (2009) 075008
  A. S. Kukushkin et al., J. Nucl. Mat. 415 (2011) 2011
  H. D. Pacher et al. J. Nucl. Mat. 415 (2011) S492
  G. W. Pacher et al. Nucl. Fusion 51 (2011) 083004
  A. S. Kukushkin et al. Fus. Eng. Design 86 (2011) 2865
1996
2001
2009
▬ 1996 (ITER physics basis 1999)
▬ 2003 (neutral-viscosity added)
▬ 2004 (refined molecular collision kinetics added)
▬ 2005 (Lyman radiation trapping)

## Slide 7: Revised ITER Divertor Design studies: metal wall & SOLPS-ITER
R.A. Pitts, E. Kaveeva, V. Rozhanski, S. Wiesen, X. Bonnin et al, NME 2019
PSOL=100MW
Assessment of several control parameters, together with satisfying a number of constraints (e.g. power loading and core He density or radiation)  establishment of DEMO operational windows and SOLPS-ITER based scalings
Extension towards EU-DEMO design: assume validity of model first, e.g. through FSD experiments Add physics: inclusion of drifts/currents, improved impurity models, neutral buffering/conductances, Lyman opacity effects, large frad (e.g. XPR) etc Add constraints: divertor shape, field geometry, engineering limits, cost  towards an optimized DEMO divertor configuration ( WPDIV, WPTFV)

## Slide 8: DEMO divertor assessment with new SOLPS-ITER
Work only started in FP8: F. Subba EU-DEMO  WPDES
SOLPS-ITER model parameters (no drifts/currents)
  Input power into edge: 150 MW
  D-puff: 1e23 atoms/s (~ 200 Pa m3 s-1)
  Minor D pellet volumetric source: 7e21 (s-1)
  D+He+Ar plasma
  Ar puff: 1.5e19 atoms/s
Zeff ~1.9 in the core
HFS
LFS
HFS deeply detached
Low temperatures; <1eV at max particle flux/density
Negligible heat flux ~ 1MW/m2
LFS partially detached
temperature low @ strike-line < 1.5eV
Heat-flux max 2MW/m2

## Slide 9
Core-Edge coupling

## Slide 10: Previous DEMO ASTRA/SOLPS4.3 coupling
Core & pedestal:
ASTRA/ICPS model
MMM/Weiland models, shear stabilised; JET/AUG
Edge:
SOLPS4.3 setup as in ITER – but no direct coupling
Provide ASTRA with ni/Ti,e DT/He fluxes at spx
Derived scalings for point-of-detachment, i.e.:
H.D. Pacher, G.W. Pacher, A.S. Kukushkin, G. Janeschitz DEMO conceptual study EFDA TW6-TRP-002

## Slide 11: Numerical assessment of integrated DEMO operational space
H.D. Pacher, G.W. Pacher, A.S. Kukushkin, G. Janeschitz DEMO conceptual study EFDA TW6-TRP-002
DEMO operating window, I=21 MA, Ne seeding feedback
Review of reduced integrated models: e.g. T. Luda et al: coupling of ASTRA/MISHKA w/ Kallenbach multi-point model of SOL
Review ASTRA/SOLPS-ITER coupling: functionality and code-implementation setup of revised EU-DEMO reference scenario
Also: Coupled JETTO-SANCO/SOLPS-ITER simulations: IMAS coupling to SOLPS-ITER foreseen (collaboration w/ IO)
Interface requirements for improved scenario integration: Assess overlapping computational region between SOLPS-ITER (2D) and ASTRA (1D); identification of an improved scheme to couple: improved pedestal model (i.e. including core radiation), H&CD models etc

## Slide 12
Transients – Divertor re-attachment

## Slide 13: What else can cause a loss of detachment?
Well, many things…
Fluctuations in the separatrix density.
Fluctuations in the separatrix power (e.g. pellet induced transient a-particle heating)
Combinations thereof.
Technical failure (e.g. impurity puff valve).
Control failure.
…others…
[Wiesen, NF 2017]
Impurity radiation control required
JETTO-EDGE2D
ITER

## Slide 14: Fuelling Pellet induced re-attachment
High density
Short bursts of re-attachment during pellet ablation
Such simulations help to predict and mitigate impact of unavoidable transients in HF  ITER & DEMO divertor engineering and operational design
[Wiesen, NF 2017]
JETTO-EDGE2D
ITER

## Slide 15: Re-attachment in DEMO
The maximum tolerable steady-state HF on the current DEMO SN divertor plate is 10-20 MW/m2. [J.H. You, G1 review mtg] This value can be achieved only in detached plasma conditions (with seeded impurities).
In case of accidental divertor reattachment, the divertor reaches burn-out (leading to an in-vessel LOCA) in about 3 sec.
Divertor sweeping (to be activated only in emergency cases) to allow the divertor surviving while the current is ramped down [Maviglia, FED 2016]. Needs the presence of IVC.
Siccinio, NF 2019
RACLETTE: 10s HF ramp 10..70 MW/m2

## Slide 16: Re-attachment in DEMO
What about “fast termination”?
A fast plasma shutdown (like in ITER) at full current would pose unacceptable risks on the machine integrity [Maviglia, NME 2021],[Lehnen, IAEA 2016].
In parallel, the current cannot be ramped down faster than ~0.2 MA/s without losing vertical stability control. (the increase of ramp down rate with the use of IVC is presently being investigated)
[Siccinio, FED 2020]
ITER
DEMO
[Lehnen, IAEA 2016]

## Slide 17: The (provisional) solution
Diagnostics able to detect reattachment before it happens (e.g. spectroscopy following the radiation front) [Biel, FED 2019].
Divertor sweeping (to be activated only in emergency cases) to allow the divertor surviving while the current is ramped down [Maviglia, FED 2016]. Needs the presence of IVC.
[Maviglia, NME 2021]
[Siccinio, NF 2019]
10s HF ramp 10..70 MW/m2

## Slide 18
Open points (FTD-DCT)

## Slide 19: Open points
Operational aspects
Basic physics
Reduced models
„Off-baseline“ investigations
What needs to be done in order to validate the current DEMO solution
(or to find a better one)?

## Slide 20: Open points - Operational
Feasibility of sweeping in detached/near-detached conditions, with/without seeding
Reliable detachment control scheme with “minimum”/controllable impact on core. Strong justification for IVC.
Feasibility of ramp-down in shape with/without sweeping (worse 0.2MA/s?)
Exploration of reattachment with loss of impurity seeding (e.g. determination of time-scales) in DEMO-similar divertor conditions
Exploration of reattachment with loss of power and/or due to increased PSOL (in DEMO e.g. from pellet ablation close to edge or increased Palpha)
These points should be prioritized w.r.t. physical understanding of the underlying phenomena (see next slides), since they could be addressed in a shorter time and allow for an early change of design.
Response from FSD
Feasibility of sweeping in (near) detached conditions: JET: data available for horizontal target configuration, limited diagnostic in corner C/C configuration, more data available in V/H config. Also V/V  Action: Analysis requires data mining and contact SCs of baseline and hybrid scenarios  human resource allocation
Rampup-down (w/ or w/o sweeping): Requires numerical analysis and possibly testing on smaller device for model-experimental data comparison  Action: needs dedicated proposals for ramp down and modelling of ramp down possibly in RT12
Re-attachment: Investigate available experimental data from AUG and JET with seeding, power cut-offs, pellet fueling transients, pump cut-off (also: sawteeth or H-M-L trans)  Action: Analysis requires data mining and contact SCs of scenarios  human resource allocation

## Slide 21: Open points – Basic Physics
Physics of re-attachment, as function of power, density and impurity (incl. fluctuations), pellets; time-scales
Transport in divertor region: e.g. prediction of broadening factor S, impact of drifts
Prediction of impurity concentration and compression ratio
Optimum impurity mix (species) for DEMO-like conditions (models?)
On size scaling (geometry) and impact on impurity transport /compression
LH transition threshold (and possible hysteresis) with radiating core (e.g. XPR) going beyond Martin's scaling; revised IPB98 scaling with impurity radiation loss (or rather include radiation in transport models?)
Predictability of time-dependent state-of-the-art models and tools to predict divertor transients and dynamics; flight-simulators (FSD/FTD together with ETASC)
SN/conventional
Response from FSD (1/2)
Re-attachment physics: Key question is trying to identify the relevant components determining the time scales on present day devices, and then extrapolate  Action: slow-transients expts, data mining, potential new expts
Transport in divertor: Composite effect of Cross-field drifts, perpendicular turbulent transport and diffusive transport via CX of momentum and power, complex  requires full model, input from RT09/13/14/15/18
Impurity concentration/compression ratio: fwd/rev field expts RT13/14, basic models exist, extrapolation: full model reqd?, size scaling expts AUG-JET  Action: require modelers and spectroscopists working on AUG/JET/ITER to sit down to decide what could be done; end of 2021 campaign; depends on DEMO scenario
Impurity mix: The optimization criteria/metric needs to be defined first, max frad seems independent on mix, but confinement depends on mix

## Slide 22: Open points – Basic Physics
Physics of re-attachment, as function of power, density and impurity (incl. fluctuations), pellets; time-scales
Transport in divertor region: prediction of broadening factor S
Prediction of impurity concentration and compression ratio
Optimum impurity mix (species) for DEMO-like conditions (models?)
On size scaling (geometry) and impact on impurity transport /compression
LH transition threshold (and possible hysteresis) with radiating core (e.g. XPR) going beyond Martin's scaling; revised IPB98 scaling with impurity radiation loss (or rather include radiation in transport models?)
Predictability of time-dependent state-of-the-art models and tools to predict divertor transients and dynamics; flight-simulators (FSD/FTD together with ETASC)
SN/conventional
Response from FSD (2/2)
Size scaling: Comparisons from experiment for N2 existing between AUG and JET; (reduced model existing Henderson, Hitzler, Huber 2020)  Action: requires human resource, could be done without additional pulses, RT13/14/18 & previous JET/AUG comparative expts
LH transition threshold:  Action: Information from JET and WPTE experiments on isotope effects and scalings; L-H threshold with radiation: data mining required to identify if and what type of experiments exist  potential new experiments
Flight simulators: TSVV11, sufficiently and timely? Enough resources for reduced-models on core/edge coupling? Transients?  top-down approach needed?

## Slide 23: Open points – Reduced Models
Expanding on the extension/improvement of 0D model towards 1.5/2D model w.r.t confinement regime (reduced model) - scaling? Numerical model?
Towards improved figure-of-merits for HF (i.e. detachment) and cZ
[Siccinio, NF 2019]
Based on
Martin scaling for PLH
Goldston & Reinke Scalings for cZ and lq
Conservative case:
Response from FSD
cz: ongoing, current approach double track for cz 1) experiments on AUG and JET  extract scalings for cz 2) Numerical modelling done for various devices, but combining modelling results from various publications not done
Higher B-field: no activity inside WPTE; numerical experiment attempted by Hitzler but not very successful numerically  Action: recommendation remains to reach out to C-MOD data, analysis exists, modelling and detailed comparison died out in 2017/2018; Compass-U?
Transport, i.e. lq & S: Input from RT13/14/18

## Slide 24: Open points – „off baseline“
Resilience of ADC against re-attachment
Reattachment dynamics in ADC (e.g. double-null)
Does reattachment change its dynamics in ELM-free regimes (different “pedestal” conditions, fluctuations of different nature – e.g. bursts in I-mode)?
Response from FSD
ADC’s resilience against re-attachment: Needs to be proposed for WPTE RT18 – not included in current activities that focus on maximizing dissipation as primary objective to identify if the ADCs are real candidates…  Action: proposal submission but should be second priority after having established if ADC provide significant dissipative advantage
Re-attachment dynamics in ADC (e.g. DN): Generally nearly no D/DN activity  Action: require explicit proposals and pulses and a clear question to be answered (as we do not even know the dissipative properties of DDN from experiment)
Reattachment in ELM-free regimes: Could be incorporated in RT09/08/13 if target scenario identified (closing gaps)