## Slide 1
DEMO transient and dynamic phases an analysis of the priorities
E. Joffrin, M. Siccinio and F. Koechl

## Slide 2
Definitions:
Phases that are not triggered by alarms but consitutive of a typical scenario for reaching and landing the desired operating scenario for optimised fusion power in DEMO
Scenario flat top assumptions: H=1 no ELM high beta (~3) radiation( >90%) detached regime as operating point (120% Greenwald) + auxillary heating (ECRH). Regime left undefined in this study.
Transient « planned » phases and scenario:
Definitions

## Slide 3
Transient phases
1 2
3 4
Flat top
(defined previously)
Phase I: Breakdown - Burnthrough – X-point & L-mode ramp-up
Phase II: Access to high confinement regime
Phase III: End of Burn – transition to L-mode ramp-down
Phase IV: Ramp-down – L-mode plasma landing

## Slide 4
Rating:
DEMO priority:
1=to be done in 2022;
2=action to be discussed for 2023 and follow up the on-going development in FSD WPs;
3=no actions required at this stage
Resource impact for executing the task: 1=low ; 2=medium ; 3=high
Approach
Identify which physics/technical questions that should be addressed in the area of scenario transients as defined earlier.
Prioritize the questions in terms of DEMO priorities
Assess the resource impact and the work presently being done in FSD or elsewhere for each questions (not exhaustive)

## Slide 5
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Modelling suite breakdown-burnthrough-ramp-up. ECRH assist. | Integration of the burnthrough model (TSVV11) | 2 | 2 | Existing BD codes to DEMO – BKD0 + GRAY. RT03 (WPTE) - (WPrIO + TSVV11 + WPSA)? include background gas from the wall.
 | Introduce edge modelling in L-mode code | 2 | 2 | TSVV11 (QUALIKIZ); RT03 RAPTOR, Sauter, ppy.
Flux consumption (Ip ramp, shape sequence, X-point formation, fuelling, heating requirements, minimize duration) | Level of ECRH power required to minimize flux consumption | 2 | 2 | METIS (+ray tracing)
 | Impurity W level: Modelling with model. | 1 | 2 | ASTRA/RAPTOR : calculating the W in ramp-up : reduced tool. TE/PWIE Experiment: AUG, WEST Plasma background existing ?
 | DEMO simulator: X-point formation and subsequent shape sequence with CREATE simulation including a more sophisticated transport description. | 1 | 2 | Limiter phase to be done with simple transport model TSVV11, but reduced model JETTO or ETS
Breakdown - Burnthrough – X-point & L-mode ramp-up
Phase I

## Slide 6
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Avoidance of run-away or supra-thermal electrons and MHD boundaries | Assess the run-away domain in dIp/dt, low density conditions. | 2 | 1 (master project?) | ITPA work on-going (P. de Vries)
 | Assess kink or reversed q instabilities in ramp-up in DEMO. | 2 | 1 (master project?) | WPCD MHD workflow to be considered
Control of heat load in the ohmic ramp-up in detachement condition after the X-point formation + impurity control (extrinsic and intrinsic) | Impurity modelling for minimizing W in the core after X-point formation: use of ECRH power | 1 | 2 | See above
 | Minimize erosion of W in ramp-up to tell W influx - reduced model | 1 | 2 | Data of AUG and WEST (N2 in ramp-up: ERO modelling available)
 | Detachment control in L-mode ramp-up: (1;2) | 1 | 2 | Experiment RT01; RT14. JET past experiment. + TSVV7
Breakdown - Burnthrough – X-point & L-mode ramp-up
Phase I

## Slide 7
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Isotopic effect in the ramp-up | Isotopic effect on current ramp-up | 3 | 2 | JET observations / data mining Transport models with isotope effect Different sputtering H/D/T Integrated modelling available for this?
Breakdown - Burnthrough – X-point & L-mode ramp-up
Phase I

## Slide 8
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
MHD boundaries during transition. (including ELM avoidance) | Analysis of stability risks | 2 | 2 | Data mining for an MHD study (AUG, WEST, JET)+ modelling id required
q profile evolution with increasing boostrap fraction to reach target beta | JETTO SANCO calculations | 2 | 1 | Extend Koechl simulation within DEMO activity. TSVV11 Experiment in WPTE (Felici)
Additional power requirements to reach high confinement phase. L-H threshold. | LH threshold / power requirement | 1 | 2 | JET/AUG/… L-H threshold experiments (H,D,T) results. Modelling: TSVV1 JETTO SANCO calculations (Koechl within DEMO activity)
Ion/electron power equipartition | Access to the relevant collissionality regime | 1 | 1 | included in TSVV10/TSVV11 + Florian existing simulations
Dynamic of the fusion power rise including fast particle losses | Experiments mimicking Pfus with ECRH/ICRH in real time, in WPTE devices | 1 | 2 | JINTRAC+ASCOT Experiment mimicking the fusion in real time.
Access to high confinement regime
Phase II

## Slide 9
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Dynamics of radiation balance in detached conditions. Power control | See detachment / re-attachement topic |  |  | TSVV 7
W impurity transport control: high Ti or high central Te during the transition (R. Dux). | Ti temperature screening | 2 | 2 | ITER (Loarte, JETTO/SANCO). JET recent experiments. More experiments in WPTE machine to demonstrate this effect: RT01/RT02 + modelling and application to DEMO? Small/no ELM regime?
Density control in real time | Model of density control for DEMO including time scales | 2 | 1 (master project?) | DEMO activity in WPDC (Kai Jacob Brunner) Pellet usage. Test in exp?
Access to high confinement regime
Phase II

## Slide 10
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Radiation (including synchrotron) and power balance control during the transition when Pfus decreases in detached conditions Role of the fusion power + auxiliary power in the dynamic of the transition | Exit from H-mode. Expanding what already available or planned (column 5) | 1 | 2 | Radiation calculation for DEMO in a DT plasma (ASTRA); Slow ramp-down down (0.1MA/s) to low density experiment in full tungsten device in detached conditions in AUG/WEST? Experiments mimicking the fusion power using ECRH/ICRH in real time in WPTE devices: WPTE: RT01, RT12; JET Baseline ITER modelling with JINTRAC – ASTRA-simulink for DEMO. Develop this including kinetic-magnetic coupling (DEMO future activity)
End of Burn and transition to L-mode ramp-down
Phase III

## Slide 11
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Fuelling requirements for controlling the dynamic phase from H- to L- mode + pellet fuelling effect. | Fuelling termination with pellet to expel impurities | 2 | 1 | Experiments: JET De la Luna (IAEA 2018).  check whether this applies to DEMO. Control the impurity content in the core at the transition (pellet?)
Dynamic of the H-L transition H-L threshold control during the end of burn Model for the transition H-L (+type I, type III) usually using the L-H scalings. Hysterisis. | Dynamics of the H-L transition | 2 | 3 | Data mining in tokamaks. (Database + study by P. de Vries). Develop the study for DEMO from this initial experimental study. Model development in TSVV1 for the H-L transition Learn in existing experiments for the H-L transition
Error field compensation with in-vessel coils (needed at low density) Pressure and q-profile evolution at end of burn: MHD stability ? | DEMO estimate the potential amplitude of the error field. | 3 | 2 | Experiments in WPTE (RT01)
End of Burn and transition to L-mode ramp-down
Phase III

## Slide 12
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Dynamic balance of input power versus radiation losses in detached conditions in L-mode in current ramp-down | Control of detachment in L-mode (see Marco’s document) | 2 | 2 | Experiments in JET/AUG/WEST. Also data mining More experiment ?
Radiation power and density control | See ramp-up in L-mode for density control | 2 | 1 | 
Vertical stability control: control of betap and li within boundaries. MHD stability | Review of the existing work in todays machine and ITER | 1 | 1 | JET past experiments. Models existing. PPY in DEMO: shape sequence with CREATE. Simplified transport model for betap and li can be introduced later. Explore benefit of in-vessel coils.
Ramp-down – L-mode plasma landing
Phase IV

## Slide 13
Issue | Task (modelling/ experiments / data mining / analysis) | DEMO team priority | Resources impact | What is existing or could be done in the DEMO Activity or within FSD/FTD
Landing plasma shape sequence to keep heat loads and density/pumping under control | Calculate heat loads as plasma approaches the wall in the landing scenario | 1 | 2 | Code can calculate heat loads using ASTRA. TSVV7. Work to be done. Existing tools in WPTFV (DEMO) for pumping modelling
L-mode transport model (boundary conditions) | Need to improve the model in L-Mode | 2 | 3 | Liaise with TSVV11
Ramp-down – L-mode plasma landing
Phase IV

## Slide 14
Conclusions
This exercise has identified a set of 11 specific tasks on key physics or technical questions for strengthening the scenario development on DEMO for transient phases.
In many cases the tools are existing and can be used (JETTO, ASTRA, METIS, CREATE, JINTRAC, SANCO, etc …).
Also a couple of TSVVs may play a role (TSVV7, TSVV11) and could be involved. However they are unlikely to play an immediate role.
In other cases experiments can be motivated in the 2022 Programme: this can be discussed within the WPTE Programme
The proposal is now to designate ROs for each these tasks to define in more details the work plan and the resources needed in FSD or FTD.