## Slide 1
Which tools are already in place that can improve geometry treatment?
Array IGJUM3 is available for storing information about which additional surfaces is visible from a cell
Can be set via input or user provided routines
Vectors NLIMII and NLIMIE hold the range of surfaces indicated in IGJUM3 for each cell. This is taken into account in calculating intersections of particles with additional surfaces
Subroutine CUT_ADS_CELL:
  finding cells being intersected by additional surfaces.

## Slide 2
Subroutine CUT_ADS_CELL
Not as sophisticated as I remembered
Only checks triangle meshes and additional surfaces described as two-point surfaces
Available but switched off
The algorithm starts from the coordinates of the vertices specifying the line
It finds the triangles holding the vertices.
Starting from the triangle holding the first vertex the intersections with the line surface and the triangle faces are calculated.
The intersection in direction to the second vertex indicates the next cell along the line.
By moving alone the line all triángles intersected by the line are found.
This algorithm can not easily be adopted for other sorts of additional surfaces

## Slide 3
Can the octree approach be used for all kinds of additional surfaces?
Right now the octree only deals with plane surfaces defined by 3, 4 or 5 vertices
(3 <= RLB <6)
In principle the octree can b2 used for all types of additional surfaces, but
one needs to find good tests in order to check if a surface is inside of or intersects with the respective volume
This might be relatively easy for additional surfaces limited by a rectangular box (RLB=1)
It might be hard for surfaces limited by a collection of linear or second order equations
(RLB <0)