## Slide 1
P. Donnel, G. Di Giannatale, L. Villard
Global gyrokinetic studies of Negative Triangularity turbulence
P. Donnel, TSVV2 progress meeting, 02/12/2021

## Slide 2: Preparation of ORB5 for the study
Arbitrary geometry
Hybrid electron model (trap.=kin., pas.=adia.)
Global
Flux driven
Collisions
Robust boundary conditions (edge study)
ORB5 [Lanti 2019]
Recent upgrades
Non linear and multi-species collisions
[Donnel 2021]
ECRH/ECCD source [Donnel 2021]
Introduction of a buffer zone

## Slide 3: Realistic ECRH/ECCD source
Analytical developpment of a quasilinear operator to model ECRH [Donnel 2021] and ECCD [to be submitted] in the case of an equatorial propagation of the beam.
Comparisons with LUKE/C3P0 are ongoing
ECCD
ECRH

## Slide 4: Three options for the buffer zone
Naive Krook
Krook conserving particles:
+ C
with C is a scalar chosen to conserve over spatial bins
Collisionnal buffer
(Handled via Langevin kicks)
In all cases,
if
where
See Giovanni’s presentation for more details and upgrades

## Slide 5: Generation of the MHD equilibrium with CHEASE
CHEASE is a MHD equilibrium solver. It needs as an input
The shape of the plasma boundary
Profiles of pressure and plasma current
The following steps have been performed to construct the equilibria for the study
Identify a pair of well diagnosed TCV shots with positive and negative triangularity
Take the experimental profiles and extend them in prevision of the buffer (flat pressure, no current, change the shape of the plasma boundary)
Make sure the equilibria are in agreement with experimental datas (profiles in the «core», plasma shape at the «LCFS»)

## Slide 6: Choice of the initial profiles for the study
Two well diagnosed TCV shots with matched profiles (60797 for δ>0, 58499 for δ<0) have been chosen.
[Fontana 2020]
For this parameters, a mixed ITG/TEM turbulence is predicted (TEM dominant [Merlo 2019] )

## Slide 7: Hybrid e- + collision + ECRH + shaping
Buffer zone
Smaller fluctuations in the case of negative triangularity
Large impact of shaping on the electric potential development
P. Donnel, TSVV2 progress meeting, 02/12/2021

## Slide 8: Important effect of time on the buffer potential
time
P. Donnel, TSVV2 progress meeting, 02/12/2021

## Slide 9: Energy decaying rate
δ<0
δ>0
δ<0
δ>0
δ<0
δ>0
Significant improvement of confinement in negative triangularity in the edge. Marginally the opposite in the core
P. Donnel, TSVV2 progress meeting, 02/12/2021

## Slide 10: Particle confinement time
δ<0
δ>0
δ<0
δ>0
Significant improvement of confinement in negative triangularity in the edge. Marginally the opposite in the core
P. Donnel, TSVV2 progress meeting, 02/12/2021

## Slide 11: Limited impact of the source level
100 kW
200 kW
300 kW
P. Donnel, TSVV2 progress meeting, 02/12/2021

## Slide 12: Conclusion
Flux-driven, global GK simulations of shaped plasmas in presence of collisions have been performed for the first time with ORB5
Improved confinement of negative triangularity retrieved (only when including trapped kinetic electrons and collisions)
Difficulty to reach a quasi-steady state
Necessity to improve the boundary condition

## Slide 13: Next steps
Study the impact of buffer (type, , ) in adiabatic electrons, then with hybrid electrons
Try to reach a quasi-steady state
Upgrade of GYSELA to be able to simulate the same physics
Comparison between GK codes (ORB5, GENE, GYSELA)
Comparison between GK simulations and experiments
Giovanni’s presentation

## Slide 14: Non linear collision operator
Generalised Laguerre
Irreducible
Harmonic
Moment of the distribution
[Hirshman 1981, Ji 2006]
Unshifted Maxwellian distribution
Normalized velocity:
t
t
t
t
t
t
1
1
Truncation of the distribution function consistent with neoclassical physics
t
t
Collision of a distribution function of species a () on a distribution function of species b ():