## Slide 1: Linear KBM simulations in W7-X equilibria and plans for nonlinear simulations
TSVV#13 Progress Update – November 8th 2021
Paul Mulholland , Josefine Proll and MJ Pueschel
in collaboration with Ksenia Aleynikova

## Slide 2: Outline
Reproducing previous linear KBM results (Aleynikova 2018) – how they were carried out?
New exploratory linear simulations (different gradients, values, W7-X configurations)
Looking for suitable regime for nonlinear KBM runs (not yet done in W7-X)
Plans going forward

## Slide 3: Current Deliverable - D2.6 / D-KBM-BASIC
Map out KBM saturation and flux scalings (linear and nonlinear electromagnetic ITG stabilization) at high vs. low magnetic shear, and apply the acquired knowledge to the W7-X configuration space. This will expand the physics basis on electromagnetic turbulence in 3D geometry.
Due dates:
  Linear part of the work will be performed during 2021.
  Nonlinear analyses to be accomplished by Dec. 2022.

## Slide 4: Current Deliverable - D2.6 / D-KBM-BASIC
Map out KBM saturation and flux scalings (linear and nonlinear electromagnetic ITG stabilization) at high vs. low magnetic shear, and apply the acquired knowledge to the W7-X configuration space. This will expand the physics basis on electromagnetic turbulence in 3D geometry.
Due dates:
  Linear part of the work will be performed during 2021. (On track )
  Nonlinear analyses to be accomplished by Dec. 2022. (Start later this year)

## Slide 5
Reproducing linear results
in W7-X
Aleynikova 2018

## Slide 6
Reproducing linear results
in W7-X
KJM
Discrepancies due to using equilibria with different “volume-averaged for both species” =
Aleynikova 2018
Local dynamic
for one species

## Slide 7
Reproducing linear results
in W7-X
KJM
Aleynikova 2018
Local dynamic
for one species
One VMEC equilibrium file: held constant
evaluated by GENE as is increased
Inconsistent approach – equilibrium should change with
Simulation approach
KBMs – driven by pressure gradient
GENE:
Discrepancies due to using equilibria with different “volume-averaged for both species” =

## Slide 8: approach - levels of consistency
Totally inconsistent – keep equilibrium constant and constant as local is increased in GENE
Partially consistent – keep equilibrium constant, evaluate self-consistently as is increased
Consistent (as much as possible) – vary equilibrium files throughout simulation (corresponding to increased ), and evaluate self-consistently as is increased

## Slide 9: approach - levels of consistency
Totally inconsistent – keep equilibrium constant and constant as local is increased in GENE
Partially consistent – keep equilibrium constant, evaluate self-consistently as is increased
Consistent (as much as possible) – vary equilibrium files throughout simulation (corresponding to increased ), and evaluate self-consistently as is increased
Fast computation of large linear runs
For studying behaviour of instabilities
Insufficient accuracy

## Slide 10: approach - levels of consistency
Totally inconsistent – keep equilibrium constant and constant as local is increased in GENE
Partially consistent – keep equilibrium constant, evaluate self-consistently as is increased
Consistent (as much as possible) – vary equilibrium files throughout simulation (corresponding to increased ), and evaluate self-consistently as is increased
Fast computation of large linear runs
For studying behaviour of instabilities
Insufficient accuracy
For higher accuracy studies
Finding linear instability thresholds
Finding suitable regimes for nonlinear studies
Nonlinear simulations

## Slide 11
Small crosses – totally inconsistent:
Fixed equilibrium
Fixed
Large crosses – partially consistent:
Fixed equilibrium
Consistently calculated
We applied second approach
Aleynikova 2018

## Slide 12: approach – impact of inconsistency in W7-X
Varying equilibrium consistently:
increases with dynamic
Aleynikova 2018
Inconsistent – equilibrium held fixed:
= 0 as dynamic increases

## Slide 13
Choosing W7-X Configurations
KJM
ILD
FIS
DKH
Want a variety of shear values, safety factors, etc.

## Slide 14
Choosing W7-X Configurations
KJM
ILD
FIS
DKH
Want a variety of shear values, safety factors, etc.
Will compare these two configurations to start

## Slide 15
KJM
ILD
= 3
△ - ITG
□ - KBM
Effect of geometry on KBM threshold
ITG
ITG
KBM
KBM

## Slide 16
KJM
ILD
= 3
△ - ITG
□ - KBM
Effect of geometry on KBM threshold
ITG
ITG
KBM
KBM
ITG-KBM -threshold decreases for lower ?

## Slide 17
= 2
= 3
= 4
△ - ITG
□ - KBM
Effect of gradients on KBM threshold
Geometry: KJM
ITG
ITG
KBM
KBM

## Slide 18
= 2
= 3
= 4
△ - ITG
□ - KBM
Effect of gradients on KBM threshold
Geometry: KJM
ITG
ITG
KBM
KBM
ITG-KBM -threshold decreases for increasing

## Slide 19
Recap of linear simulation progress
Reproduced previous linear KBM results in W7-X
Selected variety of W7-X configurations with different levels of shear and safety factor
Begun simulating KBMs linearly (partially consistently up to now)
Noted effect of varying temperature gradients and shear on linear KBM behaviour

## Slide 20
Recap of linear simulation progress
Reproduced previous linear KBM results in W7-X
Selected variety of W7-X configurations with different levels of shear and safety factor
Begun simulating KBMs linearly (partially consistently up to now)
Noted effect of varying temperature gradients and shear on linear KBM behaviour
Next:
Will need to run same simulations fully consistently with more configurations before drawing conclusions
Find suitable parameter regimes for nonlinear runs

## Slide 21: Search for nonlinear KBM regime
NL regime difficult to find due to peaking at in W-7X (for high temperature gradients)
Need finite (where KBMs stable) in order for NL runs to saturate
Ideally, will find a regime analogous to HSX
Want to isolate a KBM -range which has a finite lower bound (> 0)
Aleynikova 2018
McKinney 2021

## Slide 22: Exploratory linear simulations
= 2
= 2%
□ - KBM
△ - ITG
Geometry: KJM

## Slide 23: Exploratory linear simulations
= 2
= 2%
□ - KBM
△ - ITG
Distinct peak in for KBMs: purely numerical?
Geometry: KJM

## Slide 24: Exploratory linear simulations
= 2
= 2%
□ - KBM
△ - ITG
Distinct peak in for KBMs: purely numerical?
Geometry: KJM
Further investigation required, e.g. n_pol >1

## Slide 25: Linear and nonlinear KBMs in HSX
McKinney 2021
KBMs: Low linear growth rate, yet cause of large nonlinear heat flux
Quasilinear estimate of heat flux

## Slide 26: Linear and nonlinear KBMs in HSX
McKinney 2021
KBMs: Low linear growth rate, yet cause of large nonlinear heat flux
Quasilinear estimate of heat flux
KBMs very important nonlinearly - dominant cause of transport

## Slide 27: Nonlinear plan going forward
Motivation – enhance physical understanding of KBMs (very important nonlinearly)
Compare linear and nonlinear features – how do KBM thresholds change?
How much can linear tell us – e.g., do high growth rates imply large nonlinear heat flux? Do KBMs dominate nonlinearly?
Limitations of GENE flux tube simulations: can saturated nonlinear KBM simulations be achieved in ANY configuration?

## Slide 28: Final remarks
Linear simulations well underway – will dive deeper and investigate effects of shear in W7-X
Almost ready to explore nonlinear regimes (before end of this year)
Nonlinear simulations - difficult in some configurations (for reaching saturation in realistic regimes)
Find suitable parameter regimes that reach saturation to better understand nonlinear electromagnetic instability behaviour

## Slide 29
Extras

## Slide 30: Deliverables
By 2022: map out KBM saturation and flux scalings (linear and nonlinear electromagnetic ITG stabilization) at high vs. low magnetic shear, and apply the acquired knowledge to the W7-X configuration space.
By 2023: perform linear and nonlinear simulations using high- and low-beta W7-X equilibria and profiles for direct link to experiment.
By 2024: construct and test quasilinear models first for electrostatic kinetic-electron turbulence, then for high-beta high-grad-T_i plasmas, in order to determine to what extent fast quasilinear transport models can be applied to finite-beta stellarator plasmas.

## Slide 31
Importance of using correct
Need to be fully consistent!