## Slide 1: Runaway Electrons in Tokamak Disruptions Where do we stand? What should we do?
E. Nardon
Acknowledgments: TSVV 9 team
EUROfusion FSD Science Coordination Meeting, 18/01/22

## Slide 2: Outline
Present knowledge and open questions
Prospects for ITER
Tools and plans

## Slide 3: Outline
Present knowledge and open questions
Prospects for ITER
Tools and plans

## Slide 4: Theory
Review papers: [Breizman NF 2019] [Boozer PoP 2015]
RE generation mechanisms have been identified and explored theoretically:
  Primary:
    Non-nuclear: Dreicer, hot tail
    Nuclear: Tritium β decay, Compton scattering
  Secondary: avalanche
Seminal theory works from several decades ago (e.g. [Rosenbluth NF 1997]) but important recent developments:
  Effect of partial screening of the nuclear charge of partially ionized impurities [Hesslow JPP 2018]
    Bound electrons may boost the avalanche [Hesslow NF 2019]
  Phase space dynamics
    Theory of 2 threshold E|| fields [Aleynikov PRL 2015]
    RE vortex [Guo PPCF 2017]
  Self-consistent model for hot tail generation during a thermal quench [Aleynikov NF 2017]
  …

## Slide 5: RE generation models
Validation of RE generation models in quiescent plasmas is well advanced
  Threshold E|| field larger than Connor-Hastie value in several machines [Granetz PoP 2014]
  Kinetic whistler wave instabilities may play a key role in this [Liu PRL 2018]
Models for RE generation during disruptions are not mature yet
  More difficult than quiescent situations because of 3D MHD
    Electron transport due to magnetic stochasticity
    Electron acceleration by large MHD-driven E|| [Sommariva NF 2018]
    Impurity mixing
  3D MHD codes…
    …are just beginning to produce ~ plausible disruption simulations [Nardon PPCF 2021]
    …have not yet produced disruption simulations with a self-consistent treatment of REs
      but test particle studies have been done with JOREK [Sommariva NF 2018] [Särkimäki, in prep.]
  <3D codes (e.g. ASTRA-STRAHL [Linder NF 2020] or DREAM [Brandström MSc 2021])…
    …are more advanced in terms of self-consistent RE modelling
    …but how to take 3D MHD into account?
      3D-MHD-related factors are often used as knobs in order to match experimental data → Validation or ‘fancy fit’?

## Slide 6: RE beam impact
Physics of the RE beam impact is only partly understood
‘Standard’ RE beam impacts seem to be highly localized
  ∆rRE ~ 1-2 mm allows reproducing post-mortem observed melt pattern on JET [Chen AAPPS 2021]
  Order of magnitude of ∆rRE seems consistent with a Larmor radius
Toroidal peaking is observed, e.g. at JET ‘beyond misalignment tolerances’ [Reux NF 2015]
  Suggests role of MHD
Termination is typically bursty (HXR, magnetics) at DIII-D and JET
  Due to MHD? Or perhaps to RE filaments [Eriksson PRL 2004]?
A large fraction of the magnetic energy can be converted into RE kinetic energy during the termination
  Crucial in ITER because typically Emag >> Ekin
  The converted fraction grows with τloss/τres [Martin-Solis NF 2014]
  → A fast termination (small τloss) with clean a background plasma (long τres) is beneficial
A proposed ITPA DivSOL/MDC collaboration on the “Characterization of power deposition to PFCs by REs” is under discussion (coordinators: E. Hollmann, E. Nardon)

## Slide 7: RE beam mitigation
Benign RE beam termination observed in JET and DIII-D after a D2 SPI into the beam [Reux PRL 2021]
  JOREK simulations suggest a strong heat flux spreading due to large MHD [Bandaru PPCF 2021]
    Probably much larger MHD than in ‘standard’ terminations
  Absence of Emag → Ekin conversion thanks to fast termination and clean background plasma probably also plays a role

## Slide 8: Outline
Present knowledge and open questions
Prospects for ITER
Tools and plans

## Slide 9: The ITER Shattered Pellet Injection (SPI) system
  Objectives:
    Thermal load mitigation
    Electromagnetic load mitigation
    RE avoidance
    RE mitigation
  Up to 24 pellets from midplane (3 different ports)
  Pellet size ~ wine bottle cork (1 pellet contains ~2 x 1024 atoms)
  Material: Ne+H2
    Ne needed to radiate the energy and make the current quench short enough
    H2 may be useful for RE avoidance or mitigation
  Velocity: a few 100 m/s
  Shattering by bend at end of flight tube
    Number & size of shards depend on bend angle and pellet velocity

## Slide 10: Prospects for RE avoidance in ITER (1/3)
Increasing ne by injecting H2 reduces all seeds except Compton
  Would need to reach ne ~ 2-4 x 1021/m3 to avoid large beam from Compton-initiated avalanche, according to [Martin-Solis NF 2017]
  …but recent simulations with GO predict that this will not work because of recombination, such that a multi-MA RE beam will form, whatever the assimilated Ne+H2 mixture [Vallhagen JPP 2020]
  Open question: may MHD instabilities deconfine REs before the beam becomes dangerous?
Too slow CQ
General considerations:
  Avalanche gain scales exponentially with Ip → Will be >> than in present machines
  Dreicer seed expected to be negligible (Te sufficiently ‘high’ during CQ)
  Hot tail seed hard to predict but could be very large
  Nuclear seeds small but non-negligible due to huge avalanche gain

## Slide 11: Prospects for RE avoidance in ITER (2/3)
Non-nuclear phase may be easier (no Compton source) but hot tail generation remains a risk
However, hot tail generation might be suppressed by a 2 step scheme: 1) H2 SPI, 2) Ne SPI [Nardon NF 2020] [Vallhagen, in prep.]
    H2 SPI → dilution cooling without immediate TQ, leaving time for electron distribution to cool down to a few 100 eV as a Maxwellian
Open question: effect of the drift of ablation plasmoids towards the LFS?
  Large radial transport of the injected material observed at DIII-D [Shiraki APS 2021]

## Slide 12: Prospects for RE avoidance in ITER (3/3)
Other ideas:
For the active phase (assuming negligible hot tail seed): post-TQ injection of solid fragments to stop nuclear seeds before they avalanche [Nardon NF 2021]
Shard cloud
RE
Waves / kinetic instabilities
  Role of ~MHz modes in RE generation during DIII-D disruptions suggested by observations [Lvovskiy PPCF 2018]
  Modelling interprets the modes as Compressional Alfvén Eigenmodes [Liu NF 2021]
  Exploitable in ITER?
    Need to avoid collisional damping, i.e. need low enough ne, high enough Te

## Slide 13: Prospects for RE mitigation in ITER (1/2)
Injection of high Z material into the RE beam used to be considered as a possible mitigation scheme, but…
In ITER, high vessel conductivity implies Zp = f(Ip) for fast CQ
→ Strongly limits the possibility to reduce Ip before impact
Emag → Ekin conversion during the termination could be large
→ Pessimistic outlook for strategies based on high Z material injection according to DINA modelling [Konovalov IAEA 2016]
Courtesy J. Artola
2D JOREK simulations
How much mitigation is needed, i.e. what is the tolerable IRE at impact?
Estimates based on a ‘scraping-off’ model (∆rRE ~ a few mm) and assuming no Emag → Ekin conversion give a tolerable IRE (for cooling channel integrity) between ~100 kA and ~3.6 MA depending on hypotheses, e.g. concerning toroidal uniformity [Chen AAPPS 2021]

## Slide 14: Prospects for RE mitigation in ITER (2/2)
H2 SPI into RE beam is now considered the best hope for RE mitigation in ITER after promising results at DIII-D and JET.
Prospects and open questions for ITER [Paz-Soldan APS 2021]:
  Shards will probably be sublimated at the edge of the RE beam
  Subsequent expansion of ablation clouds to be clarified: do clouds stay neutral enough that they can expand across the whole plasma? [Kiramov NF 2020][Samulyak et al., ongoing]
  If they do not expand much, will the material mix sufficiently fast? [Hollmann APS 2021]
  Assuming good mixing, recombination can be obtained with the right amount of H2
    Possibly key to get
      fast and large MHD instability
      clean background plasma
  Amplitude of MHD modes? Need 3D non-linear MHD modelling, e.g. with JOREK [Bandaru PPCF 2021] or M3D-C1 [Liu APS 2021]
Another idea (not assessed yet): spread the impact by applying Resonant Magnetic Perturbations

## Slide 15: Outline
Present knowledge and open questions
Prospects for ITER
Tools and plans

## Slide 16: Tools (TSVV 9)
2 main ‘workhorses’:
DREAM kinetic code [Hoppe CPC 2021]
  Solves 1D flux surface averaged transport equations
    Disruption-oriented (e.g. includes impurities)
  Self-consistently evolves the electron distribution function using a bounce-averaged kinetic equation
JOREK 3D MHD code [Hoelzl NF 2021]
  Can include REs as a fluid [Bandaru PRE 2019] or as test particles [Sommariva NF 2018] [Särkimäki, in prep.]
Other tools: LUKE, ASTRA, ETS, …

## Slide 17: Plans (1/2)
Simulate RE generation and avoidance in ITER with DREAM and JOREK (revisit GO study)
  DREAM will provide more precise kinetic effects
    First investigations on hot tail + stochastic transport published in [Sveningsson PRL 2021]
    More simulations planned under Chalmers Univ.-IO collaboration agreement
  JOREK will allow assessing the possible effect of MHD instabilities
    Planned under IPP-IO collaboration agreement
Improve RE generation models in <3D codes:
  In particular concerning 3D MHD effects:
    Transport due to magnetic stochasticity
    Acceleration by MHD-driven E||
    Impurity mixing
  Strategy:
    Assess effect based on JOREK simulations, e.g. using test particles [Särkimäki, in prep.] [Sommariva NF 2018]
    Increase our confidence that JOREK captures these effects well
    Provide reduced models to DREAM and others
Mainly covered by TSVV 9 but hope for support from WPTE for validation, + support from IO

## Slide 18: Plans (2/2)
Validate DREAM for RE generation
  Database of pulses
  Uncertainty quantification
Validate JOREK for RE generation
  For a few pulses, detailed comparison with experimental data using several synthetic diagnostics
Assess effect of drift of ablation plasmoids towards the LFS and consequences for 2 step SPI scheme
Model RE mitigation by D2/H2 SPI
  Develop DREAM and JOREK to model self-consistently the RE beam and its background plasma …and D2/H2 SPI into this system
  Model the beam termination with JOREK, starting from an MHD stable situation and self-consistently including the background plasma
  Model the beam termination with DREAM, with ad hoc 3D MHD effects (e.g. from JOREK)
  Validate against e.g. JET or DIII-D data
  Make ITER predictions and find optimal strategy
Study possible use of (RE-driven or externally injected) waves / kinetic instabilities for RE avoidance or mitigation

## Slide 19
Backup slides

## Slide 20
K. Särkimäki