## Slide 1: Core Instabilities (ETG, ITG, TEM) and Configuration Effects
Gavin M. Weir, Marc Beurskens
On behalf of the W7-X Team

## Slide 2: Three dimensional magnetic geometry significantly modifies the stability properties of microturbulence
Quasi-isodynamic configurations with the maximum-J property are predicted to be theoretically resilient to collisionless trapped particle modes, such as the TEM [J.H.E. Proll PRL 108 2012]
Reason: Delocalization of trapping regions and curvature drive: Trapped particles sample good curvature (on average)
Where = and =, the heat transport driven by TE and ITG modes is expected to dominate over that from ETG modes in stellarators [G.G. Plunk, P. Xanthopoulos, G.M. Weir et.al., PRL 122, 2019]
Reason: High variation in local shear prevents formation of large radially coherent structures in stellarators
The ITG mode is predicted to be highly localized along a thin strip on the outboard side of W7-X [P. Xanthopoulos PRL 113 2014]
Reason: Large variation in curvature perpendicular to magnetic field
Courtesy P. Xanthopoulos
RMS potential fluctuations in W7-X,
driven non-linearly by the ITG mode.

## Slide 3: The neoclassical optimization of W7-X modifies the turbulent transport
Approximate quasi-isodynamicity (maximum-J) :
"high-mirror", "high-iota" > "standard" (within r/a<0.7)
Flux-surface compression (~Elongation):
  Directly modifies neoclassical transport coefficients
  Modifies real-space gradients (d/dx)
  Highly correlated with rotational-transform in W7-X
  Weakly correlated with trapped particle fraction
Low-iota
High-iota
J.A. Alcusón et.al., PPCF, 2019.
Notes: Additionally, the elongation of W7-X can significantly modify the heat transport.

## Slide 4: ITG driven transport is expected at low ion temperature gradient drive a/LTi~1.4
Low-iota
High-iota
J.A. Alcusón et.al., PPCF, 2019.
  The Gyrokinetic Electromagnetic Numerical Experiment [Jenko et al. PPCF 47 (2005)]
High-iota
Standard
High-mirror
Courtesy P. Xanthopoulos
Nonlinear electrostatic gyrokinetic simulations (GENE):
Flux surface simulations, radially local
Adiabatic electrons
Turbulent ion heat flux driven by ITG turbulence
Approximate quasi-isodynamicity (maximum-J) :
"high-mirror", "high-iota" > "standard" (within r/a<0.7)
Flux-surface compression (~Elongation):
  Modifies real-space gradients (d/dx)
  Weakly correlated with trapped particle fraction
Notes: Additionally, the elongation of W7-X can significantly modify the heat transport.

## Slide 5: Profile resiliency is observed in tokamaks, but not in conventional stellarators
Profile resiliency is the manifestation of stiffness in the electron heat flux
  The ratio of the heat pulse to power balance diffusivity quantifies profile resiliency:
Gyrokinetic modeling indicates that stiffness is driven by turbulent microinstabilities such as the ETG, ITG, and TEM
 Characterizing electron heat transport via heat pules propagation: Stiffness in the electron heat flux?
 Characterizing ion heat transport via power balance measurements: Stiffness in the ion heat flux?
Reproduced from Ryter, PPCF 52 (2010)
  Tokamaks with profile resiliency:
  Conventional stellarators:

## Slide 6: Matched kinetic profile experiments in three configurations of W7-X with varying degrees of approximate quasi-isodynamicity
Matched kinetic profile experiments are necessary to identify magnetic configuration effects on anomalous electron heat transport
Varied the ECRH power deposition location and launched power to match kinetic profiles
Standard / High-iota
Standard / High-mirror
G.M. Weir et al., Submitted to NF (2020)

## Slide 7: Matched kinetic profile experiments in three configurations of W7-X with varying degrees of approximate quasi-isodynamicity
Matched kinetic profile experiments are necessary to identify magnetic configuration effects on anomalous electron heat transport
Varied the ECRH power deposition location and launched power to match kinetic profiles
  The off-axis heating location corresponds approximately to the peak in the neoclassical heat flux (Standard / High-mirror)
Standard / High-iota
Standard / High-mirror
G.M. Weir et al., Submitted to NF (2020)

## Slide 8: Matched kinetic profile experiments in three configurations of W7-X with varying degrees of approximate quasi-isodynamicity
The anomalous core electron heat transport increases with , with a stiffness
Core anomalous electron heat transport is quantitatively similar to non-linear gyrokinetic calculations of the ETG-driven heat transport where Te>Ti and a/LTe > a/LTi
G.M. Weir et al., Submitted to NF (2020)
=1.50.2
=1.40.2
Standard / High-mirror
(0.35<r/a<0.5)
=1.30.1
=1.00.1
Standard / High-iota
(0.35<r/a<0.5)

## Slide 9: The heat pulse diffusivity is more sensitive to changes in turbulence drive than steady-state, power balance analysis
"Standard"-3.7
Square wave ECRH modulation
  17 Hz ECRH modulation
  67% duty cycle
  <20% of total power
The heat pulse diffusivity is determined from the perturbation amplitude-decay, , and phase-delay
,
Jacchia et al., Phys. Fluids 3 (1991)

## Slide 10: The electron heat transport is not stiff in low- W7-X plasmas
0.0 1.0 2.0 3.0 4.0
[m/s]
The electron heat transport is not stiff in low- W7-X plasmas, but it is dominated by anomalous sources
Measured stiffness is consistent with previous measurements in conventional stellarators,
The heat flux scales linearly with at low a/LTe. With on-axis, intense ECRH the apparent stiffness increases.
G.M. Weir et.al., Presented at ISHW (2019)
[keV]
Electron Temperature Profiles
Notes: Electron temperature

## Slide 11: TEM modes are stabilized by collisional detrapping, while the ITG/ETG modes are unaffected by collisions
There is a change in stiffness versus effective collisionality: it is mostly due to a change in ( is approximately constant),
The trend in and versus collisionality is similar in three magnetic configurations with varying levels of quasi-isodynamicity
Standard
High-iota
High-mirror
(0.35<r/a<0.5)
G.M. Weir et al., Submitted to NF (2020)
(0.35<r/a<0.5)

## Slide 12: The stiffness trends downwards with increasing collisionality in W7-X
The TEM mode is stabilized by collisional detrapping; ITG/ETG modes are unaffected
The change in stiffness with collisionality is mostly due to a change in ( is approximately constant)
   Attributed to a transition from TEM to ITG driven electron heat transport in similar experiments on ASDEX-Upgrade
ASDEX Upgrade
Standard
High-iota
High-mirror
Wendelstein 7-X
(0.35<r/a<0.5)
G.M. Weir et al., Submitted to NF (2020)
F. Ryter et al., PRL 95 (2005)

## Slide 13
Ion turbulent heat transport
 Ion temperature clamping
Wendelstein 7-X and ASDEX Upgrade

## Slide 14: Ion temperature clamping in electron heated W7-X plasmas
PECRH = 0.5-7 MW
ne = 1-14·1019 m-3
Te = 1-10 keV
W7-X Stellarator transport
Ion temperature Ti,0 clamped at ~ 1.5keV
No strong configuration dependence
Experimental Ti well below neoclassical predictions

## Slide 15: Ion temperature clamping in AUG L-mode plasmas
AUG Tokamak transport
AUG Ti clamping
PECRH = 0.5-5 MW
ne = 2-8·1019 m-3
Te = 1-11 keV
Ion temperature Ti,0 clamped at < 1.5keV
L-mode or weak H-mode plasmas (0.8 MA, q95 = 5)
What causes the clamping in both devices?

## Slide 16: Expectations for ion turbulent heat transport from linear calculations
Ion heat transport is largely driven by Ion Temperature Gradient driven turbulence (ITG)
Both devices feature a strong additional drive for Te/Ti
Tokamak
Stellarator
Tokamak
W7-X stellarator
(ITG)
(ITG)
= 3
= 2
= 1
= 0.7
[Zocco, Xanthopoulos et al. JPP 84 (1), 2018]
Linear calculations
Linear calculations

## Slide 17: Effect ot Te/Ti on profile stiffness in stellarators: W7-X
Non-linear calculations
Te/Ti
W7-X Stellarator transport
For Te/Ti = 1, no strong degree of stiffness
But Te/Ti exacerbates transport stiffness stronger for nonlinear calculations than linear calculations
W7-X
W7-X stellarator
(ITG)
Linear calculations

## Slide 18: W7-X power balance for ECRH power-scan in Helium
Power scan in helium plasma at ne,0 = 8 1019 m-3
Vary PECRH: 1.2 to 3.9 MW
Te,0 = 1.2 – 3 keV
Ti,0 = 1.2 – 1.8 keV
Er < 0  ion root.
Variation of Qi by a factor 8 in this single power step experiment
Qi,anom >> Qi, NC (Qi,anom = Qi,exp - Qi, NC )
Te,0 = 1.2 – 3 keV
Ti,0 = 1.2 – 1.8 keV
ne,0 = 8 1019 m-3
Er < 0  ion root
Qi,anom >> Qi, NC
W7-X Stellarator transport

## Slide 19: Interplay between heatflux Qi, ratio Te/Ti and gradient 1/LTi
Depending on plasmas radius the ratio increases with PECRH = 1.2 – 3.9 MW
r/a = 0.3:
  Qi,anom increases with PECRH
  increases with PECRH
  decreases with PECRH
r/a = 0.66:
  Qi,anom increases with PECRH
  = constant with PECRH
  increases with PECRH
 Increasing Te/Ti enhances ITG turbulence
Qi,anom
x10
Qi,anom
x7
increases with PECRH
= 1
decreases with PECRH
increases with PECRH
W7-X Stellarator transport

## Slide 20: W7-X achievable ion temperature gradient at r/a = 0.3
W7-X Stellarator transport
Te/Ti increase suppresses
gradient ?
increases with PECRH
decreases with PECRH

## Slide 21: W7-X achievable ion temperature gradient at r/a = 0.4
W7-X Stellarator transport
Te/Ti increase suppresses
gradient ?
increases with PECRH
decreases with PECRH

## Slide 22: W7-X achievable ion temperature gradient at r/a = 0.5
W7-X Stellarator transport
Te/Ti increase suppresses
gradient ?
=1
~ const. with PECRH

## Slide 23: W7-X achievable ion temperature gradient at r/a = 0.66
W7-X Stellarator transport
Te/Ti increase suppresses
gradient ?
=1
increases PECRH

## Slide 24: So what may be behind the so-called clamping of Ti?
PECRH
Heats electrons
Increases power exchange
Pex
exacerbates turbulence:
Stiffness increases
Increases
Te/Ti
Clamping of Ti
gradients
Clamping of central Ti
Tokamak transport
Stellarator transport

## Slide 25: (1) How can we raise Ti,0 with dominant electron heating?
Te/Ti increase
= clamping
Non-linear calculations (kinetic electrons)
W7-X Stellarator transport
increasing Te/Ti makes the ITG scaling jump to curves of apparent stiffness.
Thus keeping Te/Ti = constant avoids clamping and keeps the degree of apparent stiffness low.
Raise PECRH and ne together whilst Te/Ti = constant (Recipe for ECRH enhancement)  high density operation
Low Te/Ti
= Low Stiffness!
χturb ~ χGB

## Slide 26: Conclusions
Jan. 14, 2021
Core turbulence and configuration effects in OP1
26
The stiffness decreases with collisionality in W7-X (at low plasma beta); indicating stabilization of and/or transition to non- driven turbulence, with a stiffness 2: - turbulence exists and is measurable in low-beta W7-X plasmas that is consistent with -TEM/ETG turbulence
The characteristics of the turbulent electron heat transport are dependent on the dominant instability
- -TEM is thought dominant in the outer core region of W7-X (r/a>0.7)
- -TEM/ETG appear to be dominant in the core of W7-X (at low plasma beta; r/a<0.5)
- What is the effect of ITG on electron heat transport? (work in progress)
Ti,0 clamping is caused by strong increase in ITG turbulence as Te/Ti is increased; in ECRH plasmas the drive (electron heating) enhances the turbulence.
- Increasing PECRH and density simultaneously such that Te/Ti ~ constant reduces clamping would be beneficial.
Predictive modelling of ITG driven transport (as in TGLF) is innacurate as quasi-linear models do not reproduce non-linear calculations (work in progress).
- Increasing Te/Ti shows a larger disparity between linear and nonlinear simulations
- The apparent critical gradient for ITG driven turbulence is larger for nonlinear than linear calculations (Dimits shift)

## Slide 28: Synthetic modelling of energy exchange and its saturation
Use truncated Gaussian profiles
ne = 7x1019 m-3, Ti = 1.5 keV
Te = 2-6 keV, Te=Ti where Te<Ti
pex saturates at Te ~ 4 keV
Qex continues to rise due to V increase
Best ion heating through energy exch. at Te ~ 3-4 keV (for Ti = 1.5 keV!).
(No benefit from additional e-heating)
ne scan shows that at ne ~ 1.5x1019m-3 the ion heat flux is ~5MW at r/a ~ 0.3

## Slide 29: (2) Can we reduce the stiffness further? Optimise configuration!
Nonlinear gyrokinetic simulations (GENE)
Adiabatic electrons
W7-X Stellarator transport
electrostatic potential fluctuations
caused by ITG turbulence
Flux surface simulations, ITG radially local
Elongation enhances ITG drive
But reduces neoclassical transport …
[Xanthopoulos PRL 2014]

## Slide 30: (3) ITG supression: geometry affects the turbulence onset
ITG grows with a/LTi
TEM grows with a/Ln
No “Stability valley“
As no maximum-J property
Tokamak (positive shear)
ITG
TEM
[Alcusón,
Xanthopoulos et al
Plasma Phys.
Control. Fusion 2020]
Tokamak transport
W7-X standard configuration
Seen in pellet
experiments
ITG grows with a/LTi
TEM grows with a/Ln
“Stability valley“ when a/LTi ~ a/Ln
Thanks to maximum-J property
“Stability valley“
ITG
TEM
Stellarator transport

## Slide 31: Sharp transitions to turbulent heat transport are a general observation in fluids
S. Chandrasekhar, Hydrodynamic and Hydromagnetic Stability. Dover Pub., 1961
U. Stroth, PPCF 40 (1998)
Reproduced from Stroth (1998), adapted from Chandrasekhar (1961)
Onset of convection in a large tank heated from the bottom for a variety of neutral fluids (silicone oils, ethylene, glycol, heptane and water)
    Nu ~ Convection / Conduction
    Ra ~ Dimensionless temperature gradient
Critical gradients are a general characteristic of drift-wave driven turbulence and transport!

## Slide 32: Electron temperature fluctuations in W7-X are consistent with expectations from drift wave driven turbulence
2.5 cm
~6 cm
G.M. Weir et al., EPS (2016, 2017, 2018)
G.M. Weir et al., TTF (2018)
M. Hirsch et al., Proc. ECE/ECRH Workshop EPJ WoC 203 (2019)
U. Hoefel et al., Rev. Sci. Instrum. 90 (2019)
Z [m]
|B| [T]
R [m]
The "ZOOM" device is a 16-channel, high-resolution extension to the ECE diagnostic
Adapted for use as a CECE diagnostic during turbulence studies
Lr~7-9 mm
Lr~3-5
5-25 kHz
r/a

## Slide 33: Looking forward …
CECE
Looking past OP2:
Multi-dimensional plasma density / electron temperature fluctuation measurements are necessary in W7-X
Further development of microwave diagnostics
Near edge  driven turbulence
(<nT> cross phase and correlation reflectometry meas.)
Core region  driven turbulence
(multi-dimensional correlation radiometry meas.)
AEA21 Port Plug-in on W7-X
For OP2: A new CECE radiometry diagnostic

## Slide 34: Conclusions up to now:
The stiffness decreases with collisionality in W7-X (at low plasma beta); indicating stabilization of and/or transition to non- driven turbulence, with a stiffness 2: turbulence exists and is measurable in low-beta W7-X plasmas that is consistent with -TEM and ETG turbulence
Core electron temperature fluctuations are present in W7-X; further comparisons with modeling is necessary
~ 3-5 in the core of W7-X
The characteristics of the turbulent electron heat transport are dependent on the dominant instability
-TEM is thought dominant in the outer core region of W7-X (r/a>0.7)
-TEM/ETG appear to be dominant in the core of W7-X (at low plasma beta; r/a<0.5)
  Multi-dimensional (non-invasive) fluctuation measurements are necessary to develop an understanding of the spatial distribution of turbulence and its dependencies in stellarators

## Slide 35: Maximum-J, quasi-isodynamic configurations are resilient to collisionless Trapped Electron Modes
The neoclassical optimization of W7-X modifies the turbulent transport
Trapped particles sample on-average good curvature due to delocalization of trapping regions and bad curvature regions
High-mirror Configuration
Standard Configuration
High-iota Configuration
unstable
stable
Standard
High-iota
High-mirror
J.H.E. Proll et.al., PRL 108, 2012
G.G. Plunck, JW. Connor, P. Helander, J. Plasma Phys. 83, 2017
J.A. Alcusón et.al., PPCF, 2019.
Notes: Theoretically, the neoclassical optimization of W7-X modifies the turbulent transport in W7-X.
On the left I am showing the local magnetic field strength and curvature as a function of distance along a field line for three magnetic configurations in W7-X. The trapping regions for deeply trapped particles and bad curvature regions are delocalized in the High-mirror configuration, while they coincide for the standard and high-iota configurations. Another way of saying this is that the

## Slide 36: Maximum-J, quasi-isodynamic configurations are resilient to collisionless Trapped Electron Modes
The neoclassical optimization of W7-X modifies the turbulent transport
Trapped particles sample on-average good curvature due to delocalization of trapping regions and bad curvature regions
The maximum-J property of W7-X improves with plasma beta
High-mirror configuration
J.H.E. Proll et.al., PRL 108, 2012
G.G. Plunck, JW. Connor, P. Helander, J. Plasma Phys. 83, 2017
J.A. Alcusón et.al., PPCF, 2019.
High-mirror Configuration
Standard Configuration
High-iota Configuration
Notes: On the left I am showing the local magnetic field strength and curvature as a function of distance along a field line for three magnetic configurations in W7-X. The trapping regions for deeply trapped particles and bad curvature regions are delocalized in the High-mirror configuration, while they coincide for the standard and high-iota configurations. Another way of saying this is that the

## Slide 37: Turbulent transport in tokamak and stellarator
Tokamak: ITER Physics Basis 1998 (IPB98):
Stellarator: International Stellarator Scaling (ISS04)
Tokamak transport
Stellarator transport
Both scalings indicate gyroBohm transport due to microinstabilities
χGB~ T3/2
Tokamak:
> DNC
Stellarator:
> DNC
depending on T, eff

## Slide 38: Effect ot Te/Ti on profile stiffness in stellarators: W7-X
Non-linear calculations
Te/Ti
W7-X Stellarator transport
For Te/Ti = 1, no strong degree of stiffness
But Te/Ti exacerbates transport stiffness ~(Te/Ti)2
Non-linear  Linear
Increase of stiffness
W7-X
W7-X

## Slide 39
Ion profile stiffness and its mitigation
on ASDEX Upgrade

## Slide 40: ASDEX Upgrade TGLF simulations: ECRH deposition radius scan
Te
Simulation
Simulations with Trapped gyro-Landau-fluid model (TGLF) [Kinsey et al, Phys. Pl. 2008]
The model solves for the linear eigenmodes of ITG, ETG, TEM, TIM and KBM turbulence
Simple quasilinear saturation rule for eigenmodes. Benchmarked on Gyro and experiments
AUG Tokamak transport
PECRH = 5 MW
ECRH deposition
scan rdep/a= 0.1
and rdep/a = 0.75
index | r/a= 0.1 | r/a = 0.75
0% | 5 MW | 0 MW
25% | 3.75 | 1.25
50% | 2.5 | 2.5
75% | 1.25 | 3.75
100% | 0 | 5
(Tped = 500 eV
= constant)
Te
Simulation
(Tped = 500 eV
= constant)

## Slide 41: ASDEX Upgrade TGLF simulations: ECRH deposition radius scan
ion heatflux Qi
simulation
AUG Tokamak transport
Simulations with Trapped gyro-Landau-fluid model (TGLF) [Kinsey et al, Phys. Pl. 2008]
Te,0 varies widely, but Ti,0 saturates.
 Typical ITG behaviour where Increase of Te/Ti enhances turbulence and leads to “Ti-clamping“
Ti
Simulation

## Slide 42: Mitigating the effect of stiff profiles in tokamaks: pedestal versus core confinement
If pedestal is increased, the core follows suit
In H-mode plasmas the pedestal mostly sets the confinement for the “stiff“ core
In L-mode plasmas ion temperature clamping may occur
Fast ions may also mitigate the core transport stiffness
Total thermal pressure (βp)
pedestal normalised pressure (βp)
Core and pedestal strongly coupled
in a wide range of H-mode plasmas
Beurskens-NF-2013
Tokamak confinement
Tped/Tcore = constant
1/LT = constant
Tokamak transport

## Slide 43: Conclusions
Tokamaks and Stellarators:
Ti,0 clamping is caused by strong increase in ITG turbulence as Te/Ti is increased.
In ECRH plasmas the drive (electron heating) is enhancing the turbulence.
 Increase PECRH and density simultaneously such that Te/Ti ~ constant reduces clamping.
Tokamaks:
The stiff core confinement can be lifted by a pedestal as Pped/Pcore ~ constant in H-mode.
Predicitive core transport modelling possible as linear eigenmode propagation (TGLF) matches experiment.
Stellarators:
3D configuration can be optimised by e.g. reducing the elongation, to decrease stiffness further.
Density profile control such that ~ is enhanced can supress ITG sustainably?
Predictive modelling as in TGLF difficult as linear eigenmode propagation does not match non-linear calculations (work in progress).

## Slide 44: ETG modes can become important in W7-X where the drive for TE and ITG modes is reduced
Where = and =, the heat transport driven by TE and ITG modes is expected to dominate over that from ETG modes in stellarators
Configuration-Pech |  | 1.0 | 1.5 | 2.0
“Standard”-3.7 | [m2/s] | 0.7 | 0.5 | 0.4
“Standard”-2.0 | [m2/s] | 0.35 | 0.25 | 0.2
Configuration-Pech |  | 1.0 | 1.5 | 2.0
“Standard”-3.7 |  | 0.7 | 0.5 | 0.4
“Standard”-2.0 |  | 0.35 | 0.25 | 0.2
G.G. Plunk, P. Xanthopoulos, G.M. Weir et.al., PRL 122, 2019
Nonlinear gyrokinetic simulations (GENE)
Electrostatic simulations (=0) assuming adiabatic ions and kinetic electrons
Flux tube simulations, radially local, “standard” magnetic configuration at r/a=0.4
Setting = 3.6, = 0, = 0. Varying
F. Jenko et.al., Phys. Plasmas 7, 2000, F. Jenko et.al., PPCF 47, 2005,
P. Xanthopoulos et.al., Phys. Plasmas 16, 2009

## Slide 45: ETG modes can become important in W7-X where the drive for TE and ITG modes is reduced
Simulations
1.0
1.5
2.0
Te>Ti a/LTe>a/LTi
Te>Ti a/LTe>a/LTi
Configuration-Pech |  | 1.0 | 1.5 | 2.0
“Standard”-3.7 | [m2/s] | 0.7 | 0.5 | 0.4
“Standard”-2.0 | [m2/s] | 0.35 | 0.25 | 0.2
Configuration-Pech |  | 1.0 | 1.5 | 2.0
“Standard”-3.7 |  | 0.7 | 0.5 | 0.4
“Standard”-2.0 |  | 0.35 | 0.25 | 0.2
Nonlinear electrostatic (=0) gyrokinetic simulations (GENE)
Assuming adiabatic ions / kinetic electrons
Radially local flux tube simulations,
“standard” magnetic configuration (r/a=0.4)
Setting = 3.6, = 0, = 0. Varying
Standard / High-mirror
Standard / High-iota

## Slide 46: The stiffness trends downwards with increasing collisionality in W7-X
The TEM mode is stabilized by collisional detrapping; ITG/ETG modes are unaffected
The change in stiffness with collisionality is mostly due to a change in ( is approximately constant)
Standard
High-iota
High-mirror
(0.35<r/a<0.5)
G.M. Weir et al., Submitted to NF (2020)