## Slide 1: HydKin: brief introduction and perspectives
D. Borodin et al.

## Slide 2: EIRENE A&M reaction data base
Atomic processes:
mostly ADAS (including bundled states, MS etc.)
Molecular processes:
Books (latex): AMJuel, HydHel, H2Vibr, Methane
 EIRAM web interface (eirene.de) (V.Kotov)
Table data:
CxHy (HydKin?..), N2, NxHy, …
Accessible through HydKin
HYDKIN (eirene.de)
http://www.eirene.de/hydkin/
Closed by password for now…
One can test “pure A&M side“ decoupled from transport with high flexibility:
1D beam or constant plasma logic
Relaxation times
Sources/sinks and reservoirs are available

## Slide 3: Hydkin as solver
Master operator
Vector of species
Sources
Sinks
Arbitrary time, multiple timesteps
Any specie can be tracked or declared as “reservoir” with enforced density
Various output (, matrix of transitions, branching, to ERO, to EIRENE?..)
Some visualisation
Web-based interface (pearl)
http://www.eirene.de/U1_U4_JUEL-4229.pdf

## Slide 4
D.Reiter view on using HydKin
IAEA presentation (2013),
lectures etc.

## Slide 5: B.Küppers – work plan
Incorporate H2 Daten in HydKin
   (at first Mal AMJuel, H2Vibr other „old“ FZJ data)
Determine default cases (with checkboxes like by the HxCy family)
  a) H2 (most trivial case),
  b1, b2) H2 resolved by vibration levels (7 und 14 Levels, c)
  include MAR/MAD
Provide scalings for H2/D2/T2
  Physical basis should be provided by DB, FC etc
Put HydKin online (find solution for libraries issue)
Assist with EIRENE Webpages
   Details need to be defined…
Provide automatic reaction input for EIRENE from HydKin (classic + JSON)
Documentation and versioning of HydKin

## Slide 6: Yacora for H in different plasma regimes
Excitation of atomic hydrogen…
Huge number of free parameters  Evaluation needs a lot of time and experience
np
H
H+
H3+
H2
H-
recombination
dissociative
recombination
direct
excitation
mutual
neutralization
dissociative
excitation
dissociative
recombination
H2+
…in ionizing…
…and recombining plasmas
np
H
H+
H3+
H2
H-
recombination
dissociative
recombination
direct
excitation
mutual
neutralization
dissociative
excitation
dissociative
recombination
H2+
np
H
H+
H3+
H2
H-
recombination
dissociative
recombination
direct
excitation
mutual
neutralization
dissociative
excitation
dissociative
recombination
H2+
Yacora is alternative CRM for the hydrogen atom (under active development):
 In principle a complete set of input parameters, but some are based on simple assumptions.
Attached divertor plasma
Driver region of NBI sources
Detached divertor plasma
Expansion region of NBI sources
[D.Wünderlich and U.Fantz,
Atoms 2016, 4(4), 26]
Courtesy D.Wünderlich,
IPP-Garching
CMSS-2021, D.Borodin

## Slide 7
Yacora: inclusion of molecular source term
Stationary Yacora run vibrationally resolved:
Particle species
Reactions
H2 source term
proton impact
electron impact
vibrational transitions
electron impact
At low Te<10eV proton impact and vibrational transitions dominate

## Slide 8
source= 1021 m-3s-1
Yacora: inclusion molecular source term
Stationary Yacora run vibrationally resolved:
results
small temperature (T<5eV):
density peak
main reactions: vibrational excitation and proton impact

## Slide 9: Assessment of the available A&M data bases
H2VIBR rates do not include all the CR processes considered in AMJUEL; also particular rates are different
transport-free Eirene simulations agree with YACORA
60% of reduction attributed to difference in rates  remaining difference due to transport of vibrationally excited states
Up to 40% reduction in effective dissociation rate due to transport of vibrational states
Effects cannot be directly assessed due to differences in the H2VIBR and AMJUEL rates
 Full scale H2 CR model inside EIRENE?..
Andreas Holm,
M.Groth, et al.,
PET 2021,
CPP 2021

## Slide 10
ADAS’96 data for H/D/T spectroscopy

## Slide 11: 3D-integration of line intensities for 2D cameras in ERO2.0:
Improved synthetic diagnostics are necessary e.g. for DEMO
Brightness is conserved in geometrical optics! So, one can integrate the cells.
Toroidal rotation of 2D SOLPS-ITER simulations in 3D tokamak context needed!
Plasma near VT
VT surface

## Slide 12: Ideas for improvement of EIRENE CRMs
Rethinking data formats
  Use new ADAS “mdf” formats?..
  Use YACORA formats?..
  Use original CCC, RMPS etc. data
  Sustain reproducibility for fitting formulae data
  Go to linearly (log, spline, poly, …) tab data? ASCII or BINARY (e.g. HDF5)?
  We need flexible (XML, JSON?...) master files for any data collection
Rethinking data input
  We need well-readable reaction lines.
  Input by vibrational and rotational states should be semi-automatic.
  Transition matrix generation should be automatic.
  We need back-compatibility with old EIRENE input files
  Input for EIRENE and postprocessor should be the same!
Which postprocessor?..
  YACORA, EIRENE (“eirene –pp”), HYDKIN (perl + web)?
  We need to treat sinks and sources, particle velocity distributions (1D beam), define “reservoirs” as HydKin solver provides
  We need synthetic diagnostics to validate the code/data with spectroscopy and bolometry
Probably we need to combine all options in a single CRM

## Slide 13
How we can organize EIRENE-YACORA interaction?
YACORA can provide the data for the EIRENE main loop directly
  Some development will be needed on YACORA side. FZJ should be contributing to this programming.
  Partially it can be done as post processing tools (easy part to agree).
  Some data critical for EIRENE may be missing in YACORA. EIRENE may need additional flexibility. If YACORA is the only/primary way of using A&M data, FZJ should be able to do such development by the own team.
YACORA provides just the data, EIRENE keeps (rather develops…) its own data structure
  How do we properly acknowledge YACORA effort on compilation and validation of the data?
  We still need to agree on formals, wrappers etc.
We just consult with each other on the data sources, do some code-code validation etc.
  I would wish a stronger cooperation!..
  We can take a good example and start over with it including understanding missing functionality on both sides
We use external platforms and experinece
  ADAS EU „mdf“ files, IAEA GNAMPP, D.Tskhakaya (IPP CR), BIT1/BIT2 codes.
This is just a list of possible ways to go. Obviously, the cooperation should go in mutual interest, fully voluntarily, adequate to available resources and well-fitting to plans and obligations of all sides!

## Slide 14
Thanks for the attention!
 2 more slides on CXN...

## Slide 15
CXN in EIRENE: W erosion in JET divertor
Diagnostic optimised scenario “M18-18”
Fusion performance scenario “M18-02”
“M18-02”
“M18-18”
CXN
CXN
CXN
CXN
CXN
CXN
CXN flux routinely extractable from EIRENE simulations (just post processing of the output).
Use and importance of the CXN fluxes by ERO2.0 demonstrated for both Be and W erosion in JET-ILW and ITER.
CX reactions take considerable fraction of EIRENE performance, however FKH and parallelization allows large speed-up for simulations at ITER and DEMO scale.
H.Kumpulainen, M.Groth, et al., PFMC-2021, NME paper in press

## Slide 16: CXN and direct plasma impact fluxes in ITER
Courtesy J.Romazanov,
DPG-2021, NF-2022 paper
SOLPS+OEDGE  ERO2.0
Be self-sputtering is also of importance!

## Slide 17
Thanks for the attention!