## Slide 1: Gas fueling hardware overview
Thierry Kremeyer1, C.P. Dhard1, P. Drews3, E. Flom2, G. Fuchert1, M. Jakubowski1, M. Krychowiak1, E. Wang1, V. Winters1
Email: thierry.kremeyer@ipp.mpg.de
1Max Planck Inst. for Plasma Physics, 17491 Greifswald, Germany
2University of Wisconsin - Madison, Madison, WI 53706, USA
3Forschungszentrum Jülich GmbH, IEK–Plasmaphysik, 52425 Jülich, Germany

## Slide 2: Fueling
Gas injection Pellets NBI
Divertor gas system HFS vs LFS with blower gun Link to TG Fast ion
Main gas system (HFS) OP2.1 steady state only LFS
MPM gas system (LFS)
Gas puff imaging (LFS)
ICRH gas system (LFS)

## Slide 3: Gas Fueling – OP1.2
Main Gas System - 5 AEZ ports (each module) + AEO30
  H, He, N, Ar, Ne, Diboran
  H flow: max. 2.4E+22 a/s
  Prefill, Nozzle far away from plasma – feedback control overreaction
Divertor Gas System - 5 Nozzles in AEH30 + AEH51
  5 Nozzles in AEH30 + AEH51
  Succesfull feedback control
  Fueling efficiency sensitive to nozzle location
  Evidence for island/edge transparency at high frad
Nozzle
5 4 3 2 1
 | Valve 5 | Valve 4 | Valve 3 | Valve 2 | Valve 1 | Main
Mean | 0.12 | 0.22 | 0.31 | 0.44 | Broken | 0.28
SD | 0.01 | 0.07 | 0.04 |  |  | 0.09
Injections | 6 | 15 | 8 | 1 |  | 7
frad | 0.17-0.22 | 0.16-0.31 | 0.16-.024 | 0.2 |  | 

## Slide 4: Gas Fueling – OP2.1 New hardware
Divertor Gas System extension
  H flow: 8E+19 a/s – (OP1.2 3.6E+22 a/s) – OP2.1 2.3E+23 a/s
  5 Nozzles in AEH30, AEH50, AEH51. 1 Nozzle (Nozzle 3) in all other divertor modules
  Feedback on: Interferometer, NGM, Divertorbolometer, WDia, Targettemperature
MPM with piezo head
  H flow: ~3 E+20 a/s
  Fast piezo valve with FZJ-GAS2 head from AEK40
  Variable distance to LCFS, 1 Gas type a day
Gas puff imaging
  H flow: 2E+20 a/s – 6.E+20 a/s, supersonic (~Mach 1.1)
  H and He from AEK50
  Collimated, but no sharp puffs (~2E+20 atoms leak after valve closing)
ICRH gas system (1-CCD-T0005.2)
  H flow: 2.9E+18 – 2.4E+20 a/s
  H, D, He from AEE31
  10 Hz with minimum pulse of 10 ms on and 90 ms off
Gas puff imaging

## Slide 5: Gas Fueling – OP2.1 Physics
Neutral penetration
  What physics dominate - Density along flight path? Accelerated by CX? Ionization in island with strong diffusion?
  Fueling location (Divertor vs. HFS vs. LFS)
  Island topology (Icc or valve location or planar coils) Toroidal and Up/Down assymetries
  Different gas flows (low and very high) - Tunneling with high fluxes?
  Control Core vs SOL fueling
  Ne, N, Ar – impurities
  He as recycling proxy, neutral He penetration
Recycling
  Gas injection as proxy for recycling neutrals
  Divertor vs HFS wall vs LFS wall
Ionization source in SOL
  Where do particles ionize in the SOL
  Link to SOL transport