## Slide 1: Proposals OP2.1: characterization of the cryo pump and pumping efficiency

## Slide 2: Proposals
3 proposals related to the pumping efficiency and the characterization of the cryo pump
Contributors: V. Haak, CP Dhard, D. Naujoks, V. Rohde (IPP), S. Varoutis, C. Tantos (KIT), G. Motojima, S. Mazusaki (NIFS)
Characterization of the cryo vacuum pump during commissioning
Pressure variation at low iota and high iota side pumping gaps and estimation of pumping efficiency at AEH and AEP ports (with/without CVP)
Characterization of the cryo vacuum pump during plasma operation (3 parts)
- characterization of the CVP during plasma operation in steady state attached discharges (CP)
- characterization of the CVP during plasma operation in steady state detached discharges (CP)
- characterization of the CVP during plasma operation in transition to detachement

## Slide 3: 1. Characterization of the cryo vacuum pump during commissioning
Goals
verify/study parameters for the operation and regeneration of the CVP
estimate the pumping speed of the CVP (every individual unit and all 10 units together)
measure the amount of pumped hydrogen
verify results from the DIVGAS and ANSYS simulations

## Slide 4: 1. Characterization of the cryo vacuum pump during commissioning
Approach
Cool down and stabilize the CVP
Close the valves to the PV pumping system
Inject hydrogen (less than 0.2bar*m^3; the explosive limit is at 2.2bar*m^3) and keep the pressure in the plasma vessel constant at 1*10e-03 mbar. The actual amount of hydrogen to be injected has to be determined according to the H2 dilution capabilities at plasma vessel vacuum system.
Regenerate all CVP together to 30K according to the predefined procedure
Once the PV pressure stabilizes then start the procedures for pumping down the plasma vessel to ca. 1*10^-7 mbar
Then, the whole process is repeated ten times for each individual cryo pump unit. This unit is cooled down, <0.01bar*m^3 H2 is injected and the cryo pump is regenerated afterwards. Pumping down the plasma vessel could be avoided until all the ten CVP are tested one by one.
Once all the CVP are tested, the PV has to be pumped down to ca. 1*10^-7 mbar. CVP could be warmed-up to ambient temperatures.
Victoria Haak

## Slide 5: 1. Characterization of the cryo vacuum pump during commissioning
Requirements
Gas injection
Neutral gas pressure measurements in the plasma vessel + QMS measurements
Victoria Haak

## Slide 6: 2. Pumping efficiency at the AEH and AEP port
Goals
Study the pumping efficiency at the different ports (AEH and AEP)
Study the pumping efficiency at the AEP port with respect to the new collars
Study the pumping efficiency of the TMPs with active cryo pumping
Compare the pumping speed to the results from OP1.2b
Provide values of the pumping speed as an input for the simulations

## Slide 7: 2. Pumping efficiency at the AEH and AEP port
Approach
Repeat selected shots from OP1.2b (in standard and high iota configuration) with and without the cryo pump ( 2+2 shots)
Repeat shots from the proposals concerning the characterization of the CVP during plasma operation in standard and high iota configuration ( 5+5 shots, ca. 10s each)
Requirements
pressure measurements in the plasma vessel and subdivertor
gas injection
QMS/DRGA measurements
Standard configuration EIM005+2520/ High iota configuration FTM004+2520 (7+7 shots)
Heating and density control; values to be specified

## Slide 8: 3. Characterization of the cryo vacuum pump during plasma operation in transition to detachment
Goals
Study the pumping speed of all 10 CVP together during plasma operation in different magnetic configurations
Provide input/ compare to results from the simulations
Compare the pumping speed in transition to detachment to the pumping speed in steady state attached and detached discharges (see related proposals)

## Slide 9: 3. Characterization of the cryo vacuum pump during plasma operation in transition to detachment
Approach
CVP is regenerated and cooled down
Repeat a predefined shot (according to the two related proposals) five times
All valves to the TMPs are open
All valves closed
One valve of the pumping port on the low iota side (AEH) closed, the other two (AEH and AEP open)
Both valves of the pumping port on the low iota side (AEH) closed, the valve at AEP open
Both valves of the pumping port on the low iota side (AEH) open, the valve at AEP (pumping port on the high iota side) closed
Repeat these five shots without the cryo pump
10 shots in total for one magnetic configuration

## Slide 10: 3. Characterization of the cryo vacuum pump during plasma operation in transition to detachment
Requirements
Neutral gas pressure measurements in the PV and subdivertor
Gas injection (hydrogen fueling)
QMS/DRGA measurements
20 shots (10 in standard configuration (5 with and 5 without cryo pump) and 10 in high iota configuration)
5MW ECRH heating
5e19m^-3 density feedback control