## Slide 1: Proposal ideas on fast electrons in the edge
C. Killer for TG Scenario, 21.02.2022

## Slide 2: Recap: indications for electron population far outside the SOL
hot spots on walls, probes, … (at positions that are not expected to receive heat loads)
negative floating potentials seen by probes (where it should be zero, since n=0)
occurring in pure ECRH plasmas with PECRH/ndl > 1 (for PECRH in MW and ndl in 1019m-2)
relevance to TF 1: Exploration of heating scenarios using upgraded plasma heating capabilities
  Exhaustive operational map of the W7-X configuration space incl. operation limits
  Demonstration of safe operation of heating systems
see also:
  Physics meeting 20.11.2019
  TG scenario 16.03.2020, 21.09.2020
[video: Aleix Puig Sitjes]
20181002.46

## Slide 3: some more obversations
hot spots in low density plasmas depending on magnetic configuration
stationary “stripes” on MPM  presumably by electron population tied to rational surface
EJM
KJM

## Slide 4: Relevance for OP2
TF I: Exploration of heating scenarios using upgraded plasma heating capabilities
  Exhaustive operational map of the W7-X configuration space incl. operation limits
  Demonstration of safe operation of heating systems
ECRH power has increased from OP1 and will increase further
  does the PECRH/ndl > 1 existence regime transfer to higher power? Hopefully not…  map out operational space (in heating power, density, potentially ECRH details (choice/settings of gyrotrons))
acceleration mechanism
  candidate: Parametric Decay Instability. First observations in OP1.2b, experiments with upgraded diagnostic planned [Moseev+DTU]
  parallel electric fields (similar to tokamak runaway mechanism) can transiently appear in edge due to current distribution, but no candidate for plasma in equilibrium [Aleynikov]
fundamental understanding of fast particle losses
  experimentally observed fast electron losses as validation for ASCOT, BEAMS3D
  (in some configurations (e.g. KJM), MPM data indicates ion losses in pure ECRH plasmas)

## Slide 5: Proposals for OP2.1/2.2
piggyback survey using MPM whenever electric probes are operated
  look for fast particle signatures outside the SOL whenever electric probes are operated (see caki_007 in OP1.2b)
  in addition have an eye on pop-up divertor probes (although these only cover a much smaller spatial area)
use MPM and video cameras in PECRH, n operational space
  if this is caused by PDI, SOL density profiles are important  study variations of SOL density profile while keeping ndl constant.
  PDI group is preparing dedicated proposals (TG Heating?)  perhaps attach MPM operation to those proposals
  in OP1.2b, worst scenario was in reversed field. Coincidence?  Carefully check reversed field experiments
  inject pellets / Tespel in fast electron scenario  increased ablation (seen in TJ-II)
new electron probe for measurement of non-thermal electron currents (FZJ/EAST)
  shielding ions (small aperture, electrical bias)  only sensitive to electrons
  resolves direction along/against field (indications for preferred directionality of electrons in OP1.2)
  presentation later today (TG Edge/Divertor, 21.02.2022 15.30)