## Slide 1: Effects of SOL drifts on sheathdrop and plasma potential
A Pandey, C Killer, Valeria Perseo, Matt Kriete, Yu Gao, M Endler

## Slide 2: Effects of SOL drifts on sheathdrop and SOL currents
Objectives:
how the drifts can affect sheath potential drop and plasma potential above the divertor in standard configuration.
would also relate to the effect of drifts on the heat flux deposition on the divertors through the sheath transmission factor.
Approach:
Correction of error fields
Measure the floating potential and plasma parameters through divertor LP
Calculate : plasma potential, sheathdrop, heat flux through the sheath
Compare for forward and reversed field cases
The plasma potential calculated may serve as input to the MPM mach probes for comparison
Specific requirements:
  Forward and Reversed field
  Diagnostics : Divertor Langmuir Probes, MPM with Mach probes, CIS, Divertor IR Cameras
Can be combined with:
  Detachment discharges with Forward and reversed field
  Up/Down asymmetry proposals
  SOL drift proposal
Task Force(s) | I, II, III
Mag. Configurations | EJM
No. of programs | --
Requested Parameters | 
Heating [MW] (ECRH, NBI, ICRH) | Low and high edge densities

## Slide 3: CIS measurements showing uni-directional flow over most of image at low density are consistent with direction of binormal drift
CIS forward model
stagnation point
Stagnation point shifts in direction of → now counter-clockwise throughout most of island
island has left-handed helicity: counter-clockwise around island → counter-clockwise around torus (positive flow)
points toward island O-point due to decreasing toward O-point
Forward field: counter-clockwise (positive) around torus
clockwise around island
CIS measurements
Forward field drift direction
CIS image at low density is largely red ( counter-clockwise), consistent with prediction
CIS forward model does not capture many details, likely due to very simple emission assumption (uniform throughout SOL)

## Slide 4: Quick refresher
Floating potential :
  unbiased (floating) surface exposed to the plasma gets charged to floating potential
  Electron current = ion current  No net current
  Negative with respect to the plasma potential
  Usually negative with respect to the ground
  Ground  0 V
Floating Potential

## Slide 5: Measured Floating potential in low iota and standard (F/R)

## Slide 6: Measured Floating potential in low iota and standard (F/R)

## Slide 7: Measured Floating potential in low iota and standard (F/R)
The sheathdrop is computed on the divertor probes using the analytical model given in Phys. Plasmas 26, 013507 (2019)

## Slide 8: Measured Floating potential in low iota and standard (F/R)
The sheathdrop is computed on the divertor probes using the analytical model given in Phys. Plasmas 26, 013507 (2019

## Slide 9: Measured Floating potential in low iota and standard (F/R)

## Slide 10: Measured Floating potential in low iota and standard (F/R)

## Slide 11: Magnetic field incidence angle on the divertor
Magnetic configuration | at surface near Probe 1 | at surface near Probe 2 | at surface near Probe 3 | at surface near Probe 4 | at surface near Probe 5 | at surface near Probe 6 | at surface near Probe 7 | at surface near Probe 8 | at surface near Probe 9 | at surface near Probe 10
Standard | -1.40 | -1.10 | -0.80 | -0.50 | -0.20 | 0.50 | 0.80 | 10 | 1.20 | 1.40
Low Iota | 0.20 | 0.40 | 0.70 | 10 | 1.20 | 1.90 | 2.10 | 2.30 | 2.50 | 2.70
Magnetic configuration |  |  |  |  |  |  |  |  |  | 
Standard | -1.40 | -1.10 | -0.80 | -0.50 | -0.20 | 0.50 | 0.80 | 10 | 1.20 | 1.40
Low Iota | 0.20 | 0.40 | 0.70 | 10 | 1.20 | 1.90 | 2.10 | 2.30 | 2.50 | 2.70