## Slide 1: WPSA Code Management & Simulation 2022 plans
WPSA Code Management & Simulation Area Coordinator:
G. Falchetto CEA, IRFM (France)
WPSA General Meeting, 4-6 May 2022

## Slide 2: OUTLINE
WPSA Code Management and Simulation strategy
WPSA CM ACTIVITIES 2021-22
WPSA CM Tasks & Deliverables 2022
Agenda

## Slide 3: WPSA Code Management and Modelling area strategy
Establish reliable modelling codes, workflows and operation related tools for routine use in JT-60SA scientific exploitation
Modelling support to the enhancements and diagnostics procured by EU
Specific focus on modelling the Initial Research Phase
+ contribute to Integrated Research Phase wall diagnostics design (F4E/WPDIV)
Updated Project Phases BA SC 29

## Slide 4: EUROfusion WPSA code management and modelling activities 2021-2022
Operation oriented tools and synthetic diagnostics :
      Discharge simulator development
      Breakdown simulator development & optimization of BD scenarios
      Electron Cyclotron Wall Conditioning ECWC simulation tools validation
      Visible imaging analysis tools provision (camera tomography, EDICAM)
      Integrated Data Analysis tools requirement capture
      Proposal for disruption mitigation/avoidance trigger
      Assessment of PCI measurement
      FILD synthetic diagnostics
Modelling for JT-60SA Initial Research Phase scenarios
    Scenario modelling with operationally oriented integrated modelling transport codes
    Edge and divertor modelling (C scenarios + wall diagnostics design support)
    Energetic Particle stability analysis
    MHD stability analysis
    RWM control
    Non-linear MHD modelling of pellet triggered ELMs
    Runaway electron heat loads on PFC
    Disruption modelling tools ready for validation
new
new
Coordinate with
Experiment Team
Topical Group Leaders
Notes: The ongoing tasks under the “code management and modelling” area coordinated by Gloria Falchetto within EU project WPSA aiming at supporting JT-60SA scientific exploitation were presented.
On the one side, the development of operation related simulation tools such as the discharge simulator: first METIS CREATE-NL strong coupling has been achieved, although unstable in transient phases, hence an improved coupling method between FBE-transport codes (NICE/METIS) is being implemented.
On the other hand, ongoing modelling focused at addressing initial research phase scenarios: successful Scenario 2 ramp-up modelling with JINTRAC; SOLPS-ITER grid sensitivity study in pure D case assessing suitable reference resolution for benchmarking with SONIC; gyrokinetic Energetic Particle stability analysis (LIGKA) aiming at automated application of the EP workflow to the assessment of EP-stability in ramp-up and steady-state plasmas; non-linear MHD modelling of pellet triggered ELMS (JOREK) in Scenario 4 with reduced pedestal pressure (40kPa); computations preparing for validation of disruption modelling tools (CARMA0NL-CARIDDI) on JT-60SA mechanical data; and, finally, newly started task on simulations of energy deposited by runaway electrons (FLUKA) on PFC.

## Slide 5: WPSA.CM Modelling Tasks 2022
TOPIC | Deliverable 2022 | Del Owner
Scenario development transport analysis | Integrated modelling of ramp-up of initial research phase scenarios with first principles transport models | L Garzotti D Taylor et al (UKAEA) P Strand D Yadikin E Fransson (VR) P Huynh (CEA)
MHD and control | MHD stability chain deployed to users | R Coelho (IST)
 | Application of CarMa-D model in state-space representation for developing RWM control time simulation and test controller concepts | L Pigatto et al (ENEA RXF)
 | Validation of disruption modelling tools (CarMa0NL-CARIDDI) on first JT-60SA mechanical data | F Villone et al (ENEA CREATE)
 | Estimate of heat load levels and distributions caused by REs via a workflow coupling particle tracing codes to FLUKA. | J Caloud A Casolari E Macusova (IPP.CR)
Pedestal and edge | Report/publication on (JOREK) modelling of multiple pellet injection in self-consistently evolving pedestal profile | S Futatani (CIEMAT UPC)
Energetic Particle modelling | Demonstration of automated application of the EP workflow to the assessment of EP-stability in ramp-up and steady state plasmas. | Ph Lauber (IPP-Garching)
 | Provide ASCOT distribution function for beam ions | A Snicker (VTT)
 | Analysis of linear AE stability of initial research phase (H,D) scenarios | R Coelho (IST)

## Slide 6: WPSA.CM Modelling Tasks 2022
TOPIC | Deliverable 2022 | Del Owner
Edge and divertor modeling | Sensitivity study of low n /current drive scenarios with C divertor, with SOLEDGE3X edge transport code, including impurity seeding impact | G Falchetto K Galazka (CEA)
 | Assessment of JT-60SA Initial research phase II scenario 2 via edge/divertor modelling integrated with core conditions (SOLEDGE) | L Balbinot (ENEA)
 | Modelling of C wall Scenario 2 with SOLPS-ITER. | P Chmielewski (IPPLM)
 | Report on the benchmark of SOLPS_ITER to SONIC. | G Rubino D Coster (ENEA, IPP)

## Slide 7: WPSA.CM Operation related Tasks 2022
TOPIC | Deliverable 2022 | Del Owner / Team
 | Plasma operation oriented tools | 
Plasma discharge simulator | Verified JT-60SA pulse simulator including implementation of current, gaps and vertical stabilization controllers | E. Joffrin JF Artaud G Giruzzi C Boulbe B Faugeras (CEA, Univ Nice) M Mattei D Frattolillo et al (ENEA CREATE)
 | Provision of discharge simulator select test cases | William Bin G Giruzzi (ENEA CNR Mi, CEA)
ECWC modelling | Report on the validation of ECWC code (TOMATOR-1D) on the first data from JT-60SA Integrated Commissioning | J Buermans (LPP-ERM-KMS)
Breakdown modelling | Documentation on runs on JT-60SA breakdown using a nonlinear optimization technique. | Daria Ricci L Figini M Mattei (CNR Mi, ENEA CREATE)
Integrated Data Analysis | Plan for the implementation of IDAV for JT-60SA scientific exploitation | R Fischer D Stieglitz (IPP Garching)
Disruption trigger | Proposal for building parsimonious disruption mitigation/avoidance triggers | Jesùs Vega (CIEMAT) M Gelfusa A Murari R Rossi T Cracinescu (ENEA, IAP) F Bairaktaris A Papadopulos (NCSRD)

## Slide 8
TOPIC | Deliverable 2022 | Del Owner / Team
 | Synthetic diagnostics development | 
Turbulent transport | Assessment of the JT-60SA PCI diagnostics measurement, on relevant high-beta gyrokinetic turbulence including fast ions | A Iantchenko (EPFL)
Visible imaging | Feasibility study of tomographic inversion for characterizing runaways in plasma conditions relevant for JT-60SA | J Cavalier J Svoboda (IPP.CR)
 | Improved EDICAM visualization tools | T Szepesi et al (EK)
FILD | Optimization of FILD detector head geometry using synthetic diagnostics | M Garcia-Munoz et al (CIEMAT Univ Sevilla)
new
WPSA.CM Synthetic diagnostics Tasks 2022

## Slide 9: WPSA CM - Modelling session
Today 14h - 17h30 S1-3: Initial research phase modelling
Edge/divertor
MHD control
pedestal
stability
Fast particles
Operation regime development
EEG
WPDIV

## Slide 10: WPSA CM - support to operation & diagnostics
Tomorrow Thu 5th
Operation related tool development : Integrated Data Analysis
15h30 – 16h30 Modelling in support to diagnostics
Divertor
WPDIV
Fast particles
Transport

## Slide 11: WPSA CM - support to IC and operation
Friday 6th 10h30 – 12h30 S3-2 Integrated Commissioning Relevant Operation related tool development and modelling
MHD:
Runaway
Disruptions
IC

## Slide 12: THIS MEETING: SCIENTIFIC DISCUSSION
Expected contents of the presentations/discussions:
scientific discussion on the status of the tasks
development plan
needs of input data
publication plan
coordination with QST and experiment team
Progress towards the deployment of
validated modelling and analysis tools
for operation and scientific exploitation