## Slide 1: Simulations of the Initial Research Phase II scenarios withSOLEDGE2D/SOLEDGE3X-EIRENE
K. Gałązka1,2, L. Balbinot3, G. Ciraolo1, G. Falchetto1 and P. Innocente4
1) CEA, Cadarache, FRANCE
2) IPPiLM, Warszawa, POLAND
3) Università della Tuscia, Viterbo, ITALY
4) Consorzio RFX, Padova, ITALY

## Slide 2: Aims of edge/SOL modelling
Assess the heat loads on the wall and targets (check also the neutrals loads)
Predict the onset of detachment
Propose a seeding strategy to mitigate heat loads
Contribute to the design studies of divertor / wall diagnostics (ENH session tomorrow)
Requirements:
Reliable magnetic equilibrium (including divertor legs) and wall data (chamber + subdivertor)
Machine Data : puffing valve positions and available gases, auxiliary heating power
Power and particle flux through the inner simulation boundary
Reliable prediction of transport based on
  Experimental findings and previous simulations from C-wall JET
  Estimations from core and pedestal modelling
  Existing scalings
Experience from core modelling welcome!
SA-SE.CM.M.03-T003 | D1- Sensitivity study of low n /current drive scenarios with C divertor, with SOLEDGE3X edge transport code, including impurity seeding impact.
 | D2 - Assessment of JT-60SA Initial research phase II scenario 2 via edge modelling integrated with core conditions.
No active cooling in the Initial Research Phase - power exhaust mitigation is crucial

## Slide 3: Scenario #2 constraints from the RP / PID
D plasma
Uncooled C wall
Maximum heating power: 19/26.5/33 MW (from PID: 27 MW)
Core density: 5.6×1019 m-3
Estimation of power loads for the reduced power case:
Expected input power to SOL: 20-23 MW
H-mode operation (PSOL > 10 MW)
SOL width < 1.5 mm
Maximum particle source at core boundary: Sn = 2.5×1021 s-1 (NBI)
Deuterium puff range: ΓD = [0, 1.8 × 1023] s-1
Maximum pumping speed: 100 m3/s
Sn = 1.0×1021 s-1
ΓD = 1.0×1022 s-1
2 pumping surfaces with albedo 0.95
D fuelling valve position
(another one in the chamber top)
Pumping surfaces
Subdivertor currently
not modelled
MAX 5MW
MAX 13MW

## Slide 4: Construction of the grid
SOLEDGE2D-EIRENE grids
used in the past simluations
SOLEDGE3X-EIRENE grids
„New” grid incorporates the secondary X-point amid the volume at the top of the chamber.
Adjusted the details of the wall.
Equilibrium from the IDM repository.

## Slide 5: Modeling parameters & status of work
Auxiliary input power scan: [15, 17.5, 20. 22.5, 25] MW (50/50 electrons/ions)
Particle sources: Score= 2.5×1021/s, ΓD = 1.0×1021 s-1, pump albedo 0.95
Electron density at the seaparatrix should be ~ 2×1019 m-3
Transport coefficient profiles (for the H-mode)
Starting from pure D
Sputtering for C
Gas puff of Ar/Ne impuritues
Power scan completed for pure D, L-mode
Power scan started for pure D, H-mode
Pending:
Power scan with C impurity, H-mode
Power scan with seeded impurity, H-mode
Subdivertor modeling

## Slide 6: Publication plan
EPS conference:
  K. Galazka et al. "SOL modelling of the JT-60SA tokamak initial operational scenario using SOLEDGE3X-EIRENE code" (contributed poster)
AAPPS-DPP2022 conference:
  K. Galazka et al. "Particle transport and heat loads in JT-60SA studied by SOLEDGE3X-EIRENE code." (not decided)
Draft to be sent to Nucl. Mat. and Energy:
  L. Balbinot et al. (previous work)