## Slide 1: WPSA General Meeting - FP9 Enhancements: EC Stray Detection System
A. Moro, L. Figini, S. Garavaglia (ISTP - CNR) C. Piccinni (IPP - Garching)
with contribution from WPSA (C. Sozzi, J. Ayllon) and IO (A. Sirinelli, G. Vayakis)

## Slide 2: Scientific Objectives and Task Description
Madrid
Napoli
Padova
Milano
Design and procurement of EC Stray Detection diagnostic for JT-60SA including the preparation of a proposal to be considered by QST-F4E-EUROFusion.
Adaptation of the ITER bolometer to JT-60SA will be explored.

## Slide 3: Tasks activities
Madrid
Napoli
Padova
Milano
EC Beam tracing analysis Analysis considering IC and final antenna configuration - System requirements
In vessel ECH sensor study IO-F4E-EUROfusion-QST Collaboration Agreemeent
Engineering integration study Selection of in-vessel locations for sensor: - strong QST involvement (dedicated meetings, next one May 19th) - proposal for sensor allocation and interfaces (e.g. cabling and support) definition
Prototyping, basic sensor testing, calibration and commissioning plans coatings characterization and measurements tests on (adapted) ITER bolometer (TBC after 2.), diagnostic qualification proposal

## Slide 4: ECH Sensor System for ITER
Madrid
Napoli
Padova
Milano
Specification | Symbol | Value
Overall Sensor volume | V | 61.4x31x16 mm3
Sensor weight | m | 170 g
Temperature range | DT | [100-816 ℃]
Transient sensitivity | dDT/dt/p | 1.93 10-5 K m2/J
Steady state sensitivity | dDT/dt/p | 5.65 10-4 K m2/J
Power resolution | Pstep | 100 kW (optimized to 20 kW)
Thermal response |  | 1 K/s
Response time | t | 1.3 s (optimized to 0.3s)
Accuracy | DPden | 375 kW/m2 (optimized to 120 kW/m2)
Signal amplitude | DV | ~ few mV [0-10 mV]
DV between hot and cold bolometer
DV ➠ DT ➠ ECH power
Thermal model (i nodes)
Algorithm for Ti(t)
Extensive design studies, prototyping, FDR stage (IO, Bertin Technologies)
10 prototypes – 2 for JT-60SA
2 cylinders, ∅ 4mm
N. Masseen et al., “Microwave Detector design for ITER”, ITER_D_JR2KH6
A. Sirinelli, “System Design Description (DDD) 55.GB In-vessel ECH Detectors”, ITER_D_V2GEA7 v1.0
A. Sirinelli, “55.GB - ECH sensor AMESIM model”, ITER_D_5PRGQM
D𝐕 = (𝑺𝑨 − 𝑺𝑪)(𝑻𝟐 − 𝑻𝟏)

## Slide 5: Collaboration under IO-F4E-EUROfusion-QST
Madrid
Napoli
Padova
Milano
Coating R&D at ITER (Development and qualification):
• ECH coating is the most critical parameter for the performance of the sensor
• The absorption efficiency @ 170 GHz required to be compliant with the performances is 80%.
• The development of this electro-magnetic absorbing coating consists in defining the coating composition, the substrate preparation and the deposition process and measure its absorption performances
Courtesy of A. Sirinelli and Bertin Technology

## Slide 6: Ceramic coating measurements at ISTP-CNR lab
Milano
Ceramic coating samples measurements at ISTP-CNR lab
20 samples: Ti2O3 (5), Cr2O3 (8), Al2O3Ti2O3 (7) with different coating thickness
2 frequency bands to cover the 70-220 GHz range
2 launched polarizations (E-plane, H-plane)
13 incidence angles (15-70 deg)
determine material properties (ε, tan δ) and mm-wave fractional power loss
provide adapted coated cylinder (optimal coating & thickness, covering largest freq. range)
Madrid
Napoli
Padova
H-plane
E-plane

## Slide 7: In-vessel sensor integration (in progress)
Madrid
Napoli
Padova
Milano
ECH layout during EP:
Steerable launchers, P8 & P11
Integration considers:
Preferred option: 2 sensors close to ECH (LFS)
no direct illumination
stabilizing plate
in the shadow of the tiles
Alternative option: inside other ports, (P10 equ, P18, still under investigation)
2nd reflection (with support of beam tracing analysis for expected Pden)

## Slide 8: Conclusions
Status of the task
  Engineering integration of ‘adapted’ ITER bolometer
  Coordination with QST
Schedule proposed requires IO feedback (‘weak’ point):
  shipping of prototypes
  FDR outcomes (to define dedicated tests)
  sensor models (particularly important for CAD integration)
  coated bolometer optimized for JT-60SA to be manufactured
Publication plan
  Contributions submitted to EC-21 & SOFT 2022 conference (June, Sept.). SOFT proceeding will be published in Fusion Engineering and Design.