## Slide 1
EDICAM visible camera system Tamás Szepesi for the EU and JA EDICAM teams

## Slide 2
EDICAM overview – Design parameters
T. Szepesi The EDICAM system | WPSA Coordination Meeting 2022.05.04. 2
Single channel wide-angle fast video diagnostics
Features
  Field-of-view: 80° (wide-angle)
  Tangential view
  Temporal resolution: 100 Hz @ 1.3 Mp (1280x1024)
     max. 400 Hz full frame, up to 20 kHz for ROIs
  Spatial resolution: better than 13 mm (over 3-8 m distance)

## Slide 3
EDICAM overview – Camera capabilities
T. Szepesi The EDICAM system | WPSA Coordination Meeting 2022.05.04. 3
Advanced camera control: multiple ROIs
Define several regions to be observed
  different size and position
  independent timing (frame rate)
  up to 6 ROIs can be defined
Real-time features and image processing capabilities
All data is flowing through an FPGA (≈ fast chip) → offers real-time image processing
events: intensity threshold on image, time, external input (TTL)
  → events are detected automatically in real-time
actions: start/stop ROI readout, external trigger (TTL)
  → actions are performed autmatically in real-time
CMOS chip
ROI 2
ROI 1
FPGA
cam.head
10 Gbit/s fiber link
Modular design:
camera head + FPGA card
Small
Durable
Image processing
Events

## Slide 4
Project timeline
T. Szepesi The EDICAM system | WPSA Coordination Meeting 2022.05.04. 4
Completion
acceptance tests passed / 11 July 2019
delivered to Naka / 22 July 2019
Installation
port plug installed / 10 April 2020
first in-vessel images / 16 April 2020
first high-quality images / 14 May 2020
Commissioning
individual linkage test / Nov 2019
4x integrated linkage tests in 2020
  → in last one overperform specifications
software update / March 2021
5th integrated linke test in 2022
All tests were passed, EDICAM is ready for operation.

## Slide 5
Planned work 2022 and beyond
T. Szepesi The EDICAM system | WPSA Coordination Meeting 2022.05.04. 5
Participation in the Integrated Commissioning
on-site presence throughout the campaign (?)
operation of the camera
help to commission the tokamak
  observe breakdown
  determine plasma size and position
  observe radiation collapse / disruption
  detect ECRH shinethrough
  detect hot-spots, UFOs
  observe radiation during ECWC
test and exploit camera functionality
Longer term upgrade
change of camera receiver card (outdated, no spare)
change control PC operating system from Win7 to Ubuntu
  → originally planned for 2022, but don’t want to do it before IC

## Slide 6
Publication plan
T. Szepesi The EDICAM system | WPSA Coordination Meeting 2022.05.04. 6
Publications in the past
2019: poster on ISFNT
  description of the whole system
2020: paper in Fusion Enginering and Design 153, 111505
  all details of the system incl. port plug, vacuum, mechanics, optics
Planned publications
conference and/or journal paper on the first results

## Slide 7
Thank you for your attention!