## Slide 1: What is detachment?
On the search for a practical key metric at W7-X
Thierry Kremeyer for the detachment subgroup

## Slide 2: Background
“We are therefore interested in ﬁnding a way to decrease the particle ﬂux reaching the target, for given upstream conditions in the SOL. Such a state has been found and is called divertor detachment. […]
The characteristic, in fact the deﬁning, observations of detachment are:
  ‘roll-over’ and decrease of the ion saturation current, j+sat, of Langmuir probes built into the inner and outer divertor targets, (d), (f), i.e. the ‘nt -rollover’ seen on ASDEX, ﬁgure 16.4;
  the Dα radiation from the target regions does not roll over/decrease, but continues to increase with ne, (e), (g).
A further feature of detachment is that it occurs when the target Langmuir probes indicate low temperatures, Te ≈ a few eV or less “ - Stangeby, Plasma Boundary Book IoP 2001
Less particles neutralizing on the target
Amount of particles re-ionizing continues to increase with ne
In practice:
Decrease of peak j+sat on Langmuir probes
Peak temperature below 10 eV or even 5 eV
Leonard divides detachment in momentum, particle, and energy detachment.

## Slide 3: What are the detachment conditions?
Necessary condition; What has to be true for a discharge to be called detached?
Reduce heat loads to a tolerable level at the divertor (10 MW/m2)
Low target temperatures to minimize sputtering (< 5 eV for tungsten)
…
Sufficient condition; If a discharge is detached then the following is true:
…
Reactor relevant detachment:
Enough recycling for sufficient neutral pressure at pumpgap (continous flow, 0.1 mbar)
High SOL density reduces impacting energy and decreaes neutral penetration
…

## Slide 4: Detachment at W7-X
Stangeby‘s detachment definition is not fulfilled at W7-X (Hα radiation decreases)
Robust and practical definition
Based on one or multiple metrics that are applicable to all magnetic field configurations
  One metric should be a control parameter
  We don‘t have to hit the exact value, but we need to know in which direction to turn „the knob“
Analog metric that depicts the entire spectrum
  Attached – all power at the target
  More power is radiated away, heat and particle loads are reduced
  Ionisation front moves inward – less plasma in SOL – SOL becomes more transparent for neutrals
  Tiny plasmas – no plasma in the SOL
frad has been used by a variety of people to differentiate these different scenarios.
  Readily available
  Covers entire spectrum from „all heat load on the target“ to „no heat load on the target“
  Applicable to all magnetic field configurations