## Slide 1: DIFFER contributions to SP-X1
Ivo Classen, Hennie van der Meiden, Jordy Vernimmen, Jonathan van den Berg

## Slide 2: Deliverables
Near target measurements:
  TS on Magnum and UPP
Passive VUV spectroscopy in Magnum
TALIF on Magnum
  Diagnostic development
  First step towards CARS/VUV-LIF

## Slide 3: Magnum-PSI
up to 5 eV
= 1019 – 1021 m-3
up to 1025 m-2s-1
q up to 50 MWm-2
Pulses: up to 20eV and 1GWm-2
Differential pumping:
neutrals: 0.3 Pa during plasma

## Slide 4: Section B
Passive VUV spectroscopy in Magnum-PSI
Coming soon to DIFFER: see contribution CU

## Slide 5: Section C
Active spectroscopy on Magnum-PSI
COmmisioning: TALIF (atoms)
Future: CARS/VUV-LIF (design ready 2022) (molecules)

## Slide 6: Motivation
6
The ro-vibrational distribution plays a major role: MAR rate can vary multiple orders of magnitude
Direct measurement difficult, but H2(r,n) distribution previously successfully measured in both linear plasmas and tokamaks (no current set-ups)
 Build new diagnostic on Magnum-PSI (divertor relevant plasmas) based on proven methods: VUV-LIF and CARS (TU/e, Plexis)
DIFFER will finance this from institute’s budget
From Vankan et al.

## Slide 7: Active spectroscopy: 3 methods
7
VUV-LIF based on Stimulated anti-Stokes Raman scattering (population  >2,J)
Coherent anti-Stokes Raman spectroscopy (CARS):
(population  ≤2,J)
Two photon Absorption Laser Induced Fluorescence (TALIF)
(density H atoms in ground state)

## Slide 8: VUV-LIF principle
VUV LIF spectroscopy of H2 ground state
Excite ground state ro-vib level to electronically excited state
Measure fluorescence signal
Scanning the laser wavelength excites different ro-vib states
110 to 165 nm for n=0 to n=14

## Slide 9: Status TALIF on Magnum-PSI
TALIF:
  Density of atomic H density Also applicable to N
  Excitation: 205.14 nm (for Ly b absorption with 2 photons)
  Fluorescence: Ha
Dye laser setup operational and generates 205 nm laser light
First attempt to obtain first signals on Krypton gas (check system operation) in May 2022
Plan first try-out for atomic density measurements in Pilot-upgrade: June 2022

## Slide 10: CARS in Magnum-PSI: status
10
Lower vibrational states (n<=2) can be measured with CARS
CARS:
4-wave mixing process
660-700 nm probe beam
532 nm pump beam
Dye laser setup operational (assume same laser as TALIF, Nd:YAG should be a seeded type)
Conceptual design in progress: Installation should start in September 2022
First tests in Magnum-PSI: Q2 2023

## Slide 11: Status VUV-LIF setup
Laser in VUV range (down to ~ Ly a)
 Raman cell (SARS)
In vacuum
VUV monochromators
Conceptual design in progress

## Slide 12: Thank you for your attention!