## Slide 1: Advanced spatially hybrid fluid-kinetic modelling of plasma-edge neutrals
Wim Van Uytven, W. Dekeyser, M. Blommaert, N. Horsten and M. Baelmans
24/6/2022
application to ITER cases using SOLPS-ITER

## Slide 2
Ion
Neutral
Electron
Plasma
(macro-scale
transport)
Neutrals (micro-scale transport)
Scope: accurate & efficient neutral modelling

## Slide 3: Simulation strategies for neutrals
plasma fluid finite volumes B2.5
kinetic neutrals
Monte Carlo EIRENE
fluid neutrals
finite volumes
B2.5
accurate many different reactions/processes
expensive for dominant CX (CPUt = f(coll))
statistical noise
faster
no statistical noise
limited reactions (no molecules in B2.5)
validity = f(coll.)
plasma fluid finite volumes B2.5
→ best of both worlds through hybrid fluid-kinetic methods?
Notes: + interessant voor optimalisatie, transient, …

## Slide 4: Atomic and molecular reactions
Neutral atoms
Neutral molecules
Molecular ions
For now: no atom-atom, atom-molecule or molecule-molecule reactions → linear transport problem

## Slide 5: Advanced fluid neutral models (atoms only)
[Horsten, N., PhD Thesis, 2019] → development in in-house code
[Blommaert, M. et. al (2018). CtPP] → implementation in SOLPS-ITER + benchmark with EIRENE (slab case)
[Van Uytven W. et al (2020). CtPP] → separate Tn + full consistency plasma-neutral coupling in SOLPS-ITER (slab case)
[Van Uytven W. et al (2022). NF] → implementation in extended grids SOLPS-ITER + benchmark ITER cases
Continuity, parallel momentum, and energy equation
Transport coefficients: closure based on dominant CX
BCs based on moments of velocity distribution after TRIM recycling + reflection

## Slide 6: Grids: ITER with voids

## Slide 7: Knudsen number
average CX mean-free path of neutral atoms
macroscopic length scale of the problem
Rules of thumb:
Kn < 0.01 strict validity fluid approach
0.01 < Kn < 0.1 good validity fluid approach
0.1 < Kn < 1 transition to kinetic
Kn > 1 strong kinetic effects
Kn > 10 fully kinetic
Notes: Omdat anders: additional possible cause of convergence issues in the presence of MV noise, very sensitive to what you take 4 orders of magnitude!

## Slide 8: Results AFN: ITER Be-Be (ni,c = 6∙1019 m-3)
Beryllium
Plasma coupled to kinetic Monte Carlo neutrals (EIRENE)
Plasma coupled to advanced fluid neutrals
Fluid only, no voids

## Slide 9: Results AFN: ITER W-Be (ni,c = 4∙1019 m-3)
Tungsten
Plasma coupled to kinetic Monte Carlo neutrals (EIRENE)
Plasma coupled to advanced fluid neutrals
Fluid only, no voids
Notes: Poorer agreement: higher knudsen numbers, highter temperatures: more fast reflection: less 2ev molecules

## Slide 10: Shortcomings atom-only fully fluid
Coupling with void regions
No accurate fluid description for molecules
Fluid models not valid in entire divertor / SOL
Spatially hybrid modelling

## Slide 11: Hybrid fluid-kinetic modeling: different flavours
Micro-marco (mM)
  N. Horsten, et al., CtPP 2020, 60 (5-6), e201900132
  N. Horsten, et al., JCP 409 2020: 109308.
Spatially hybrid (SpH)
  M. Blommaert, et al., NME 2019, 19, 28–33.
  N. Horsten, et al., NME 2021, 27, 100969.
Condensation-evaporation
  M. Valentinuzzi, et al., NME 2019, 18, 41–45.
(Multi-Level) Kinetic-diffusion Monte Carlo ((ML-)KDMC)
  B. Mortier, et al. arXiv 2020 preprint arXiv:2012.08985.
  B. Mortier, et al. JCP 2021: 110736.
This work
Notes: Wat hier mondeling vertellen?

## Slide 12: Spatially hybrid: general
Split equation in fluid and kinetic part
If
then
+
+
We may need/want fluid and kinetic parts to communicate
Apply fluid closure for fluid part
Notes: Split-up is based on sources. Fluid and kinetic co-exist in the domain.

## Slide 13: Shortcomings atom-only fully fluid
Coupling with void regions
No accurate fluid description for molecules
Fluid models not valid in entire divertor / SOL

## Slide 14: Spatially hybrid: plasma-void interface
Kinetic neutrals are followed until ionization
Surface source in EIRENE sampled from truncated Maxwellian fluid neutral distribution
Fluid  kinetic
Fluid neutral boundary condition
Moments of Maxwellian  imposed fluxes
interface
vessel
[M. Blommaert et al., PSI 2018]

## Slide 15: Shortcomings atom-only fully fluid
Coupling with void regions
No accurate fluid description for molecules
Fluid models not valid in entire divertor / SOL

## Slide 16: Inclusion of molecules
No validated fluid model for molecules exists at this point
Treat molecules fully kinetically
Focus on treatment of atoms from dissociation [N. Horsten et al., PSI 2020]
  everywhere fluid: higher speed-up, less accuracy
  everywhere kinetic: less speed-up, higher accuracy
Notes: Niet de dominante CX botsing van de atomen

## Slide 17: Shortcomings atom-only fully fluid
Coupling with void regions
No accurate fluid description for molecules
Fluid models not valid in entire divertor / SOL

## Slide 18: Generalized spatially hybrid
fluid neutrals
fluid neutrals
plasma fluid neutrals
fluid neutrals
kinetic neutrals
plasma kinetic neutrals
Kn. too high
Kn. OK
Notes: Hier ga ik later op verder
Dit is toegestaan door lineariteit van de vergelijkkingen

## Slide 19: Remaining issue spatially hybrid
Kinetic neutral atoms born from
  plasma-void interfaces
  dissociating molecules
  kinetic parts of targets
can still end up ondergoing a lot of collisons → ‘condense’ kinetic atoms in high CX regions to the fluid neutral population

## Slide 20: Kinetic→fluid condensation
Knudsen number of kinetic particle
→ terminate EIRENE trajectory
→ transfer mass/mom/ene to fluid neutrals
user-def. transition threshold
Fluid neutral fluxes
Interaction plasma ↔ fluid neutrals
After each CX reaction:
no
continue particle tracing
yes
Condensing kinetic atoms
we now also create noise on fluid neutral population

## Slide 21: Spatially hybrid with kinetic→fluid condensation
kinetic neutrals
Monte Carlo EIRENE
fluid neutrals
finite volumes
B2.5
plasma fluid finite volumes B2.5

## Slide 22: Kinetic→fluid condensation
Investigate Knt on a broad scale: Knt = 0.1, 1, 10 and 100
Interpretation as first-flight model
  first few collisions are the ones where atom distribution still deviates most from plasma Maxwellian
  useful first-flight information still captured with Knt > Knt,phys

## Slide 23: Inclusion of molecules
No validated fluid model for molecules exists at this point
Treat molecules fully kinetically
Focus on treatment of atoms from dissociation
  everywhere fluid: higher speed-up, less accuracy
  everywhere kinetic: less speed-up, higher accuracy
  now: launch everywhere kinetic, atoms will condense to fluid in high CX regions
Notes: Niet de dominante CX botsing van de atomen

## Slide 24: Variants for target BCs
Kn > Knb ? → HYB-2
Kn < Knb ? → HYB-1
ions & fluid neutrals
EIRENE TRIM
kinetic neutral atoms
kinetic neutral molecules
ions & fluid neutrals
B2.5 TRIMfl
fluid neutral atoms
kinetic neutral molecules
HYB-1: fluid atoms, kinetic molecules
HYB-2: kinetic relaunch
HYB-3: automated selection of fluid or kinetic approach
[N. Horsten et al. PSI 2020]
For now: Knb = 0.1

## Slide 25: Results: trapezoidal slab case (incl. molecules)

## Slide 26
Fluid fraction trapezoidal slabs

## Slide 27: Results: ITER with voids (incl. molecules)

## Slide 28: “Naive” particle distribution

## Slide 29: Speed-up and noise
Standard deviation in statistically steady-state, average over all cells in outer divertor leg
Conclusions made in PET2021
kinetic molecules take up most of remaining CPUt in hybrid methods for Knt ≥ 1
very large speed-ups for atom-only
good speed-ups for equal noise at target with molecules
PD from previous slide
Noise-corrected speed-up

## Slide 30: Bias issue hybrid methods
→ the model error is actually lower than previously shown
→ similar results for all cases
→ bias error due to insufficient particles at PFR voids

## Slide 31: Bias issue hybrid methods
Flux of fluid neutrals launched into voids is 10x larger than incident ion flux on targets
→ hybrid may need more particles than MC to keep noise on plasma AND fluid neutrals sufficiently low everywhere
Notes: + number of numerical experiments to determine cause

## Slide 32: Neutral solution on fixed BG (HYB-1)
Upstream
Problem starts from fluid neutral density upstream near PF boundary
radial cell #
radial cell #

## Slide 33: Speed-up and noise reduction
For similar number of particles
  10-100x speed-up for cases with only atoms
  3-5x speed-up for cases with molecules
  noise reduction in the vicinity of the strikepoint
  a lot more noise where neutrals from PFR voids condense
    → bias error
Redo analysis with P proportional to fluxes for HYB
  back to cases with only atoms
  Only Knt = 0 and Knt = 10

## Slide 34: New particle distribution
#particles / stratum ~ incident flux
→ hybrid without condensation needs 2x less particles or similar
→ hybrid with condensation needs 2-5x more particles

## Slide 35: Speed-up for AO case with new PD
→ 1-3.3x speed-up for this particle choice

## Slide 36: Results for new PD
No condensation

## Slide 37: Results for new PD
With condensation

## Slide 38: Noise reduction plasma
→ huge reduction of noise on plasma variables, mainly close to target
Notes: Het probleem ligt bij de ruis op de brontemen door condensatie, kan niet rechtstreeks met plasma vergeleken worden

## Slide 39: Results for new PD
→ even with #P/stratum ~flux, HYB with condensation still runs into bias error sooner than full MC!

## Slide 40: Noise on particle sources

## Slide 41: Things that did not resolve bias issue
Minimum # collisions before condensation
Condense with a probability < 1
Turn off source rescaling
Implementation of condensation process as reaction instead of in collide.f
  Use track-length estimator instead of collision estimator (but still analog simulation!)

## Slide 42: Evaluation advanced SpH method
Simplest hybrid method
Compact implementation
No convergence issues encountered
Acceptable model error (± 10%)
No more long-lived kinetic atoms
User freedom speed-up vs. accuracy (Knt, HYB-1/2/3)
Large speed-ups (x10-100), at least for similar #particles + atoms only
Less rigorous than micro-macro
Statistics of the method needs more attention
Accessible for plasma-edge community
we now also create noise on fluid neutral population

## Slide 43: Future work
Solution for molecules needed
  More detachment → molecules more important
  Molecules will become bottleneck, regardless of speed-up for atoms
Statistical analysis
MC procedures which are optimal for absorption-dominated?
  Non-analog simulations? See e.g. PhD Bert Mortier
Test method on (partially) detached DEMO cases

## Slide 44
Thank you for your attention
Questions?
Wim Van Uytven
Division Meeting, 18/5/2021

## Slide 45: AFN transport model
Continuity
Parallel momentum

## Slide 46: AFN transport model
Energy
Notes: Internal energy equation + option to solve Ti and Tn together
p grad V term !!!!!!

## Slide 47: Numerical experiment to narrow down problem origin…(HYB-2 Knt=10)
→ bias originates mainly from fluid neutral density?

## Slide 48: AFN boundary conditions
calculation of fluid boundary fluxes based on estimated neutral velocity distriubtion and TRIM database (reflection kernel from EIRENE)
[Horsten, N., PhD Thesis, 2019]
Notes: Gedrag trim database nabootsen

## Slide 49: Grids: trapezoidal slab & narrow ITER
Trapezoidal slab
ITER without void regions
10 cm
1 m
narrow divertor
neutrals “locked up” in closed divertor
large divertor
 reduced influence kinetic neutrals
 increased influence kinetic neutrals
10 m

## Slide 50: Results for new PD
#P/strata ~ flux