## Slide 1: 2022 Scientific real-time control activities ​
Stephanie Hall and Ondrej Ficker

## Slide 2: Aim
Report on the available scientific real-time networks in EUROfusion facilities to support the development of real-time networks on JT60-SA.
1. Collect EUROfusion Experience
Provide summary and basic information on the scientific real-time networks available on JET and MAST-U.
Provide summary and basic information on the scientific real-time networks available on COMPASS.
Potentially extend to other EUROfusion facilities (ASDEX Upgrade, TCV, WEST and W7-X) through the EUROfusion Operations Network.
2. Discussion with experimental team and QST, to understand the planned JT60-SA capabilities and scientific needs.

## Slide 3: Agreed scope of activities
In scope:
  Event driven control networks
  Feedback control networks
  Advanced controller (RAPTOR, Multiple-Input-Multiple-Output)
  Network outlines to include:
    Name and description
    Sensors and actuators
    Effectiveness with reference pulses and relevant papers
Out of scope:
  Protection networks
  An engineering description of the systems running the real-time networks

## Slide 4: Devices included in the analysis
List of feedback actuators and important machine params.
 | gas | pellets | NBI | ICRH | ECRH | shape | First wall | Ip/Bt | R/A
JET |  |  |  |  |  |  | Be/W | 4/3.5 | 3/1.1
MAST-U |  |  |  |  |  |  | C | 1/0.8 | 0.7/0.5
AUG |  |  |  |  |  |  | W | 2/3.1 | 1.6/0.5
TCV |  |  |  |  |  |  | C | 1.2/1.45 | 0.88/0.25
COMPASS |  |  |  |  |  |  | C | 0.4/1.5 | 0.56/0.2
COMPASS-U* |  |  |  |  |  |  | W? | 2/5 | 0.9/0.28
WEST |  |  |  |  |  |  | W | 1/3.7 | 2.25/0.7

## Slide 5: COMPASS, TCV & AUG data collection
See excel file

## Slide 6: JET and MAST-U data collection
See excel file

## Slide 7: Analysis Started
Network developments are driven by the actuators available and PFC material
  NTM control, Te profile control with ECRH/ECCD available
  Excessive radiation/impurity accumulation control with W in PFCs
  Isotope mixture/ heating optimisation with ICRH
  Etc.
Differences in terminology and approach – network vs components (estimator – controller – actuator management) that are independent and combined as required
This study is valuable to identify synergies, pros and cons of the various approaches in order to drive the new controller development in current and new devices, particularly JT60-SA

## Slide 8: Future Plans
2022 plans:
  Complete data collection
  Write report on findings
Discussion with the Experiment team (ELs, TGLs) - get list of expected/desired network
Discussion with QST – current QST RT network setup
Collaboration plans with WPPrIO:
  EON workshop on hardware, software basis (framework)
  Define scope and goal for a similar real-time protection analysis (EON workshops or report).
  Joint analysis to identify synergies and joint development opportunities

## Slide 9: EON real-time workshop
Real-Time Controller architecture workshop:
  Software/Hardware architectures
    Overall setup of system-layout, framework
    Interfaces to subsystems
    Design parameters: Update rates/ Latencies
  Operational setup- in pulse sequence
  Commissioning
  Identify similarities between systems:
    Strengths
    Weaknesses
  Identify any opportunities for sharing of information and effort
  Participants: EUROfusion and Broader Approach experts, external guests to be invited

## Slide 10: Feedback
Looking to feedback from the experimental team on what networks they are considering to use for their topical group