## Slide 1: ECWC and modelling for JT60-SA
Johan Buermans

## Slide 2
2
Johan Buermans - LPP-ERM/KMS
Modelling
Modelling
ECWC
Needs & Plans
He
D
TCV1,2
Density profiles matched with interferometry data
Transport coefficients are estimated
Code has been benchmarked for TCV He and D plasmas
AUG3
Density profiles matched with TS and MILS data
Estimates of peak density and temperature through characteristic radiation
Transport coefficients are estimated
He
D
The model reproduces the density profiles using conventional assumptions on anomalous diffusion and outward convection and provides insight on the fraction of absorbed EC power. A value for the latter is hard to obtain from experimental data.

## Slide 3
3
Johan Buermans - LPP-ERM/KMS
ECWC
AUG3
Confirms TCV experiments
Plasma follows the field lines
Convection directs the plasma to the LFS
Magnetic mirror reduces the plasma flux to the HFS
TCV1,2
Vertical field optimizes plasma density
ExB drift guides the plasma to the LFS
Plasma can be guided to desired areas on HFS using dedicated magnetic configurations
Magnetic mirror reduces the plasma flux to the HFS
Camera tomography
Helps visualizing the plasma flows
Can help to determine density and temperature
Modelling
ECWC
Needs & Plans

## Slide 4
4
Johan Buermans - LPP-ERM/KMS
Needs & Plans
Modelling
ECWC
Needs & Plans
Analysis of wall conditions:
  Evolution of outgassing after discharges + effect of conditioning on outgassing
  Particle balance for all discharges : contribution of wall fueling
    Gas content, mass spectrometry: impurity content
    Langmuir probe measurements for PWI ?
Modeling of ECWC to complement experimental observations:
Pressure gauges, magnetic field configuration, injected power
Availability of density profiles:
  Use of EDICAM camera data for ECWC modelling
    Tomographic reconstruction
    Ratios of the emission intensities of various atomic spectral lines
  Interferometry, Thomson scattering, spectroscopy to complement the density profiles?
TCV1 Tom Wauters et al, RF plasma simulations using the TOMATOR 1D code: case study for TCV helium ECRF plasmas, Plasma Phys. Control. Fusion 62 (2020), 105010 doi: 10.1088/1361-6587/aba767
TCV2 Johan Buermans et al, ECWC experiments and modeling on TCV, 48th EPS Conference on Plasma Physics, 2022, Maastricht
AUG3 Tom Wauters et al, Characterisation of Electron Cyclotron Wall Conditioning Plasma in ASDEX Upgrade, Nucl. Fusion: NF-105694 submitted