## Slide 1
SOLPS-ITER / SONIC
Benchmark
08/09/2022
Giulio Rubino

## Slide 2
Outline
G. Rubino | WPSA General Planning Meeting | 09 September 2022 | Budapest | Pag. 2
Main goal and general overview
Previous study: mesh resolution assessment
Profiles comparison in pure D plasma
Current status and future work

## Slide 3
Main goal and general overview
SOLPS-ITER/SONIC benchmark with a step-wise approach
Pure D with
C wall (for reflection)
D + intrinsic C
D + intrinsic C
+ extrinsic Ar
Grid Sensitivy
study
Partially detached
and attached
Comparison
Assessment of the
effect of different
impurity model
JT-60SA scenario-like
configuration
G. Rubino | WPSA General Planning Meeting | 09 September 2022 | Budapest | Pag. 3

## Slide 4
Mesh resolution assessment
3 different poloidal resolutions taken into account : 60x36, 120x36, 240x36
PSOL ~ 6MW and ne,sep ~ 2e19 m-3
Increase in the computational time (more than linearly) by increasing poloidal resolution
Assessment of discretization error εdiscr [K.Ghoos et al 2019 Nucl. Fusion]
Assessment of the poloidal resolution to gradient ratio: λФ / Δx, λФ = |Ф/▽Ф|
Trade-off between the accuracy of the solution and the computational time
120x36 grid resolution
 | Fluid neutral | Fluid neutral |  | EIRENE | EIEIRENE | 
 | Coarse | Ref. | Fine | Coarse | Ref. | Fine
εdiscr(%) | 51.8 | 32.8 | 20.7 | 56.8 | 38.7 | 26.8
G. Rubino | WPSA General Planning Meeting | 09 September 2022 | Budapest | Pag. 4

## Slide 5
Same mesh in both codes (mesh convertor developed by Shohei-san)
Boundary conditions and inputs set as close as possible
No drifts, flat transport coefficients, no SOL currents
Very similar profiles both at midplane and target
Partially detached pure D plasma
G. Rubino | WPSA General Planning Meeting | 09 September 2022 | Budapest | Pag. 5
Thanks to Shohei-san
Outer midplane
Inner target
Outer target

## Slide 6
Different upstream mesh width: need to check the mesh cut level
Different upstream profile (ne,omp and Te,core ) get same profiles for a better target comparison
Te differences are more pronouced  need to exclude the influece of the upstream conditions
Attached pure D plasma
G. Rubino | WPSA General Planning Meeting | 09 September 2022 | Budapest | Pag. 6
Thanks to Shohei-san
Outer midplane
Inner target
Outer target

## Slide 7
Pure D comparison in attached conditions:
  Get the same upstream conditions use the same core temperature boundary condition (ion end electron fluxes)
  Check the external D puffing rate
  Make energy balance and analysis of the different terms in the equations
  Strong differences are observed in case of parallel SOL current (Current continuity equation is solved)  Investigations are ongoing
D + intrinsic C
  Definition and verification of the setup ongoing:
    Ychem and Yphys? Turn off physical sputtering?
    Define wall properties, i.e. wall material  C+SS+Cu (problem of Ar on Cu reflection data) as suggested by Nakano-san
    First assessment of C vs C+SS wall definition shows negligible differences
  Simulations are ongoing
Future Plans
  Setup impurity seeded cases (Ar) in collaboration with QST team
Current status and future work
G. Rubino | WPSA General Planning Meeting | 09 September 2022 | Budapest | Pag. 7

## Slide 8
Thank you
for your attention