## Slide 1: CRM for EIRENE simulations of EU-DEMO detachment
D. Borodin, F. Cianfrani

## Slide 2: INTRODUCTION
CRM: list of particles/reactions: balance equations  equilibrium btw plasma A&M species
YACORA: solver+ established database [1]  CRM in tokamaks
EIRENE: Monte-Carlo transport solver + CRM
Detached plasma divertor: plasma temperature below 10eV atomic and molecular (A&M) reactions
CRM with molecular source  main reactions in
molecular source from simulations  transport
AIM:
This work:
EU-DEMO
JET
Interchange btw YACORA and EIRENE to provide CRM for detachment control modelling

## Slide 3: COLLISIONAL-RADIATIVE MODEL
Reaction | Type | Source
H2 + e → H2+ + e + e | molecular ionization | H2vibr
H2 + e → H2(btriplet) → H + H + e | neutral dissociation | H2vibr
H2 + e → H + H+ + e + e | dissociative ionization | Amjuel
H2 + H+ → H2+ + H | charge exchange (CX) | H2vibr
H + e → H+ + e + e | ionization | Amjuel
H2+ + e → H + H+ + e | neutral dissociation (MAD) | Amjuel
H2+ + e → H+ + H+ + e + e | dissociative ionization (MAI) | Amjuel
H2+ + e → H + H | dissociative recomb (MAR) | Amjuel
H+, H, H2+,H2
Particle species
Molecular source:
Reference value
Plasma parameters:
Fixed electron and ion densities:
ne = ni = 1019m-3 for [1]
ne = ni = 1021m-3 for [2]
Temperature: Te = Ti = 0.2÷30eV.
H+, e sinks (reservoirs)
EU-DEMO
JET
[1] M Groth et al. 2013 Nucl. Fusion 53 093016 [2] F Subba et al. 2020 Nucl. Fusion 61 106013

## Slide 4: COLLISIONAL-RADIATIVE MODEL: results
YACORA solver
large H2 density
H2+ density peak
EU-DEMO
JET

## Slide 5: COLLISIONAL-RADIATIVE MODEL: results
low temperature (T < 2eV) leading reaction chains:
H2+H+→ H2++H H2++e → H+H++e
MAR/MAD competition at very low temperature
MAD
MAR
H2+H+→ H2++H H2++e → H+H
EU-DEMO

## Slide 6: VIBRATIONALLY RESOLVED CRM
vibrationally resolved molecular states H2(v) (v=0 ..14) with electron-induced ladder-like trans H2(v) + e → H2(v±1) + e rates H2vibr
vibrational transitions are the main reaction channels at low temperatures
EU-DEMO

## Slide 7: MOLECULAR TRANSPORT
molecule density scales linearly with the source  effective source term
up-stream region: substantial overlap effective source and density
Gas puffing
JET

## Slide 8: MOLECULAR TRANSPORT
molecule density scales linearly with the source  effective source term
JET
Gas puffing
divertor region: discrepancy  novel physical conditions (dominance of CX reactions at low temperature)

## Slide 9: CONCLUSIONS
CRM for A&M reactions in
1) it captures game-changing branching difference in dependence of plasma temperature for various reaction contributions (MAD vs MAR, vibrational trans vs dissociation/ionization)
2) the molecular source (D2 influx) is introduced and a way to related it with EDGE2D-EIRENE runs including transport in divertor is demonstrated
3) it is staged for both standalone use (as presented) and for intergration into EIRENE for detachment control analysis
4) an extension to include isotope effect and electronic excitations for computing spectroscopic emission (opacity) is foreseen.

## Slide 10
Thanks for the attention!