## Slide 1: New facilities for HYDKIN toolbox
D.Borodin, F.Cianfrani, B. Küppers

## Slide 2
HYDKIN:
toolbox for plotting and manipulation of A&M data with a user-friendly graphical interface: HYDKIN
EIRENE databases: AMJUEL, HYDHEL, H2VIBR, METHANE, ..
available at http://www.eirene.de/hydkin/
Password-protected (for access contact the authors)
Reiter Phys.Scripta 2009

## Slide 3
HYDKIN: particle solver
    1-dimensional
    reservoirs, P/Q species
    spectral analysis
    sensitivity analysis

## Slide 4
HYDKIN: particle solver output
Development of stationary equilibrium
Default case (see next slides)
reservoir
“infinite reserve” of particles at fixed temperature and density

## Slide 5
HYDKIN:
HYDKIN can be used to
to import/export data (db, fhg, json formats),
to produce input data for EIRENE and for other codes,
to check and improve the results of the simulation,
to check data for consistency, abnormal features, ..
to understand the physics and identify the most significant processes (among the selected ones).

## Slide 6
HYDKIN: comparison recomb. rates
JH Ly-α opaque
JH: Johnson-Hinnov J. Quant. Spectr. Rad. Transf. 1973
SF: Sawada Fujimoto J. Appl. Phys. 1995
SF n=1
SF Ly-α removed
JH rad + 3b recomb
SF rad + 3b recomb
SF n=2
e + H+  H

## Slide 7
HYDKIN: comparison dissociat. rates
HYDHEL
AMJUEL
Factor 3 wrong
e + H2  H + H + e

## Slide 8
new HYDKIN:
Availables now from main page at
Still work in progress (temporary stop)

## Slide 9
new HYDKIN: grouping of reactions
OLD: reactions grouped by database
NEW: reactions grouped by formula → identified by number
plotter: reactions from different databases → comparison
solver: radio button: avoid multiple reactions with same formula

## Slide 10
new HYDKIN: grouping of reactions
Grouped reactions differing for vibrational resolution (one row)
next stage: bundle vibrational state

## Slide 11
new HYDKIN: columns
List of (retractable) columns:
number: identify the reaction (AMJUEL number w/o letters)
reaction: formula
reference
data type: experimental, calculated, mixed…
Peculiar properties: additional info
generation: 0 for now
data origin: type of fit (original data, improved fit, …)
File/chapter: database/section

## Slide 12
new HYDKIN: default cases
Deduced from JET (EDEGE2D-EIRENE) and DEMO simulations
with and w/o vibrational resolution
Subba et al. Nucl.Fusion 2021
Groth et al. Nucl.Fusion 2013
+ molecular volumetric source

## Slide 13
new HYDKIN: default cases- unresolved
H2 dissociation
H2+ dissociation
Heavy particles collisions dominating at low temperature
MAR/MAD competition at low temperature

## Slide 14
new HYDKIN: default cases- resolved
Higher vibr states
Vibrationally resolved data from H2VIBR provides a reduced dissociation rate.
AMJUEL: unresolved
H2VIBR: resolved
H+ + H2  H2+ + H
A Holm et al. CPP 2022

## Slide 15
new HYDKIN: output
new json-output containing:
background parameters
selected particles
selected reactions
    column values
    rates
preliminary for interplay with other programs….

## Slide 16: Outlook
… some issues still to be solved:
electronic states
inclusion more CRMs
inclusion further databases (ADAS, IAEA, ..)
increase readability and usability
direct link with EIRENE input files → standalone HYDKIN dedicated module
New HYDKIN:
grouping of reactions
new column/features
default cases
json output

## Slide 17
Thanks for the attention!