## Slide 1: VUV spectrometer for PSI-2 Status report PWIE-SP X.1.T-T002-D002
Michael Reinhart

## Slide 2: Overview
Work is part of deliverable PWIE-SP X.X1.T-T002-D002
Tasks:
Setup a passive spectroscopy system for VUV at PSI 2
Use VUV OES for measurements of H/H2 (and isotopologues) emission lines
Aims:
Diagnostic method for recombining plasmas in PSI-2
Input for modelling activities

## Slide 3: Status
Seya-Namioka Vacuum Monochromator
500 mm focal length
Typical resolution 0.05 nm with 1200 g/mm grating
Status: Commissioning is delayed
Under vacuum
UV light source added
Electron multiplier detector added
To be done:
Setup of controls for the scanning motor
Setup for data aquisition

## Slide 4: Example spectrum
Sample spectrum by manufacturer:
Discrimination of H-D emission of Lα possible?

## Slide 5: Setup at PSI-2
Plasma source
Magnets
Magnets
Linear
Target
manipulator
Manipulator ports
Observation ports
Langmuir probe
VUV
Spectrometer
direct view
Plasma dump
VUV
Spectrometer
Mirror path
Pros: Focus by mirror, spatial resolution possible, less restrictions on location
Cons: Potential loss of intensity, additional components (mirror+controls, pumping)

## Slide 6: Timeline
Commissioning of spectrometer: Coming months
Installation + measurements at PSI-2: next year