## Slide 1: WP PWIE: SP ADC-H Final Meeting
SP ADC-H: Roberto Ambrosino

## Slide 2: SP ADC-H Milestones and Tasks 2021-2022
Activity | Deliverable ID(s) | Task Title | Start date | End date
SP ADC-H | D001 | Engineering compatibility of best promising configurations described in WP ADC-DTT’s final report for DTT facility: recommendations for control and equilibria design | 01/2021 | 12/2022
SP ADC-H | D002 | Engineering compatibility of best promising configurations described in WP ADC-DTT’s final report for DTT facility: recommendations for VDE and disruption consequences | 01/2021 | 12/2022
Sequential WP-M ID | Related WBS ID | WP Milestone Title | Due Date [mm/yyyy] | Related GA D/M No. | Criticality of Relation to the GA D/M (high/low)
WM18* | SP ADC | Engineering compatibility assessment of potential best promising DEMO ADC solutions with the DTT facility completed (DEMO) | 31.12.2022 | PWIE.M.02 | 
WM19* | SP ADC | Engineering DEMO evaluation of most favourable ADC solutions in terms of VDE and disruption events compatibility completed (DEMO) | 31.12.2022 | PWIE.M.02 | 

## Slide 3: SP ADC-H: Overview of the activity
Deliverable: SP ADC-H.T001.D001, D002
Status: completed / partially done / in progress / delayed / cancelled
Facilities: e.g. PD # days, TOMAS or Modelling: Code name
Goal: Electromagnetic modelling of alternative configurations for the DTT device and controllability analysis of the alternative configurations
Electromagnetic modelling
Support to the DTT physic activities under WPWIE in terms of definition of additional DTT plasma configurations
Magnetic control
Design of the preliminary shape and VS controllers for SN and alternative configurations for the analysis of disturbances and transients (LH and HL).
VDE and Disruptions
Analysis of the effects of VDE and MD of the plasma facing components
Modelling: CREATE-NL, CREATE-L, MAXFEA, FIXFREE
Resources:
Involved RU: CREATE, ENEA, TUSCIA
Linked WP: WPDIV-DTT
X-divertor
Negative Triang
Double Null
Snowflake
Low
priority
Low
priority
Single Null

## Slide 4: SP ADC-H – D001 - Goals reached in 2021-22
Activity | Deliverable ID(s) | Goals reached in 2021-22
SP ADC-H | D001 | Analysis of the vertical stability performance of the DTT configurations (SN, XD, NT) Shape sensitivity of the DTT configurations (SN, XD, NT) Design of a vertical stability controller and testing on nonlinear sim. codes (SN, XD) Shape controller for SN and XD configuration and testing on the HL transition
CREATE – ENEA
R. Ambrosino, E. Acampora, A. Castaldo, G. Ramogida

## Slide 5: SP ADC-H: Passive stability performance 2021
Phases | Ipl [MA] | betapol | li | Growth rate [s^-1] | Stability Margin
RAMP-UP | 3 | 0.1 | 0.9 | 58.44 | 0.63
RAMP-UP | 4.3 | 0.1 | 0.8 | 92.35 | 0.48
RAMP-UP | 5.5 | 0.1 | 0.8 | 61.84 | 0.59
FLAT TOP | 5.5 | 0.65 | 0.8 | 36.42 | 0.74
FLAT TOP | 5.5 | 0.1 | 1.2 | 106.78 | 0.42
RAMP-DOWN | 4.5 | 0.1 | 0.89 | 34.38 | 0.78
RAMP-DOWN | 3.5 | 0.1 | 0.98 | 40.77 | 0.70
RAMP-DOWN | 2.5 | 0.1 | 1.07 | 64.04 | 0.57
Single null reference scenario
Growth rate and stability margin
Config. | Ipl [MA] | betapol | li | Growth rate [s^-1] | Stability Margin
XD | 4.5 | 0.65 | 0.8 | 71.04 | 0.50
XD | 4.5 | 0.1 | 0.8 | 77.57 | 0.56
SN-NT | 4 | 0.4 | 0.8 | 76.80 | 0.48
SN-NT | 4 | 0.1 | 0.8 | 83.90 | 0.46
Alternative configurations
The upgraded definition of the in-vessel components has been developed in 2022 under DIV-IDTT.S.07-T005-D001-D002 with a copper stabilizing plate of smaller dimension

## Slide 6: SP ADC-H: Shape sensitivity of DTT configurations
A big ELM (Wj=-1 MJ), simulated as a step in p and li, with p=8Wj/(30R0Ip2) and li=-p, namely, for the X p =-0.03 and li=0.03, has been considered.
SN
(robustly stable)
XD
Possible criticality in the divertor region and at 11 o’clock
NT
Possible criticality in the inner equatorial plane
Additional disturbancies need to be considered

## Slide 7: DTT magnetic control system
Control of alternative configurations is a major challenge in next generation devices. The main issues of magnetic control are related to:
  Vertical stability in-vessel equatorial coils and passive stabilizing plates
    Elongated plasmas suffer from the vertically unstable mode
    Strong coupling with passive structures is required to reduce the plasma growth rate
  Shape and plasma current control CS/PF coils system
    Alternative configurations are highly sensitive to variations in the plasma pressure and current distributions
  Power exhaust control in-vessel divertor coils
    Internal coils are needed for control of power exhaust parameters such as flux expansion and connection length
    Necessity to reduce thermal power on the divertor plates: strike point sweeping

## Slide 8: DTT magnetic controller design
Plasma Magnetic Control System
PLANT
Starting from 2022, the WP PWIE activities has been executed in collaboration with WPDIV-IDTT.S. CODAC and PCS for the requirements definition and assessment of the single null configuration.

## Slide 9: Shape controller design
Shape control is based on the XSC (eXtreme shape Controller) strategy, conveying the current references required for the control of desired geometrical descriptors
Shape control through virtual gap sensors has been successfully validated on the SN configuration
Alternative configurations (such as the XD) share extreme sensitivity towards disturbance in the divertor area, due to secondary x-points
Shape control through gap sensors can be cumbersome, therefore a more robust control strategy is required  Isoflux control

## Slide 10: Shape controller design: SN configuration
ITER like model of the HL transition

## Slide 11: Shape controller design: XD configuration
77
65
56
48
66
29
21
9
74

## Slide 12: SP ADC-H – D002 - Goals reached in 2021-22
Activity | Deliverable ID(s) | Goals reached in 2021-22
SP ADC-H | D002 | A disruptions analysis considering the different DTT plasma configurations (SN, NT, XD) and different disruption scenarios (upper and lower VDE) by using MAXFEA code
CREATE – ENEA
R. Lombroni, G. Calabrò, P. Fanelli, G. Ramogida

## Slide 13: SP ADC-H – D002 – Description of the activity
A set of Downward and Upward Vertical Displacement Events (DVDEs - UVDEs) were simulated considering SN, XD and NT configurations and exploring different durations of CQ
The main assumptions of the VDEs:
  Destabilizing kick of 10 ms to simulate the loss of position control;
  TQ at a given critical safety factor (=2) as betapol drop in 1 ms;
  Different CQ durations (~4 and ~40 ms);
  Halo currents growth during CQ.
Produced output:
  Induced currents and forces in the VV and the Stabilizing Plates
  Induced currents, voltages and forces in the in-vessel coils
  Plasma filaments (to be used as source term in possible future 3D analysis)
  Evolution of the plasma main parameters (Ipla, Zj, Rj, ecc)

## Slide 14: SP ADC-H – D002 – Upward VDE
SN @SOF UVDE slow
Fz VV ~ 8 MN during CQ

## Slide 15: SP ADC-H – D002 – Downward VDE
SN @SOF DVDE slow
Fz VV ~ -10MN during CQ

## Slide 16: SP ADC-H – D002 – Table of the results
Class of event | CQ [ms] | TQ init event | Halo onset | Axi-sim halo factor | Ihalo [MA] | Ip at TQ [MA] | Fz max on VV - [MN]
SN |  |  |  |  |  |  | 
DVDE FAST | ~4 | q95 = 2 | CQ | 0.3 | 1.7 | 4.8 | -4.3 (near the end of CQ)
DVDE SLOW | ~40 | q95 = 2 | CQ | 0.53 | 2.9 | 4.8 | -10.2 (during the CQ)
XD |  |  |  |  |  |  | 
DVDE FAST | ~4 | q95 = 2 | CQ | 0.38 | 1.7 | 4.3 | -4.4 (near the end of CQ)
DVDE SLOW | ~40 | q95 = 2 | CQ | 0.45 | 2.0 | 4.3 | -10.3 (during the CQ)
NT |  |  |  |  |  |  | 
DVDE FAST | ~4 | q95 = 2 | CQ | 0.35 | 1.4 | 3.7 | -2.7 (after the CQ)
DVDE SLOW | ~40 | q95 = 2 | CQ | 0.51 | 2.0 | 3.7 | -6.5 (during the CQ)
Class of event | CQ [ms] | TQ init event | Halo onset | Axi-sim halo factor | Ihalo [MA] | Ip at TQ [MA] | Fz max on VV - [MN]
SN |  |  |  |  |  |  | 
UVDE FAST | ~4 | q95 = 2 | CQ | 0.18 | 0.97 | 4.8 | 4.5 (near the end of CQ)
UVDE SLOW | ~40 | q95 = 2 | CQ | 0.36 | 1.98 | 4.8 | 7.9 (during the CQ)
XD |  |  |  |  |  |  | 
UVDE FAST | ~4 | q95 = 2 | CQ | 0.16 | 0.7 | 3.8 | -2.6 (after the CQ)
UVDE SLOW | ~40 | q95 = 2 | CQ | 0.31 | 1.4 | 3.8 | 3.0 (during the CQ)
NT |  |  |  |  |  |  | 
UVDE FAST | ~4 | q95 = 2 | CQ | 0.16 | 0.63 | 3.5 | -2.3 (after the CQ)
UVDE SLOW | ~40 | q95 = 2 | CQ | 0.41 | 1.6 | 3.5 | -2.2 (after the CQ)

## Slide 17: SP ADC-H – D002 – Conclusions
An updated DTT MAXFEA model has been set up and the reference SN, XD and NT
configurations have been reproduced showing a very good agreement with CREATE-NL code
The MAXFEA model has been benchmarked against CREATE-NL code considering a simplified disruption case with a filamentary representation of the plasma
In 2021, a set of different disruptions scenarios (DVDEs) were simulated using the reference plasma configurations and exploring different CQ durations (fast 4ms, slow 40ms)
In 2022, the list of disruptions has been expanded by including UVDEs
SN and XD DVDE slow scenario generate the highest vertical force on the VV, about -10MN during the CQ phase

## Slide 18: Additional slides

## Slide 19: SP ADC-H: DTT poloidal field coils system
DTT will be equipped with:
a CS stack composed by 6 independent elements
6 PF coils up down symmetric
2 in-vessel equatorial coils will be used in DTT both for vertical stabilization and fast radial control
  Vertical stabilization connected in antiseries
  Radial control connected in series
4 in-vessel divertor coils used for:
  Local modification of the plasma divertor region
  Sweeping control
Stabilizing plates are also needed to improve the passive stability performance of the DTT scenarios
VS coils
Div. coils
Stabiliz. plates

## Slide 20: DTT magnetic control system
VS and
Power Exhaust
Power Exhaust quantities
In-vessel circuit voltage
Starting from 2022, the WP PWIE: SP ADC-H activities has been executed in collaboration with DIV-IDTT.S. 09b-T002 – CODAC and PCS for the requirements definition and assessment of the single null configuration.
Notes: PD: Plasma Devices as in PEP listed
HHF: High Heat flux as in PEP listed
IBF: Ion beam Facility as in PEP listed
Other facilties as in PEP listed

## Slide 21: Plasma magnetic control system

## Slide 22: Vertical stability (VS) controller
VS control is ensured by IVC1 and IVC2 when connected in anti-series
An ITER-like voltage-driven vertical controller has been designed for DTT device
The VS controller has been tested successfully on non-linear simulation code for both the SN and the XD configurations, also with new passive stabilizing plates.
IVC1
IVC2
Delivered to CODAC
Notes: PD: Plasma Devices as in PEP listed
HHF: High Heat flux as in PEP listed
IBF: Ion beam Facility as in PEP listed
Other facilties as in PEP listed

## Slide 23: Plasma current controller
A current-driven control strategy allows to generate the current references in the CS-PF coils required for the plasma current control
Current references are proportional to a set of currents providing a transformer field in order to reduce coupling with the shape controller
The current references are sent to a current controller conveying the required control voltages
The control transfer function C(s) is designed to ensure a time constant of 1s
Delivered to CODAC

## Slide 24: Fast radial controller (FRC)
FRC is a voltage-driven control ensured by IVC1 and IVC2 when connected in series
Fast radial control: on a smaller time scale with respect to the ex-vessel coils
The FRC allows to block plasma radial displacement during fast transients by nullifying the radial plasma velocity
IVC1
IVC2
Notes: Please mark your Subproject in

## Slide 25: Shape controller design: Isoflux control
The isoflux strategy is based on feedback control of flux measurements in fixed control points on the reference plasma boundary
By controlling the measured fluxes to the value in the reference x-point position, the LCFS is forced to pass through the chosen control points
Isoflux control is less intuitive than gap control, however it is more robust towards disturbances
1
2
3
4
5
6
7
8
9
XP
XP_2

## Slide 26: Conclusions
Alternative configurations are heavily affected by disturbances in the divertor region
Future implications:
  Validation on the nonlinear dynamic code (CREATE-NL)
  Development of a strategy for fine control of the strike points with the in-vessel divertor coils
SN
XD