## Slide 1: WP PWIE: SP ADC.J Final report
SPL ADC.J: P. Innocente, C. Meineri, G. Rubino, A. Uccello, L. Balbinot

## Slide 2: SP ADC.J Tasks 2021/2022
Deliverable ID(s) | Task Title
D001 | SOLEDGE2D-EIRENE modelling of DTT XD configuration (P1), DN XD: (P3)) (RFX)
D002 | SOLEDGE2D-EIRENE modelling of DTT XD configuration (P1), DN XD: (P3))(UNITUS)
D003 | SOLEDGE2D-EIRENE modelling of DTT in SN and DN with the longest outer leg configurations (hybrid configuration between SN and SXD “SNhybSXD” (P1) and between DN and SXD “DNhybSXD” (P3)) (POLITO)
D004 | SOLEDGE2D-EIRENE modelling of DTT with inner divertor adaption (hybrid configuration between SN and XD “SNhybXD” (P2) and between DN and XD “DNhybXD” (P3)) (ENEA)
D005 | SOLEDGE2D-EIRENE modelling of open divertor geometry in a subset of promising shapes (shape tbd from list of modelled SOLEDGE2D-EIRENE runs) (P2) (POLITO)
D006 | SOLEDGE2D-EIRENE modelling of open divertor geometry in a subset of promising shapes (shape tbd from list of modelled SOLEDGE2D-EIRENE runs) (P2) (ENEA)
D007 | SOLPS-ITER modelling of DTT SN (closed) divertor with and without dome with drifts activated (using EIRENE) (P1) (CNR)
D008 | SOLPS-ITER modelling of DTT DN (closed) divertor with and without dome with drifts activated (using EIRENE) (P3) (UNITUS)

## Slide 3: SP ADC Tasks 2021/2022
Tasks have been summarized in three different topics:
Selection of the best divertor shape for SN, XD (and their long legs variants) between narrow (closed) and wide (open) divertor
Analysis of single null configuration without and with dome using SOLPS-ITER with kinetic neutrals and activating drifts
Analysis of DN configurations with the divertor shapes resulting from previous activity symmetrized up/down

## Slide 4
Selection of the best divertor shape for SN, XD (and their long legs variants) between narrow (closed) and wide (open) divertor

## Slide 5: Magnetic equilibria for different divertor shapes
XD – 4.5 MA
SN – 5.5 MA
XD – 4.5 MA
SN – 5.5 MA
XD – 4.5 MA
LXD – 4.5 MA
LSN – 5.5 MA
SXD – 4.5 MA
ND
WFD
A set of magnetic configurations have been produced for all divertor shapes using coils external to the vessel
The ND has parameters similar to present DEMO divertor design
The WFD allows configurations with long external legs (LSN & SXD)
The WFD with an appropriate wall allows negative triangularity configurations

## Slide 6: Divertor parameters
Device | LIT/Rx | LOT/Rx | aIT | aOT
DTT (ND) | 0.09-0.15 | 0.15-0.17 | 2.0° | 1.9°
DTT (WFD) | 0.07-0.14 | 0.24-0.34 | 1.6°-2.0° | 2.0°-2.3°
DEMO | 0.15 | 0.21 | 1.5° | 1.6°
ITER | 0.19 | 0.20 | 3.2° | 2.7°
JT-60SA | 0.21 | 0.29 | 5.6° | 3.5°
Narrow divertor is similar to (present) DEMO divertor in terms of legs length and grazing angle
Wide divertor can test a wide range of leg lengths
In general grazing angle is in between ITER and DEMO
SN configuration
Divertor | LIT/Rx | LOT/Rx | aIT | aOT
DTT (ND) | 0.09-0.11 | 0.11-0.14 | 0.6° | 0.0-0.2°
DTT (WFD) | 0.10-0.11 | 0.10-0.25 | 1.1°-1.2° | 0.3°-0.6°
XD configuration

## Slide 7: Assessment of divertor performance
Edge modeling of a representative set of magnetic configuration:
  SN in pure D power scan with PSOL=3.5÷25 MW with five different divertors and different transport parameters and with sub-divertor modeling
  XD in pure D power scan with PSOL=3.5÷8 MW with five different divertors
  SN scan in neon and argon seeding at full power PIN=30 MW with four different divertors and different transport parameters (a few cases), with sub-divertor and variation in transport parameters
  XD scan in neon seeding at full power PIN=30 MW with four different divertors
Comparison of performance with the narrow divertor
Gas puffing and top pedestal density estimation – core/edge integration

## Slide 8: D modeling: profiles at outer mid-plane PSOL=3.5-25 MW
Same separatrix density
Different top pedestal density (higher/lower pumping efficiency  higher/lower gas-puffing)
Highest top density in SN
Lowest density in XD (open markers)  low pumping efficiency due to strike points far from pumps slots
Higher top temperature in XD due to lower density
Higher separatrix temperature in XD due to longer connection length

## Slide 9: D modeling: SN profiles at targets / temperature
In pure D with the wide divertor detachment is obtained below PSOL≈7 MW at nsep=7·109 m-3
The narrow divertor is still attached at the same PSOL
Detachment threshold
Inner target
Inner target
Outer target
Outer target

## Slide 10: D modeling: SN profiles at targets / heat flux
Inner target
Inner target
Outer target
Outer target
In pure D with the wide divertor detachment is obtained below PSOL≈7 MW at nsep=7·109 m-3
Peak heat flux is well below 10 MW/m2
Similar conditions at both targets (but drifts not included)
The standard divertor provides worst performance  higher temperatures and peak heat fluxes

## Slide 11: Operation at full power with seeding
Evaluate minimum requested contamination to achieve detachment
Evaluate operative window in impurity content
Configuration stability against operating condition

## Slide 12: Full power: profiles at outer mid-plane
Higher core density with argon
Higher core temperature with neon
Higher temperature at separatrix with neon (related to NeAr cooling properties)
PIB = 30 MW (10 MW rad. in the inner core, 5 MW ELMs)
PIB splitted between e and D to achieve similar temperatures
nsep=8∙1019 m-3
PSOL=PIB-Prad,in (must be > 18-20 MW to access H-mode)
SN
SN

## Slide 13: Full power: summary of results
Full power modeling with PIB=30 MW at fixed separatrix density nsep=8·109 m-3 with neon (and argon) seeding to achieve detachment
The wide flat divertor performs relatively well for all configurations
The wide flat divertor performs better (lower Zeff and Cinp) than the standard narrow divertor in SN and XD
Argon performs better than neon in terms of <Zeff>sep and impurity concentration (Cimp) for both divertors
In the wide flat divertor SXD provides similar result than SN

## Slide 14: Standard/narrow divertor – XD with neon
Fast cooling of legs
Radiation localize at the x-point
Most radiation inside separatrix
Seems unable to sustain H-mode
<Zeff>sep=2.4
Prad,tot=28 MW
PSOL=8 MW
CNe=3.6%
<Zeff>sep=4.5
Prad,tot=25 MW
PSOL=21 MW
CNe=7.3%
XD configuration easily falls down to X-point radiator
H-mode condition can be recovered but at high impurity concentration
Can sustain H-mode

## Slide 15: Conclusions
A divertor shape able to accept many magnetic divertor configuration has been studied and optimized by the edge code SOLEDGE2D
The wide divertor can provide reliable operation for SN and XD configurations in pure deuterium at reduced power and with seeding at full power
The wide divertor provides better exhaust performance than a standard narrow divertor
With the designed pumping aperture it provides a high pumping capability for the SN configuration, less for the XD one
Results depend on transport parameters, different values for impurities or at different density can affect final conclusion
Fine tuning on magnetic configurations (strike point position, separatrix distances) can also affect results

## Slide 16
Analysis of single null configuration without and with dome using SOLPS-ITER with kinetic neutrals and activating drifts

## Slide 17: Dome studies
SOLPS-ITER with EIRENE (two different fluid meshes)
Drift and currents considered
EIRENE mesh extends in the subdivertor region
Neutral – neutral collision
Fixed albedo to get S = 120 m3/s at the Port 5 entrance (S = 100 m3/s at the at the subdivertor entrance)
D puff (from equatorial plane) and Ne puff (from Private region) adjusted to get ne,sep=8·1019 m-3 and desired outer target conditions

## Slide 18: Dome studies objectives
Assessment of the effect of dome in DTT reference scenario with drift activated
Previous studies on ITER without drifts (Kukuskhin 2002,2007) have shown the dome effect on neutral compression and of the connection between inner and outer target
pplenum
Dome
Flat plate
Evaluation of the inner and outer divertor conditions (drifts on)
Evaluation of inner/outer power asymmetry
Effect on impurities retention
Estimate of neutral pressure (neutral-neutral collision)
Effect on the pumping capability

## Slide 19: D modelling: effect of drifts
Drifts tends to increase the asymmetry between LFS and HFS
Net flux of particles from outer to inner target  ne,IT Te,IT
In attached condition the difference is more pronounced since the inner-outer neutral connection is less important
Most important effect on IT, negligible on OT
Small effect of the drifts on the general trends difference between flat and dome
Inner target
Outer target

## Slide 20: D modelling: pumping without/with dome
Increased neutral trapping w/ dome
Higher D throughput in case of dome by 30%
Increased sub divertor neutral pressure by < 2
Same trends in power scan both w/ and w/o drifts
Slight increase in the pressure estimate in drift simulations

## Slide 21: Dome effect on divertor with Ne
  The effect of dome is small in terms of detachment achievement
  The increased connection between inner and outer target with the flat plate slightly improves the divertor performance
  Most stringent limit related to temperature
Inner target
Outer target

## Slide 22: Full power: Ne seeding
  The power radiated in the dome and flat is similar to get the same outer target conditions (few % slightly higher with flat plate)
  In detached condition the radiation front moves towards the X-point
  The dome moderately improves the performance in terms of main plasma pollution
  Ne leakage is underestimated without drifts (ExB poloidal velocity)
+29%
+51%
+21%

## Slide 23: Full power: pumping
  Similar trends for Deuterium puff and pressure as in pure D cases (slightly increase in dome geometry)
  Strong effect on the Ne neutral due to the better trapping:
    Increase in the pressure by a factor 5
    Increase in the Ne puff by 10
  Dome considerably outperforms neutral Ne impurity confinement in the subdivertor region
  Better controllability and Ne pumping capability with the dome

## Slide 24: Conclusions
Dome studies show (in accordance with previous ITER studies):
  Small impact on the performance in terms of divertor performance
  Strong effect is seen on the impurity pumping capability suggesting the need to ensure a good trapping of the Ne (keep the subdivertor slots close to the Outer strike point)

## Slide 25
Analysis of DN configurations with the divertor shapes resulting from previous activity symmetrized up/down
(preliminary due to a delayed starting of the activity)

## Slide 26: DN equilibria
SP1
SP2
SP4
SP3
Ne
Ne
Ne
Ne
DN
DXD
DNLL
#6 | DN | DXD | DN with long Leg (DNLL)
[MA] | 3.8 | 2.5 | 3.5
[T] | 6 | 6 | 6
[MW] (Electron/Ion, total) | 18 (e), 12 (i) | 18 (e), 12 (i) | 18 (e), 12 (i)
Core D (part/s) | 1.1e20 | 1.1e20 | 1.1e20
Puffing D (part/s) | 8.3e22 | 1.1e22 | 17.5e22
Puffing Ne (part/s) | 9.5e20 | 5.3e20 | 9.0e20
Pumping(D,Ne) () | 200. (50 per slot) | 200. (50 per slot) | 200. (50 per slot)
#6 | DN | DXD | DN with long Leg (DNLL)
 | 3.8 | 2.5 | 3.5
 | 6 | 6 | 6
 | 18 (e), 12 (i) | 18 (e), 12 (i) | 18 (e), 12 (i)
Core D (part/s) | 1.1e20 | 1.1e20 | 1.1e20
Puffing D (part/s) | 8.3e22 | 1.1e22 | 17.5e22
Puffing Ne (part/s) | 9.5e20 | 5.3e20 | 9.0e20
 | 200. (50 per slot) | 200. (50 per slot) | 200. (50 per slot)

## Slide 27: Full power: Ne seeding (not stationary)
DN
DXD
DNLL
Ne
D-new
0.8
OMP
Ne

## Slide 28: Full power: Ne seeding (not stationary)
# | DN | DNLL
(MW) | 25 | 23
 | 4.3 | 3.2
 | 3.6 | 1.9
# | DN | DNLL
 | 25 | 23
 | 4.3 | 3.2
 | 3.6 | 1.9
The DN Ne concentration is reducing
DNLL
DN
High radiation along the long leg
Stable radiation around the x-point
sp4
sp3
sp4
sp3
sp1
sp2
sp1
sp2

## Slide 29: Conclusions
The three cases are still running, they need time to convergence, cause by the low time step.
It necessary to define criteria to compare this case with the SN reference, cause by different plasma current .

## Slide 30
Thanks

## Slide 31: Modelling methods and edge code
Transport parameters [*]:
  based on heat flux decay length lq,u≈1.5 mm for the SN in attached condition in agreement with Eich scaling;
  Profiles from JET/C-Mod experiments modelling;
  Two options for divertor region
  Equal for SN, XD and all divertor shapes
Seeding with neon and argon
Fixed pumping speed S=100 m3/s  gas-puffing adjusted to achieve target separatrix density
Not considered drifts and neutrals-neutral collisions
SOLEDGE2D-EIRENE 2D edge fluid/kinetic code
Targets:
  same separatrix density
  about same radiation (with seeding)
  H-mode condition  PSOL≥18 MW
Transport profiles
[*] L. Balbinot et al., NME 34 (2023)

## Slide 32: Wide flat divertor - SN
Neon seeding
Argon seeding
Argon provide better results than neon with similar radiation in the core
Radiation is concentrated on divertor legs
Longer legs provide larger radiative volume, better performance
<Zeff>sep=2.8
Prad,tot=23 MW
PSOL=24 MW
CAr=1.0%
<Zeff>sep=2.9
Prad,tot=22 MW
PSOL=26 MW
CNe=2.8%

## Slide 33: Wide flat divertor - XD (short and long leg)
Short leg XD
Longer leg LXD
A Longer leg provide better results
<Zeff>sep=3.6
Prad,tot=27 MW
PSOL=24 MW
CNe=4.6%
H-mode operation is possible with a reasonable impurity content
<Zeff>sep=3.4
Prad,tot=25 MW
PSOL=24 MW
CNe=3.4%

## Slide 34: Long leg configurations with neon
Long leg SN
Long external legs provides a bigger radiative volume reducing request on impurity
But top wall must be moved upward (or equilibrium must be improved)
< Zeff>sep=3.0
Prad,tot=24 MW
PSOL=26 MW
CNe=2.3%
<Zeff>sep=2.9
Prad,tot=25 MW
PSOL=25 MW
CNe=1.9%
Long leg XD (SXD)
SXD provides less impurity content in the core thanks to a higher top pedestal density

## Slide 35: 2D transport parameters map
Transport parameters have been normalized to Bt - Two options for the divertor region:
Value as in the OMP far SOL (as in the JET/C-Mod modeling)
Values like at OMP
Transport in divertor region as at the OMP far SOL
Transport in divertor region like at OMP