## Slide 1
D. Borodin
on behalf of the TSVV-5 team
WP PWIE meeting
6-9 February 2022
TSVV-5: Neutral gas dynamics in the edge

## Slide 2: TSVV-5: Neutral Gas Dynamics in the Edge
Neutral gas code that allows for an efficient use of HPC resources (towards exascale systems and/or HPC booster techniques) through suitable parallelization methods.
Revised and extended physics basis for the neutral gas model. Further development of the underlying collision-radiative model towards the full vibrational resolution for all hydrogen isotopes and specific impurities for seeding.
Improved (in contents and structure) Atomic and Molecular database for volumetric and surface processes. Database access through generalized interfaces to, e.g., atomic, molecular, nuclear and surface (AMNS) physics data.
Interfaces and boundary conditions necessary for future applications; modularization of the neutral gas code to facilitate coupling to computation fluid dynamics (CFD) codes (2D or 3D codes, turbulence codes, time-dependent) and possibly also to gyro-kinetic/gyrofluid plasma codes.
Strategy towards a validated predictive capability for integrated fusion reactor modelling for (semi-)detached divertor plasmas. Liaison with TSVV Tasks 3 and 4.
Neutral gas code that allows for an efficient use of HPC resources (towards exascale systems and/or HPC booster techniques) through suitable parallelization methods.
Revised and extended physics basis for the neutral gas model. Further development of the underlying collision-radiative model towards the full vibrational resolution for all hydrogen isotopes and specific impurities for seeding.
Improved (in contents and structure) Atomic and Molecular database for volumetric and surface processes. Database access through generalized interfaces to, e.g., atomic, molecular, nuclear and surface (AMNS) physics data.
Interfaces and boundary conditions necessary for future applications; modularization of the neutral gas code to facilitate coupling to computation fluid dynamics (CFD) codes (2D or 3D codes, turbulence codes, time-dependent) and possibly also to gyro-kinetic/gyrofluid plasma codes.
Strategy towards a validated predictive capability for integrated fusion reactor modelling for (semi-)detached divertor plasmas. Liaison with TSVV Tasks 3 and 4.
Code performance, parallelization, refactoring, domain decomposition, I/O for HPC, …
Improved physics and features incl. fluid-kinetic hybridisation (FKH) and improved CRMs
Improved AMNS data, both in structure/physics and content
EIRENE as NGM – restructuring, interfaces to other codes, time-dependent runs, kinetic ions
Validation with experiments and test of predictive capabilities for ITER and DEMO
Main simulation tool:
EIRENE code (and EIRENE-CFD packages) http://www.eirene.de/
We aim to transform it to IM- and HPC-ready neutral gas module (EIRENE-NGM) suitable for simulations on ITER and DEMO scale with large focus on (semi)detached divertor plasmas
FP-9 deliverables:

## Slide 3: EIRENE-NGM-DEVELOPERS (TSVV-5)
D.V. BORODIN, F. Cianfrani, S. Wiesen, D. Harting, P.Börner, B.Küppers
Forschungszentrum Jülich, Institut für Energie- und Klimaforschung – Plasmaphysik, Germany
W. DEKEYSER, S. CARLI, M. BLOMMAERT, N. HORSTEN, W. VAN UYTVEN, M. BAELMANS
KU Leuven, Department of Mechanical Engineering, Belgium
B. MORTIER, G. SAMAEY, ..? E. LOEVBACK ?..
KU Leuven, Department of Computer Science,Belgium
Y. Marandet, P. Genesio
Aix-Marseille Univ., France
H. Bufferand
CEA, IRFM, France
E. WESTERHOF, J.G. MUNOZ
DIFFER - Dutch Institute for Fundamental Energy Research, Eindhoven, the Netherlands
M. GROTH, A. HOLM , A.CHanDRA
Department of Applied Physics, Aalto University, Espoo, Finland
H. LEGGATE  HLST, ACH-MPG
DCU
Eirene with the infant Ploutos
ACH-VTT:
F. Granberg, J. Åström
O.LaPPI
ACH-IPPLM:
D.Yadykin
Yu.Yakovenko

## Slide 4
Contributions to “all bells and whistles ITER run”
KUL
CEA
FZJ
DIFFER
Aalto
Adjoint approach
Time-resolved
1) FE model for divertor target and FW
2) detachment in transients
3) Validatrion at Magnum-PS
ITER scenario with semi-detachement
Optimized massive parallelisation including domain decomposition
Reduced model AMNS data
NGM with interfaces
1) AMNS data structure and content 2) New CRMs for molecules (isotopes, resolution by rovibrational states)
3) Code development and maintenance
4) Kinetic ions
Code Modulisation
Validation:
spectroscopy/bolometry at JET and MAGMUM,
reduced models for isotopes in FW, outgassing etc.
Only joint effort makes it realistic on the 5 year time scale!

## Slide 5
Contributions to DEMO simulations
KUL
CEA
FZJ
DIFFER
Aalto
Adjoint approach
FE model for divertor target and FW
DEMO simulations
Optimized massive parallelisation including domain decomposition
Reduced model AMNS data
NGM with interfaces
1) AMNS data structure and content 2) New CRMs for molecules (isotopes, resolution by rovibrational states)
3) Code development and maintenance
4) Kinetic ions
Code Modulisation
Validation:
spectroscopy/bolometry at JET and MAGMUM,
reduced models for isotopes in FW, outgassing etc.
Fluid-kinetic hybridisation (FKH)
Only joint effort makes it realistic on the 5 year time scale!

## Slide 6: Recent progress with FKH (JET L-mode case)
Purely micro-macro (mM) approach for rectangular slab geometry with fixed background plasma
Micro-macro approach combined with spatially hybrid approach (Sp-mM)
• Realistic geometry with void regions
• Coupling to kinetic molecules
• Coupled plasma-neutral simulations
N.Horsten et al., PET-2021, CPP-2022
2021

## Slide 7: FKH Progress 2022 summary
The fluid, (SpH) hybrid and kinetic neutral models were validated with a realistic JET ILW L-mode plasmas cases [2]
  This not a slab, but a realistic tokamak configuration, incl. voids, molecules, …
  Large fluid-kinetic discrepancies at low density (factor 2), but smaller discrepancies at higher density (50%)
  Fluid-kinetic discrepancies in both density regimes successfully corrected by hybrid approach
Drift and n-n effects are successfully introduced
Alternative hybrid approach that avoids cancellation errors by construction under development. Hilbert expansion based fluid model derived; both diffusive & hydrodynamic scaling investigated [V. Maes, paper in preparation]
Release of fluid and hybrid approaches in extended grids version of SOLPS-ITER to the community during dedicated workshop hosted in KU Leuven, November 14-18

## Slide 8: Code development – version merging
The main focus with regard to development of the EIRENE code in 2022 was on reuniting the various diverging versions of the code used in FZJ and at ITER.
Roughly 20 different code versions have been analysed and merged together. Thereby taking advantage of developments provided by FZJ external developers.
These developments include
  Charge state bundling
  Parallelization of the code using shared memory techniques (OpenMP)
  Extensions of the existing parallelization of the code with message passing techniques (MPI) by implementation of different parallelization schemes.
  Introduction of radiation tallies
  Implementation of species resolved volume averaged tallies and their use with species specific rescaling of calculation results in order to improve the particle balances.

## Slide 9: Code development - priorities
Initially version-specific code has been generalized in a way it can be used by all the interested parties (RU or specific architecture related code removed).
All changes to the code are carefully tested (still ongoing!..).
Code modifications affecting simulation results were tracked down to their origin and the reasonability investigated.
Updated reference outputs are provided for the testcases in the continuous integration chain (CI).
We are approaching the 1st milestone release of the code, which should be a basis for further joint development

## Slide 10
EIRENE licencing - User Agreement (UA)
Old UA
acknowledgement of FZJ origin of EIRENE, non-military use, non-commercial use, no cost/liability for FZJ, etc.
www.eirene.de/new_eirene
New UA “EPL (EIRENE public license)”
Based on copyleft licence (however GPL3.0 occurs to be not suitable).
Similar declarative statements as in the old UA.
More clear statement about the EIRENE-based publications.
Developers and users are divided into “basic” and “associated” ones (AD).
NEW: commercial use of executable for any AD group.
 ADs get more rights on decision-making, direct access to the repository, etc.
ADs must keep to the “Developer Code of Conduct” (see at INDICO).
Current status: License is generally ready… and is now part of the source

## Slide 11: CRM solvers available
CRM (technically) = reaction data + SOLVER
Most solvers solve algebraic stationary system of equations
in such cases the solver is much less valuable as the A&M data collection
this statement is underlined even by the developers of the very well established and mostly up-to-date YACORA model
CRM containing molecular species is even more complex, e.g. one needs to track more processes and more states (vibrational, rotational).
Tracking all the states as separate species demands enormous CPU and memory resources.
EIRENE pre-calculates rates for each volume cell. It also allows to pre-calculate values for various Ti/Te ratios.
D.Wünderlich and U.Fantz,
Atoms 2016, 4(4), 26

## Slide 12
Te
Ti=TH+
TH
TH2
SOLPS-ITER basic simulation case for EU-DEMO
Below X-point:
Te=Ti=10eV
T(H)=T(H2) =10eV
Ne ~ 10e18 m-3
N(H)=10e20 m-3
F.Subba et al.,
NF 61 (2021) 106013

## Slide 13
SOLPS-ITER basic simulation case for EU-DEMO
F.Subba et al.,
NF 61 (2021) 106013
ne
NH
These are semi-detached conditions (1 point)
  Attached vs. detached + 2-3 semidetached cases would be wishful to have!
  We use EIRENE or standalone CRM to identify spectral features useful for the degree of detachment control for this plasma conditions
We can run (and mean to in future!) full EIRENE: SOLPS with a “frozen” fluid side (B2.5)
  This option is not mature enough for meaningful physics results
  We use standalone CRM and vary consrtant plsma conditions around
Below X-point:
Te=Ti=10eV
T(H)=T(H2) =10eV
Ne ~ 10e18 m-3
N(H)=10e20 m-3

## Slide 14: COLLISIONAL-RADIATIVE MODEL
Reaction | Type | Source
H2 + e → H2+ + e + e | molecular ionization | H2vibr
H2 + e → H2(btriplet) → H + H + e | neutral dissociation | H2vibr
H2 + e → H + H+ + e + e | dissociative ionization | Amjuel
H2 + H+ → H2+ + H | charge exchange (CX) | H2vibr
H + e → H+ + e + e | ionization | Amjuel
H2+ + e → H + H+ + e | neutral dissociation (MAD) | Amjuel
H2+ + e → H+ + H+ + e + e | dissociative ionization (MAI) | Amjuel
H2+ + e → H + H | dissociative recomb (MAR) | Amjuel
H+, H, H2+,H2
Particle species
Molecular source:
Reference value
Plasma parameters:
Fixed electron and ion densities:
ne = ni = 1019m-3 for [1]
ne = ni = 1021m-3 for [2]
Temperature: Te = Ti = 0.2÷30eV.
H+, e sinks (reservoirs)
EU-DEMO
JET
[1] M Groth et al. NF 2013 [2] F Subba et al. NF 2020

## Slide 15
YACORA: inclusion molecular source term
Stationary run vibrationally resolved:
Particle species
Reactions
H2 source term
proton impact
electron impact
vibrational transitions
electron impact
F.Cianfrani,
EPS-2022
YACORA + Source term
adjustable to the Edge2D-EIRENE

## Slide 16: СRM simulations (standalone): branching ratios
low temperature (T < 2eV) leading reaction chains:
MAR/MAD competition at very low temperature
MAD
MAR
EU-DEMO
H2+H+→ H2++H H2++e → H+H++e
H2+H+→ H2++H H2++e → H+H

## Slide 17: CRM: effect of vibrationally resolved states
vibrationally resolved molecular states H2(v) (v=0 ..14) with electron-induced ladder-like trans H2(v) + e → H2(v±1) + e rates H2vibr
vibrational transitions are the main reaction channels at low temperatures
EU-DEMO
F.Cianfrani et al.,
EPS-2022

## Slide 18: EU-DEMO – effect of resolution by vibrostates
F.Cianfrani et al.,
EPS-2022
A.Holm, M.Groth, et al.,
PET, CPP 2021
Fully in line with the EIRENE and other CRMs:
“Up to 40% reduction in effective dissociation rate due to transport of vibrational states”

## Slide 19: CRUMPET, YACORA simulations (standalone CRM)
Different CR processes cause up to 60% difference in dissociation rates
Impact strongest in the Te = 0.5–4 eV range, where molecular processes strongest
Electronic transitions affect Te > 4 eV
Vibrational transitions affect Te < 4 eV
Predicted isotope effect strongest for temperatures associated with detachment onset and detached conditions
MCCC data indicates weaker dissociation of both H2 and D2 for Te > 3 eV compared to EIRENE data (AMJUEL, HYDHEL, H2VIBR)

## Slide 20: Isotop effect in „full-scale“ EIRENE (M.Groth)
Higher div. densities for T than for H plasmas observed in
JET-ILW L-mode plasmas, both exp. and in EDGE2D-EIRENE
Generic density scan with identical transport coeffs., models
Strong reduction in ion current to outer plate not yet reproduced ⇒ likely to require changes to transport coefficients
Te,OT least affected by isotope species

## Slide 21: CRM: effect of Te on vibrational populations
ground state: Boltzmann distribution
SOURCE
X
ν = 0
ν = 1
ν = 2
ν = 3
ν = 4
ν = 5
diss./ ion.
Tvibr increases with decreasing Te
peak at low Te

## Slide 22: CRM vs EIRENE: vibr. Resolved – statistics issue
Simulations: molecular source
disagreement for the population of vibr. excited states
EIRENE: 793’300 histories
EIRENEx10: 7’933’000 histories
EIRENEx100: 79’330’000 histories
ν
ν
JET shot 81472
Gas puffing v=0
Reflection model (wall as a catalyst surface) v=0
One needs to

## Slide 23
HYDKIN (web-based A&M data tool):
toolbox for plotting and manipulation of A&M data with a user-friendly graphical interface.
includes EIRENE databases: AMJUEL, HYDHEL, H2VIBR, METHANE, .. .
available at http://www.eirene.de/hydkin/
Password-protected (for access contact the authors).
D.Reiter et al.,
Phys. Scr. 2009
F.Cianfrani et al.,
ICAMDATA-2022

## Slide 24
HYDKIN: particle solver (non-stationary)
Development of stationary equilibrium
Default case (see next slides)
reservoir
“infinite reserve” of particles at fixed temperature and density

## Slide 25
HYDKIN: what is inside?..
CRM solver (transport excluded, pure A&M side of the problem) with extensive features
  Stationary and non-stationary solution (assuming velocity and plasma pars)
  Any specie can be treated as “Reservoir”
  “Spectral analysis” based on eigenvalue approach (which reactions are most important?)
  Sensitivity analysis – vary the plasma parameters, solver settings, reactions, etc.
Plotting, solver results visualisation
  Useful for fast consistency checks and trivial analysis while constructing the CRMs
  Good for physics analysis in case one follows established routines
Flexible reaction tables interconnected with the solver and plotting
  Useful for fast consistency checks and trivial analysis while constructing the CRMs
  Good for physics analysis in case one follows established routines
  Input/output in various formats (new: JSON) including directly for EIRENE

## Slide 26
HYDKIN: using the power of the web-interface
For H2 case (example):
The basis table is highly customisable:
  Deselected reaction can be excluded from the view
  User easily selects the level of info for each reaction to be shown
  Basic, solver, plotting etc. tables are interlinked
All is optimised for checking high amounts of similar data
  Critical things are highlighted
  Data is grouped by the reactions (even if comes from various sources)
  One can start with initial configuration (standard or custom) and do only essential (e.g. from physics) changes

## Slide 27
HYDKIN – new mode (H2 case)
Buttons to adjust table content

## Slide 28
HYDKIN: comparison dissociation rates
HYDHEL
AMJUEL
Factor 3 wrong
e + H2  H + H + e

## Slide 29: new HYDKIN:
New HYDKIN:
Activities:
grouping of reactions: easier comparison btw data from different sources
new column/features: sparse information now available
default cases: testing purposes and model for molecular decay
json output: reusability for new solver runs and other codes (EIRENE)
continue improving readability and usability.
write code for generating EIRENE input file (block 4) from json output (also good for consistency check).
we want to promote .. [HYDKIN] .. as a standard pre-processing tool for Eirene:
Conclusions Eirene Code Camp 22

## Slide 30
New HYDKIN can be used to
to import/export data (JSON, tabular and other formats)
to produce input data for EIRENE and for other codes
to check data for consistency, abnormal features, etc.
to check and improve the results of the simulation
to understand A&M side of the problem and identify the most significant processes (among the selected ones)
to load/improve/save the developed configuration (selected reactions and parameters) including starting from the standard “default” pre-sets
EIRENE Code Camp 2022: we want HYDKIN to substitute certain EIRENE routines in data preparation (JSON) with consistency checks.
Reactions are grouped in the tables optimised for this kind of work

## Slide 31
Summary for CRMs
CRM improvement is very significant part of the EIRENE development
  It is key to identify useful spectroscopic features for RT control of detachment.
HydKin is largely updated and foreseen to be the main A&M pre-processing tool
  All the development is ongoing in a view of future massive data extension
  It is meant to provide flexible adjustment of CRMs and auto generation of EIRENE input
Application to the EU-DEMO case (P.Subba) shows that
  Even standalone model is useful to understand the critical branching ratios
  Tracking of vibrational states is essential
  We have agreed with P.Subba on the basic degree of detachment scan, but this for now an elaborate

## Slide 32
Thanks for the attention!

## Slide 33: New CRM Solver for EIRENE concepted
This CRM is aimed to precompute rate coefficients accounting for all parametric dependences (ne, Te, but also Ti, …) in contrast with currently used polynomial fits (AMJUEL, …) + add a number of levels/processes not accounted for at this time
The internal states (e.g. rovibrational states in molecular species) are to be tracked with a flexible a flexible control over this resolution (as separate specie or variable).
The nonstationary solution for balance equations should be the default one
(with the stationary only as a useful option).
The solver should be modular, thus usable standalone or even in other codes.
The improved A&M data input should be readable and structured (for starters JSON, potentially also HDF5). It should be pre-processed mostly automatic and easily exchanged with other codes and tools. We need tools for visualisation and testing.
  The only way to meet the exploding amounts of data from RMPS and CCC for molecules (with resolution by rovibrational states)
  IAEA GNAMPP assists, but also reveals the challenges AMD Unit: GNAMPP
Not only performance and reliability to be improved, however including additional physics can be provided!