## Slide 1: Disruption modelling w/wo stabilizing plates
G. Rubinacci, F. Villone & CREATE team

## Slide 2: Outline
Disruption simulations
  Activities carried out
  Planned activities
  Possible manning and support to IC
AVDEs
  Simplified modelling
  Estimate for JT-60SA

## Slide 3: Planned activities & status
Planned activities on disruption modelling in support of IC (Jan 2020)
  Task 1. Assessment of the available 3D geometrical description of JT-60SA
  Task 2. Derivation of an updated 3D finite elements mesh
  Task 3. Disruption simulations and post-processing (force & halo calculations)
  Task 4. Definition of set of tests to calibrate the model with the available halo and magnetic sensors
Current status (March 2020)
  Task 1. Completed
  Task 2. Completed
  Task 3. Ongoing
  Task 4. Scheduled

## Slide 4: Disruption simulation approach
If some of the operational limits are exceeded, a rapid growth of a MHD instability makes the plasma lose most of its thermal energy
  Thermal Quench (TQ)
  A current density profile flattening takes place
  The plasma current increases, experiencing a spike
Immediately after, the plasma cools down and its resistivity increases, so that the plasma current drops to zero
  Current Quench (CQ)
  Supposed linear in time on a time scale following empirical scaling laws
This may cause the vertical position feedback to lose control of plasma, giving rise to a Vertical Displacement Event (VDE)
  The plasma eventually hits the wall, injecting currents directly in the structures (halo currents)
This event has been modelled using the CarMa0NL code
  Axisymmetric plasma under the evolutionary equilibrium assumption, in presence of 3D conducting structures

## Slide 5: Computational tool
CarMa0NL: able to describe the evolutionary equilibrium of axisymmetric plasmas, in presence of three-dimensional volumetric conducting structures
Time scale of interest is supposed much longer than Alfvèn time
  Plasma mass can be neglected
  Plasma moves through equilibrium states
The formulation uses a coupling surface to describe the electromagnetic interaction between the plasma and the conductors
  The most convenient formulation can be used in each domain
Inside : plasma evolutionary equilibrium
Outside : eddy currents in 3D structures
On : suitable coupling conditions

## Slide 6: 2019 activities
Prior to 2019, several disruption simulations in presence of stabilizing plate have been carried out
  Not reported here
In 2019, a case with no stabilizing plates has been considered [G Giruzzi et al 2020 Plasma Phys. Control. Fusion 62 014009]
  Same equilibrium and wall configurations, only stabilizing plate removed
The plasma is forced to move downwards with a current step in PF coils until it hits the wall
  TQ in 3 ms, linear CQ in 12 ms

## Slide 7: 3D meshing
A detailed 3D mesh of the vacuum vessel has been produced
  Removing the passive plate, the main stabilizing effect is provided by vessel, so a rather detailed mesh is needed
  This is also needed for breakdown modelling activities (see Mattei’s presentation – Thursday)
Problem: the vessel is not periodically symmetric
  Ports do not replicate with an exactly periodic geometry
Approach used
  One mesh covering 60° toroidally and fictitiously replicated with rotational symmetry
  One mesh covering 360°, reproducing the actual situation

## Slide 8: 3D meshing
Time constant [ms] | Harm. | Notes
88.6 ms | n=0, m=0 | Toroidally directed current
80.7 ms | n=0, m=0 | Poloidally directed current
53.9 ms | n=0, m=1 | Up-down antisymmetric (vertical plasma motion)
35.6 ms | n=0, m=1 | Inboard outboard antisymmetric (radial plasma motion)

## Slide 9: 3D meshing

## Slide 10: 3D mesh

## Slide 11: Disruption simulation
Starting equilibrium configuration: Upper Single Null, high beta

## Slide 12: Disruption simulation

## Slide 13: Disruption simulation
Next steps
  Include halo currents
    First wall geometry?
  Use 360° mesh
    Necessary? It is computationally demanding
  Computation of forces on structures
    Post processing of existing simulations
  Inclusion of simulated magnetic measurements
    3D positions needed

## Slide 14: Manning
Accepted manning on 3D electromagnetic modelling in support of IC
  Disruption modelling + 3D breakdown activities (see Mattei’s presentation on Thursday)
Current status
  Around 40-50% off site time used up to now for
    3D model production, 3D model assessment, simulation set up, simulation execution
  Remaining 50-60% off site time needed for
    Refinement of simulations, post-processing, magnetic measurements (see above)
    Specific modelling activities in support of IC (see below)
Name | PM on site 2020 | PM off site 2020 | PM on site 2021 | PM off site 2021
F. Villone | 0 | 0.5 | 0.5 | 0.5
V. Scalera | 0 | 1 | 0 | 0.5
N. Isernia | 0 | 1 | 0 | 0.5
G. Rubinacci | 0 | 1 | 0 | 0

## Slide 15: Manning
No on-site activity approved for 2020 for the members of the team
  Specific modelling activities to be carried out on site will be postponed
  A direct link is missing with the experimental facility: we need someone on site taking care of this!
    Understand experimental needs and priorities
    Receive specific modelling requests in support of IC
  Examples of 3D electromagnetic modelling activities in support of IC
    TF ripple studies
    Estimate of the effects of coil misalignement
    Prediction of performance of magnetic sensors in nominal conditions (e.g. misalignement of pick-up coils; effect of 3D path of flux sensors; etc.)
    Prediction of performance of magnetic sensor in off-normal conditions (e.g. Rogowski coils measurements during disruptions; halo currents measurements; etc.)
    Modelling support to the planning of dedicated experimental campaigns for magnetic sensor commissioning

## Slide 16: AVDE modelling tool
Surface Kink Source (SKS) model
Simplified modelling tool to evaluate maximum sideway force due to external kink perturbation
  An «engineering-oriented» model
    Based on very basic assumptions (see the following)
    Focus on the «external» effects of AVDEs (maximum sideway force)
  NOT a «physical» model of disruption
    No attempt to reproduce the actual plasma evolution
    No attempt to understand what is happening inside the plasma
Only basic assumptions are made
  Maxwell equations
  Quasi-static plasma evolution
  No plasma rotation
  No plasma-wall contact
    No halo: force due to external plasma kink only

## Slide 17: Surface Kink Source (SKS) model
We start from a reference plasma axisymmetric equilibrium configuration, surrounded by a conducting vessel with arbitrary geometry
We introduce an axisymmetric shell located inside the vessel in the proximity of the plasma; a finite elements mesh of this shell is considered
Axisymmetric currents on this shell are computed so as to provide the same magnetic field as the axisymmetric plasma outside.
Two kink perturbations are applied to this shell, with the nodes of the mesh of the shell displaced as follows:
, : poloidal and toroidal angles
nnodes: number of nodes of the shell mesh

## Slide 18: Surface Kink Source (SKS) model
We assume that the kink perturbations vary exponentially in time:
  This induces non axisymmetric currents in the vessel (see figure)
  Note that  and 0r are «parameters» of SKS (see the following)
The total magnetic field is
  Coils (TF, PF)
  Plasma
  Eddy currents (due to plasma perturbation)
The interaction of non axisymmetric currents in the vessel with magnetic field gives rise to sideway forces acting on the vessel

## Slide 19: Surface Kink Source (SKS) model
The relative amplitude K of the two modes is found by imposing that the plasma is in equilibrium at each time instant, i.e. the global force acting on the plasma is zero
  This is true on a time scale >> Alfvén time, so that plasma inertia can be neglected  very good approximation for disruption modelling
We numerically impose that the integral of the Maxwell stress tensor over a surface circumventing the plasma is zero

## Slide 20: Application to JT-60SA
Different surfaces needed in the model
  the reference position of the shell
  the surfaces used for the integration of the Maxwell stress tensor
    inside and outside the wall, to compute separately the force acting on the plasma and on the wall
  the wall and the equivalent surface
Also considered a simplified description of the vessel, by assuming a single shell
  The actual meshes cover 360° in the toroidal direction; only a portion is shown for clarity

## Slide 21: Application to JT-60SA
Linear relation between displacement and magnetic field perturbation
Rich poloidal spectrum of the radial magnetic field perturbation

## Slide 22: Application to JT-60SA
Sideways force for a displacement of 5 mm, i.e. a kink magnetic perturbation of  1.8 mT
  One shell (top) and two shells (bottom)
  Maximum sideway force of the order of  2 kN/mT
  This force DOES NOT take into account asymmetric halo currents
  A single mode calculation (i.e. not imposing the equilibrium constraint) results in forces higher of one order of magnitude
Preliminary results - further activities needed
  Assessment of results obtained so far
  Quantification of expected magnetic field perturbation
  Definition of reference equilibrium (USN?)
  Definition of structures of interest (stabilizing plate?)
  Estimate of the effects of halo currents

## Slide 23: Conclusions
Symmetric disruption simulations
  Detailed 3D mesh of the vessel available and running
  Disruption simulation of USN configuration already available and currently under refinement
  Electromagnetic modelling tools ready to support IC
  Possible modelling activities in support of IC identified
  Possible manning planned
AVDEs (asymmetric disruptions) simulation
  Sideways force estimated with simplified engineering-oriented SKS model
  Estimate of such force provided in absence of halo currents
  Further activities needed