## Slide 1: Status of the JT-60SA Massive Gas Injection system
M. Dibon, S. Nakamura, G. Matsunaga, S. Davis, C. Sozzi
Acknowledgement: G. Giruzzi, Y. Kamada

## Slide 2: Outline
Current valve design
Gas preparation system
Vacuum feedthrough
Summary

## Slide 3: Current valve design
Air supply
Closure volume
120V supply
120V supply
Piezostacks
Ceramic valve stem
Copper seal
Injection volume
Disc springs
Nozzle
Kalrez seal
Gas supply

## Slide 4: Current valve design
 | Valve Type 5
Gas reservoir [cm³] | 815
Max. gas pressure [MPa] | 7.2
Max. gas amount [Pam³] | 5868
Max. inj. Particles | 1.4*1024
Opening time [ms] | < 2
Valve plate lift [mm] | 7
Nozzle diameter [mm] | 28
Size l [mm] x b[mm] x h[mm] | 140 x 110 x 292
Piezoelectric stacks | 8
Required air pressure [MPa] | 1.5
Closure volume [cm³] | 53
Valve properties

## Slide 5: Current valve design
Dye penetration test for bellows and pressure test samples at TÜV
No cracks found in welds

## Slide 6: Current valve design
4 times pressure test of bellows performed in Greifswald:
  Front bellows: Ptest = 32.2 Mpa
  Rear bellows: Ptest = 6.05 MPa
No damage found after pressure test

## Slide 7: Current valve design
Documents for application of the bellows to Ibaraki Prefecture sent to QST
  Structural drawing of each bellows
  Structural drawings of each test sample
  Visual inspection certificate of the bellows and test samples before the test
  IPP welder certificate
  Material certificates for every bellows
  Material certificates for each attachment of the test samples
  Qualification of the welding procedure of the bellows
  manufacturer
  Test protocol of dye penetration test
  Test protocol of the 4 times pressure test

## Slide 8: Gas preparation system

## Slide 9: Gas preparation system
Introducing the EPC (Electronic pressure controller) for automated gas mixing
Check valves behind safety valves
Increased mixing volume due to shorter supply lines
Changed pressure gauges (original ones died at AUG)
Compressed air safety valve blows directly into pumping room
  Pumping room radiation monitored
  Air blow off into exhaust line not allowed (H2 in exhaust line)

## Slide 10: Vacuum feedthrough
3 way valve in compressed air line for blow off into torus hall
Changed pressure gauge
PVC support to relieve stress from fittings

## Slide 11: Summary
MGI valve design finished, manufacturing drawings ready and checked by F4E
Pressure test and dye penetration tests of bellows successful
Gas preparation system modified for better automation and safety
Feedthrough flange modified for better structural integrity
MGI valve now under investigation by Ibaraki Prefecture
New gas panel and feedthrough flange under consideration by QST