## Slide 1: Doppler reflectometer in the JT-60SA tokamak Status Report D. Carralero1, T. Happel2, T. Estrada1, J. Martínez, J. García3, E. de la Luna1, T. Tokuzawa4 1Laboratorio Nacional de Fusión Ciemat, Av. Complutense 40, 28040 Madrid, Spain 2Max-Planck-Institut für Plasmaphysik, Boltzmannstr. 2, D-85748 Garching, Germany 3CEA, IRFM, 13108 Saint-Paul-lez-Durance, France 4 National Institute for Fusion Science 322-6 Oroshi, Toki-city, 509-5292, Japan

## Slide 2
JT-60SA research strategy states that:
  “The validation of theoretical models and simulation codes with the aim of establishing a solid basis for the design of ITER and DEMO scenarios is one of the main objectives of the JT-60SA scientific program.”
JT-60SA Research Plan, v3.3 (2016)
Turbulent transport of heat, momentum and particles is a major uncertainty:
JT-60SA will provide not only an increased range of parameters (b, n*, r*, etc), but also qualitatively different situations, closer to ITER/DEMO operational scenarios.
Transport-related extrapolations used by current codes must be validated.
Intro: why a Doppler reflec in JT-60SA?
1 / 7
The main messages of this proposal are:
A DR is a particularly useful diagnostic for this job. Our proposal covers the diagnostic design, implementation, and scientific operation and exploitation.
It is being developed by an interdisciplinary, multinational team including members from both the EU (CIEMAT, IPP, Oxford) and Japan (NIFS/SOKENDAI).
Notes: 2
2
2
2
2
2
2
2
2

## Slide 3: Main Features of a Doppler diagnostic
Turbulence measurements
Good for quantitative analysis: k⊥-selective, radial scans of the amplitude of local density fluctuations. By correlation studies, average size and tilt of turbulent structures can be measured.
Good coverage: by using an steerable mirror, a range of k⊥ values can be probed. Typical values are in the k⊥rs ~ 1-10, appropriated to observe ITG and TEM turbulence.
Good temporal, spatial, spectral resolution: typical values are Dtturbulence < 1 ms, Dr ~ 1 cm, D k⊥ ~ 1 cm-1. Typical radial range covers SOL, edge and core (r > 0.5, see later).
Good comparison to gyrokinetic models: by implementing GK model output in a full-wave code, a direct comparison between simulation and experiment is posible.
Flow measurements
Besides turbulence measurements, DR provides radial scans of the u⊥ of turbulent structures. By estimating vphase using simulations or assuming vphase << vExB , Er profiles can be obtained. This allows for direct comparison between turbulence amplitude and Er shear.
Calculating neoclassical flow contributions in a tokamak, utoroidal can be obtained from u⊥. By this, a DR system can be used to carry out studies in rotation and neoclassical viscosity (regardless of NBI penetration).
2 / 7

## Slide 4
EDICAM
Neutron monitor
Visible TV
Bolometer
Light guide
P18-Horizontal
Basic system description
The most likely position for the DR system would be the P18-Horizontal diagnostic flange.
The bottom third of the port is used for light guides which might be removed after 2023.
Details remain TBD.
N.Oyama, PID U2JYv4.0, 2018
3 / 7
Notes: Recent meeting, we found the question of what could be the access point. This remains to be decided. Other than that, there seems to be sufficient space for the diagnostic and no further problems have been identified. The experimental team will begin discussing this by 2021.
Final decissions regarding light guides will come after 2023.

## Slide 5: Feasibility study in JT-60SA
R = 4216 mm
R = 4954 mm
+
Launching position
P18 port
A first feasibility study was conducted in order to determine the existence of a geometric solution (launching angles, position) for the DR to probe a likely JT-60SA scenario in the region and range of k⊥ values of interest.
As a working hypothesis, a launching position at one of the lower ports of the P18 diagnostic flange has been considered, between the vacuum vessel and the stabilising plate. Final launching position still TBD.
  Selected launching position coordinates :
  R = 4500 mm, z = -640 mm
  Results do not depend strongly on the precise position of the antenna.
  Other potential launching positions could be evaluated
N.Oyama, PID U2JYv4.0, 2018
4 / 7

## Slide 6: Feasibility study: Ray tracing
A first feasibility study was conducted in order to determine the existence of a geometric solution (launching angles, position) for the DR to probe a likely JT-60SA scenario in the proposed region and range of k⊥ values.
Ray tracing code TRAVIS has been used to determine optimal launching angles for the proposed frequency bands.
  The criteria were:
  Minimize k|| to at most, k||/k⊥ < 0.1 (required for acceptable S/N ratio)
  Reflection layers close to the OMP (ballooning character of turbulence suggest optimum S/N levels)
  Single-axis rotation in steering mirror (minimize complexity of mechanical system)
  k⊥rs in the 1-10 range (ITG/TEM turbulence)
4 / 7

## Slide 7
L. Garzotti et al., NF 2018
Taking into account recent scenario predictions, three distinct regions of interest are foreseen:
- Observation of core turbulence
r < 0.8, ne ~ 4-7.5 1019 m-3
Examples: TEM turbulence, ITB formation.
- Observation of pedestal region:
r > 0.8, ne ~ 2-5 1019 m-3
Example: L-H transition, ETB formation.
- Observation of SOL region:
r > 1, ne < 2 1019 m-3
Example: SOL Er, filamentary activity.
This presentation covers the first two regions. The SOL observations are being developed by T. Tokuzawa (R.O.).
Standard H-mode scenario
Regions of interest
Advanced steady state, high power scenario
5 / 7

## Slide 8: Results: High density scenario
E-band
W-band
q = 24.3º
q = 29.1º
q = 34.1º
q = 39º
q = 43.9º
Freqs at equatorial plane
  Central region can be completely covered by W-band in O-mode.
  Edge (up to LCFS) can be covered by E-band in X-mode.
  This way, k⊥, core = 5-30 cm-1 and k⊥, edge= 3-20 cm-1 can be obtained with k||/k⊥< 0.1
6 / 7

## Slide 9: Results: Hybrid scenario
2xfec absorption
W-band
E-band
q = 24.3º
q = 29.1º
q = 34.1º
q = 39º
q = 43.9º
  Central region can be completely covered by E-band in O-mode.
  Edge (up to LCFS) can be covered by E-band in X-mode.
  This way, k⊥, core = 5-25 cm-1 and k⊥, edge= 5-25 cm-1 can be obtained with k||/k⊥< 0.1.
  W-band is strongly absorbed by the 2nd EC harmonic in X-mode.
Freqs at equatorial plane
6 / 7

## Slide 10: Current status of conceptual design
A viable conceptual design has been found for a V/W band DR:
Monostatic system. 30 mm beam waist @ cut off position for 90 GHz (1.4 m distance).
The whole system is contained in a 200 mm diameter port plug.
Q-band might be fitted in the second circular port (T. Tokuzawa)
Space limitations impose a number of critical restrictions:
Only one band at a time can be used (only core/edge observation).
The system only admits one polarization mode (O/X).
There is not enough space for antenna steering (no spectrum measurements).
  Directional coupler (E-band)
  Port plug
  Ø 200 mm
  Optimized antenna
  Elliptic
  mirrors
  RF windows
  RX
  TX
7 / 7
Notes: E-band for V/W operation. Q-band would go in the other port?
Chocked-corrugated antenna can be designed to fit in the space for the V-W bands.
Exact beam waist/distance to be optimized. Gaussian telescope design makes this result theoretically independent of frequency.
Mirrors still need optimization. Now, f= 100, 400 mm, diameter ca. 100 mm, z=+-50, horizontal distance 500 mm.
Strong angle may depart beam from gaussianity.

## Slide 11: Current status of conceptual design
A viable conceptual design has been found for a V/W band DR:
Monostatic system. 30 mm beam waist @ cut off position for 90 GHz (1.4 m distance).
The whole system is contained in a 200 mm diameter port plug.
Q-band might be fitted in the second circular port (T. Tokuzawa).
A better scenario involves access to the whole 700-400 mm space:
All features could be implemented (SOL/core/edge, steerable mirror,…).
Probably, the whole space wouldn´t be needed. Flexible solutions, involving aditional diagnostics, continuation of light guides would be possible.
  Directional coupler (E-band)
  Port plug
  Ø 200 mm
  Optimized antenna
  Elliptic
  mirrors
  RF windows
  RX
  TX
7 / 7

## Slide 12: Current status of conceptual design
A viable conceptual design has been found for a V/W band DR:
Monostatic system. 30 mm beam waist @ cut off position for 90 GHz (1.4 m distance).
The whole system is contained in a 200 mm diameter port plug.
K-band might be fitted in the second circular port (T. Tokuzawa).
A better scenario involves access to the whole 700-400 mm space:
All features could be implemented (SOL/core/edge, steerable mirror,…).
Probably, the whole space wouldn´t be needed. Flexible solutions, involving aditional diagnostics, continuation of light guides would be possible.
  Directional coupler (E-band)
  Port plug
  Ø 200 mm
  Optimized antenna
  Elliptic
  mirrors
  RF windows
  RX
  TX
A Doppler reflectometer in JT60-SA is possible: Our analysis has identified several working solutions which could address the physics program.
In order to go into further detail, we need more detailed information regarding available space.
7 / 7

## Slide 13
Additional Slides
Notes: 13
13
13
13
13
13
13
13
13

## Slide 14: Feasibility study in JT-60SA
A first feasibility study has been conducted in order to determine the existence of a geometric solution (launching angles, position) for the DR to probe a likely JT-60SA scenario in the proposed region and range of k⊥ values.
As a working hypothesis, a launching position at one of the lower ports of the P18 diagnostic flange has been considered. Final launching position still TBD. Two scenarios from the scientific plan have been considered:
High density
Hybrid
8 / 14

## Slide 15
A first feasibility study has been conducted in order to determine the existence of a geometric solution (launching angles, position) for the DR to probe a likely JT-60SA scenario in the proposed region and range of k⊥ values.
Ray tracing code TRAVIS has been used to determine optimal launching angles for the proposed frequency bands.
＋
＋
poloidal view
top view
9 / 14
Feasibility study: Ray tracing

## Slide 16: Turbulence-GK simulation comparison
T. Happel et al., 13th Int. Reflect. Workshop, 2017 & T. Happel et al., PPCF 2017
In AUG, the turbulence field has been calculated using flux-tube, non-linear GENE simulations.
Using said field as an input for 2DFW code, a synthetic DR output is obtained.
This allows for a direct comparison of DR output and GK turbulence predictions.
3 / 14

## Slide 17: Rotation and NTV
Suficient rotation is required for high-b MHD stability.
Predictive simulations show that NTV torque may be equivalent to that of NBI drive when axisymmetry is lost.
Strong impact in rotation, which will be substantially reduced.
Simulation-experiment comparisons are required to validate models.
Er may also be relevant for impurity transport
For large enough deviation of axisymmetry, impurity transport might become driven by Er, as typically in stellarators.
M. Honda et al, NF, 2014
A. J. Cole et al, NF, 2011
DIII-D
JT-60SA (AI scenario), TOPICS simulation
5 / 14

## Slide 18: Main Features of a Doppler diagnostic
Turbulence measurements
Good for quantitative analysis: k⊥-selective, radial scans of the amplitude of local density fluctuations. By correlation studies, average size and tilt of turbulent structures can be measured.
Good coverage: by using an steerable mirror, a range of k⊥ values can be probed. Typical values are in the k⊥rs ~ 1-10, appropriated to observe ITG and TEM turbulence.
Good temporal, spatial, spectral resolution: typical values are Dtturbulence < 1 ms, Dr ~ 1 cm, D k⊥ ~ 1 cm-1. Typical radial range covers SOL, edge and core (r > 0.5, see later).
Good comparison to gyrokinetic models: by implementing GK model output in a full-wave code, a direct comparison between simulation and experiment is posible.
2 / 14

## Slide 19: k-spectra characterization
A number of rays are launched on the optimal plane to simulate different launching angles from a steerable mirror.
11 / 14
  O-mode, 60 GHz
  azimuth angle
  elevation angle
  k|| = 0
  k||/k⊥ = 0.1

## Slide 20: Results: High density scenario
E-band
W-band
q = 24.3º
q = 29.1º
q = 34.1º
q = 39º
q = 43.9º
Freqs at equatorial plane
  Central region can be completely covered by W-band in O-mode.
  Edge (up to LCFS) can be covered by E-band in X-mode.
  This way, k⊥, core = 5-30 cm-1 and k⊥, edge= 3-20 cm-1 can be obtained with k||/k⊥< 0.1
6 / 7

## Slide 21: Results: Hybrid scenario
2xfec absorption
W-band
E-band
q = 24.3º
q = 29.1º
q = 34.1º
q = 39º
q = 43.9º
  Central region can be completely covered by E-band in O-mode.
  Edge (up to LCFS) can be covered by E-band in X-mode.
  This way, k⊥, core = 5-25 cm-1 and k⊥, edge= 5-25 cm-1 can be obtained with k||/k⊥< 0.1.
  W-band is strongly absorbed by the 2nd EC harmonic in X-mode.
Freqs at equatorial plane
6 / 7