## Slide 1: EDICAM: from commissioning to routine use – Part I
Tamás Szepesi
Á. Kovácsik*,
G. Kocsis, T. Szabolics, S. Zoletnik,
Centre for Energy Research
*Institute for Nuclear Techniques
Budapest, Hungary
Status
EDICAM overview
EDICAM capabilities
  Slow framing
  Fast framing

## Slide 2
T. Szepesi | PPM-7 | 2020.04.01. | Page 2
EDICAM delivered to Naka on 22 July 2019
On-site works before installation
  Unboxing, first tests
  Training of local staff
  Individual linkage test
    → communication with DCS, data transfer to server
  Integrated linkage test (all systems together)
    → partly failed due to COVID-19 (travel restrictions)
  SW/HW updates
    → SW update failed due to COVID-19 (travel restrictions)
Port plug and diagnostic installation
  Vacuum leak of P18 port → significant delays, repair finished at 27/03
  Installation foreseen for 10 April
Status of installation and commissioning

## Slide 3
T. Szepesi | PPM-7 | 2020.04.01. | Page 3
Single channel wide-angle fast video diagnostics
Features
  Field-of-view: 80° (wide-angle)
  Tangential view
  Temporal resolution: 100 Hz
     max. 400 Hz full frame, up to 20 kHz for ROIs
  Spatial resolution: better than 13 mm (over 3-8 m distance)
EDICAM overview – Design parameters

## Slide 4
T. Szepesi | PPM-7 | 2020.04.01. | Page 4
Advanced camera control: multiple ROIs, non-destructive readout
Define several regions to be observed (max. 6)
  different size and position
  independent timing
  NDR = sensor content is not erased
EDICAM capabilites – Multi-ROI features
CMOS chip
ROI 2
ROI 1
time
pixel brightness
ROI 2
ROI 1
Exposure cycle
Exposure
Reset

## Slide 5
T. Szepesi | PPM-7 | 2020.04.01. | Page 5
EDICAM capabilites – Multi-ROI features
time
pixel brightness
reset & readout
NDR readouts
Stationary objects:
Advanced camera control: multiple ROIs, non-destructive readout
Exposure
Reset

## Slide 6
T. Szepesi | PPM-7 | 2020.04.01. | Page 6
EDICAM capabilites – Multi-ROI features
Advanced camera control: multiple ROIs, non-destructive readout
Exposure
Reset
time
pixel brightness
reset & readout
NDR readouts
Moving objects:

## Slide 7
T. Szepesi | PPM-7 | 2020.04.01. | Page 7
EDICAM capabilites – Multi-ROI features
Advanced camera control: multiple ROIs, non-destructive readout
Moving objects:
Recover fast movements. Limitation: overexposure.

## Slide 8
T. Szepesi | PPM-7 | 2020.04.01. | Page 8
Camera is controlled by FPGA
All data is flowing through the FPGA
  offers real-time image processing
Events
  → intensity threshold on image
  → time
  → external input (TTL)
Actions
  de/activate ROI
  start/stop data archiving
  external trigger (TTL)
EDICAM capabilites – Event detection
FPGA
cam.head
10 Gbit/s fiber link
Modular design:
camera head + FPGA card
Small
Durable
Image processing
Events

## Slide 9
T. Szepesi | PPM-7 | 2020.04.01. | Page 9
EDICAM capabilites – W7-X experience
Inner heat shield
Vertical divertor
Outboard
Horizontal divertor
R
z
Plasma boundary

## Slide 10
T. Szepesi | PPM-7 | 2020.04.01. | Page 10
Plasma monitoring: size, position
Full frame, 50-200 Hz → ROI 1 (convention)
  Plasma and machine overview.
  Plasma size: is the plasma large enough? Is it touching the limiter/divertor?
EDICAM capabilites – Slow framing
200 Hz
W7-X plasma grows to full size (limiter version)
Fully developed
W7-X plasma
Divertor strike lines are visible.

## Slide 11
T. Szepesi | PPM-7 | 2020.04.01. | Page 11
Plasma monitoring: size, position
EDICAM capabilites – Slow framing
100 Hz
W7-X plasma
Density-radiation limit reached, plasma size is not stable.

## Slide 12
T. Szepesi | PPM-7 | 2020.04.01. | Page 12
Plasma monitoring: size, position
Sophisticated plasma boundary analysis: synthetic diagnostic
  Very basic modelling of visible radiation: assume uniform light source
EDICAM capabilites – Slow framing
Add offset (R,z)
Plasma position can be determined as well.
Projection of flux surface onto image
Color = toroidal position
synthetic image
measurement

## Slide 13
T. Szepesi | PPM-7 | 2020.04.01. | Page 13
Hot-spot detection – machine protection
(Unwanted) plasma-wall interaction: visible light emission
  Heat load cannot be determined!
  But (after)glow can be seen (T > 6-800°C)
  → important to record few sec after plasma
Universal hot-spot detection
  Location can be anywhere
  → Needs full frame ROI
  Present method: manual inspection
EDICAM capabilites – Slow framing
100 Hz
W7-X plasma
Hot-spot on shielding house

## Slide 14
T. Szepesi | PPM-7 | 2020.04.01. | Page 14
Hot-spot detection – machine protection
Dedicated hot-spot detection
  Location is known before discharge (e.g. reciprocating probe)
  → full frame ROI can be OK, but smaller/faster ROI possible
  Detection can be automated
EDICAM capabilites – Slow framing

## Slide 15
T. Szepesi | PPM-7 | 2020.04.01. | Page 15
UFO detection
UFO = hot-spot with changing location
  Difficult to detect and follow
  → can move toroidally (in/out) of view
  Manual inspection required
EDICAM capabilites – Slow framing

## Slide 16
T. Szepesi | PPM-7 | 2020.04.01. | Page 16
EDICAM capabilites – Fast framing
Observing edge turbulence – filaments in W7-X
Structures elongated along magnetic field lines → visible with exp. times < 50 µs
→ intense edge radiation due to unconditioned first wall
[S. Zoletnik et al, RSI 89 (2018) 013502]
[G. Kocsis et al, EPS 2017]
No direct observation of filaments
use correlation methods
calculate phase and coherence between two EDICAM cameras
→ high coherence (> 0.8)
→ linear phase
We observe the filaments

## Slide 17
T. Szepesi | PPM-7 | 2020.04.01. | Page 17
EDICAM capabilites – Fast framing
Utilization of multiple ROIs in the non-destructive readout mode
the EDICAM system can handle upto 6 ROIs simultaneously ≡ 6 cameras
time
pixel brightness
expo
reset
NDR readouts
NDR readouts
20171115.039
Helium plasma
Pellet injection
ROI #1: full frame, 100 Hz
Here: still image
ROI #2 and #3:
Small area (160x100), 10 kHz
Pellet penetration is temporally resolved!
Event → only during pellets