## Slide 1: EDICAM: from commissioning to routine use – Part II
Tamás Szepesi
Á. Kovácsik*,
G. Kocsis, T. Szabolics, S. Zoletnik,
Centre for Energy Research
*Institute for Nuclear Techniques
Budapest, Hungary
Set-up for 1st campaign
Planned applications
EDICAM for ECWC
Available software tools
Commissining, work plan
Plan B

## Slide 2
T. Szepesi | PPM-7 | 2020.04.01. | Page 2
Set-up
Wide-angle view: ca. 1/5 of torus
ROI 1: full frame overview
  → 1280x1024 @ 100 Hz
ROI 2, 3, …
  → fast observations
Aim: make calibration image
with illuminated torus
→ refine ROIs using real image
EDICAM for the first campaign
ROI 1
Full frame 100 Hz
ROI 2 (e.g. breakdown)
10,000 Hz
ROI 3 (e.g. limiter)
1000 Hz
FOV~80°

## Slide 3
T. Szepesi | PPM-7 | 2020.04.01. | Page 3
Plasma size and position
ROI 1: 1024x1280 @ 100 Hz
  → control-related issues can be resolved
    ECRH shinethrough
    radiation collapse
    detachment
    asymmetries (poloidal)
EDICAM for the first campaign

## Slide 4
T. Szepesi | PPM-7 | 2020.04.01. | Page 4
Plasma size and position
ROI 1: 1024x1280 @ 100 Hz
  → control-related issues
    ECRH shinethrough
EDICAM for the first campaign
W7-X plasma
Loss of ECRH absorption
Observed pattern for JT-60SA: more like a toroidal belt

## Slide 5
T. Szepesi | PPM-7 | 2020.04.01. | Page 5
Plasma size and position
ROI 1: 1024x1280 @ 100 Hz
  → control-related issues
    radiation collapse
EDICAM for the first campaign
W7-X plasma
Radiation collapse
Source of impurities may be identified as well – if within the view.

## Slide 6
T. Szepesi | PPM-7 | 2020.04.01. | Page 6
Plasma size and position
ROI 1: 1024x1280 @ 100 Hz
  → control-related issues
    detachment
EDICAM for the first campaign
W7-X plasma
Transition to detachment
Clear change is plasma size and divertor radiation pattern.
Similar behavior is expected at JT-60SA.

## Slide 7
T. Szepesi | PPM-7 | 2020.04.01. | Page 7
Plasma size and position
ROI 1: 1024x1280 @ 100 Hz
  → control-related issues
    poloidal asymmetries
EDICAM for the first campaign
W7-X plasma
MARFE-like event
Asymmetries, as well as possible sources can be identified.

## Slide 8
T. Szepesi | PPM-7 | 2020.04.01. | Page 8
Safety-related issues
ROI 1: 1024x1280 @ 100 Hz
  → hot-spots
  → UFOs
EDICAM for the first campaign

## Slide 9
T. Szepesi | PPM-7 | 2020.04.01. | Page 9
Breakdown studies
ROI 2: 640x64 @ 10 kHz
  → plasma blow-up can be resolved
EDICAM for the first campaign
W7-X breakdown
Compound movie
ROI 1: 100 Hz
ROI 2, 3: 5 kHz

## Slide 10
T. Szepesi | PPM-7 | 2020.04.01. | Page 10
Other fast measurements
ROI 2, 3, …
We need experience with the new machine!
EDICAM for the first campaign

## Slide 11
T. Szepesi | PPM-7 | 2020.04.01. | Page 11
Use for ECWC: in W7-X it could be observed
ROI 1: 1024x1280 @ 100 Hz
  → similar to other plasmas
  → faint radiation
  → lower frame rate?
EDICAM for the first campaign

## Slide 12
T. Szepesi | PPM-7 | 2020.04.01. | Page 12
JVIDACS-JEDIDAQ
  camera set-up and control
  live view
  playback (from PC storage)
IDL movie viewer
  playback (from PC storage)
  display total image intensity for whole movie
  zoom, flip/rotate, false color, gamma, brightness
  background correction, median filter (despeckle)
  export single images (with corrections)
Specific investigations
  IDL
Available software tools

## Slide 13
T. Szepesi | PPM-7 | 2020.04.01. | Page 13
EDVIS (EDICAM visualization software)
  based on Python
  can display and playback 10 movies simultaneously, time sync-ed
  display total image intensity for all movies
  supports multi-ROI format of EDICAM (HDF5 file)
  supports many external formats (mpeg, avi)
  zoom, flip, rotate, false color, gamma, brightness
  background correction
  generate time traces from movies (e.g. software ROI total intensity)
  display plasma discharge data (t.b.d.)
  export images and movies
Available software tools

## Slide 14
T. Szepesi | PPM-7 | 2020.04.01. | Page 14
No missions foreseen to Naka before campaign
The ”start-up team” shall arrive 1-2 weeks before first plasma
  Blow off the dust and wake up the system (6 months)
  Test spare power supply kit
  Make an additional linkage test if possible
    → in any case: test the data acquisition
  Establish working environment
    → check available software (IDL), data access
In-campaign commissioning
  Gain experience with JT-60SA plasmas and how machine looks like
  Set up additional ROIs
  Develop events – if needed
Commissioning, work plan

## Slide 15
T. Szepesi | PPM-7 | 2020.04.01. | Page 15
In case we cannot travel to Naka (e.g. virus crisis)
Send spare components by post
  QST personnel not trained for installing/testing
Close supervision of on-site camera operator team is necessary
  VC connection for camera setup and operation
    → to find good camera settings
  Remote access to EDICAM computers (at least PC1)
EDICAM commissioning only in late shift!
  So that we can VC from Europe
Plan B