## Slide 1: Status of TCVX23 experiment modelling in Soledge3x: last updates.
V. Quadri, P. Tamain, Y. Marandet, H. Bufferand, N. Rivals, R. Düll, G. Ciraolo, H. Yang, K. Galazka, G. Falchetto, and the SOLEDGE3X team all.

## Slide 2: What is new in the fluid model: the neutrals sink
Convection – diffusion
hp: referred to charge exchange-dominated region ()
(ref. Horsten et al, 2017, Nuclear Fusion 57, 116043)
+ flux limiter for neutrals
The whole wall is now pumping neutrals, providing a sink everywhere
The gain is visible in terms of amplitude of neutrals density in the corners.
Charge exchange is still pushing away neutrals from plasma: they tend to accumulate in the region where there is no plasma. We can observed a bit of accumulation on the outer target.
Sink
No sink
Enfaced limits:
Long distributed source along divertor legs (but not so crazy)
Strong accumulation of neutrals on the corners
Not reliable distribution of the neutrals density.
What matters is the distribution of ionization source

## Slide 3: Does the sink has an impact?
The sink has improved slightly the neutrals distribution.
 | Puff EIRENE | Puff FN with Sink
 | - | 
 | - | 
 | Puff EIRENE | Puff FN with Sink
 | - | 
 | - | 
Troubles in simulating low density (for , the solution goes towards instabilities  under investigation by slowly decrease the targets, not reliable.
The trends with fluid neutrals are in the right direction
The quantitative value can be significantly off, on the temperature at low throughput, on the density at high throughput
High values of puffs for FN (lack of molecules dynamics).
Comparison of FN with and without sink + EIRENE at different throughputs via a feedback scheme
The feedback scheme applied is not a model for predictive studies of the throughputs.

## Slide 4: 2D mean field case (): quality of FN compared with EIRENE.
EIRENE
FN
1e18
FN is able to emulate a sort of detachment, at the condition of the experiments (TCVX23 does detach at .
Plasma density and temperature for FN higher in front of the targets with respect EIR
The detachment arrives early than with EIRENE, since we have not ballistic neutrals (as soon as we get a bunch of neutrals, the interactions start in front of the targets).
EIRENE
FN
the neutrals density distribution improved but still not realisticis not the diffusive quantity in the model - does).
Realistic localization of the ionization source (despite is a bit more elongated all along the legs)

## Slide 5
Ability to get through density regimes means the basic physics of the detachment is preserved: we do dissipate momentum and energy: the model is already acceptable to qualitatively describe interactions with turbulence in 3D.
Interesting is to get to the particle balance from the 2D mean fields already with drifts and then turning on the turbulence: this might help to have a proper plasma background in 3D!
2D mean field case (): useful for the challenge of different time scales for turbulence and particles in 3D
We are able to transit in 3D with turbulence very quick
but still under investigation!
time steps

## Slide 6: Sum up of the outcomes and next steps
The comparison made in 2D has been useful for testing the goodness of the fluid model with respect to EIRENE and seems promising even for restarting turbulent case already at the global balance.
The fluid model adopted is still ameliorable but good enough for the analysis on the impact of neutrals on turbulence: the addition of the sink mitigates the accumulation of the neutrals at the corners and the localization of the recycling source is consistent, enabling some kind of detachment physics.
Next steps:
Stabilizing (some crashes occur at this time) and running longer the 3D cases to reach a proper correlation time of turbulence for the analysis on a statistical pov.
Understanding what is happening at low densities.
We would be happy to share EIRENE data to whoever is interested into!