## Slide 2: BLISS Beamline Control and Data Acquisition
Outline
  Instrument Control
  Data Acquisition
  Data Access
  FAIR Data
  Conclusion
Jens Meyer on behalf of the ESRF Software Group

## Slide 3: ESRF Beamlines and Experiment Types
    33 ESRF beamlines and 13 CRG beamlines
46 Beamlines
More than 100 scientific techniques

## Slide 4: ESRF Experimental setups

## Slide 5: Bliss : Instrument control and data acquisition
Command line driven data acquisition sequencer written in Python
Main concepts
      Hardware abstraction layer for all instrumentation used during a data acquisition sequence
        Motors, counters, monochromators, spectrometers, diffractometers, etc.
      A generic scan engine for step and continuous scans
        The use of trajectories and HKL space is possible with all scans
      Decoupling of data acquisition from data saving and analysis
        All data buffered in memory. Allows higher acquisition speed without blocking
      Coherent HDF5 storage of all acquired data at high speed and for large data volumes
        All data of a proposal, its samples and the produced datasets is saved as a coherent HDF5 data tree
      Live data display of all acquired data
        Immediate visibility of acquisition results for the user
      Easy configuration of hardware and experimental environment
        Switch between predefined acquisitions set-ups on the fly
      PyTango to interface any device from the Tango world
        https://www.tango-controls.org
https://bliss.gitlab-pages.esrf.fr/bliss/master

## Slide 6: Hardware abstraction
Direct hardware access or underlying control system?
Motors
2D Detectors
P201 card
Counter Controller
BLISS
Data Acquisition System
0D Counters
Tango Software Bus
Galil
Motor Controller
Motors
Tango Controller
2D Detectors
Tango Controller
Eiger
Tango Server
PCO
Tango Server
ETEL
Tango Server
Galil
Tango Server

## Slide 7: Hardware abstraction
BLISS Hardware Abstraction Frameworks

## Slide 8: BLISS Software architecture
Schematic view of the BLISS software layers

## Slide 9: BLISS Software architecture
Decoupling of data acquisition from data saving and analysis

## Slide 10: Building A continuous scan
Motor:samp_x
Timer
MCA
spectrum
Lima
image
Keithley
scalar

## Slide 11: Building A continuous scan
Writing a scan is writing an AcquisitionChain
  AcquisitionChain is a tree of AcquisitionObjects with master/slave relations
Scan specific
Measurement Group
MotorMaster
MusstAcqMaster
LIMAAcqMaster
MCAAcqMaster
CounterTimerAcqMaster
MCARoiCounter
MCAStatCounter
LIMARoiCounter
LIMARoiSpectrum
Synchronization electronics
2D detectors
1D detectors
0D detectors

## Slide 12: Building A continuous scan
SoftwareAcquisitionMaster : For counters that cannot be synchronized
      Epoch counter provided to link the acquisition of the 2 masters
Scan specific
Measurement Group
SoftwareTimerMaster
SamplingCounters
Hardware
synchro
Software
loop
MotorMaster
MusstAcqMaster
LIMAAcqMaster
MCAAcqMaster
CounterTimerAcqMaster
MCARoiCounter
MCAStatCounter
LIMARoiCounter
LIMARoiSpectrum
Synchronization electronics
2D detectors
1D detectors
0D detectors

## Slide 13: Why Bliss?
Flint - Live Data Display
    Live scan data
    Calculated data can be pushed to Flint

## Slide 14: BLISS Software architecture
Decoupling of data acquisition from data saving and analysis

## Slide 15: Bliss data access
Streaming API
H5py like API for transparent on- and offline data access
      The API switches transparently to file access when data is no longer available online

## Slide 16: Online data analysis - EWOKS

## Slide 17: Online data analysis - EWOKS
      Graphical chaining of predefined processing tasks by the user
      Web GUI to build workflows
      Specific workflow tasks for every scientific domain
      Can run fully automated or manually
      Processing by CPU or GPU, locally or batch cluster
      Results can be stored or fed back to the acquisition system
Workflow System for Online Data Analysis and Reduction
  EWOKS is running in daily operation on 25 beamlines today!

## Slide 18: The proof is in the pudding
With BLISS and EWOKS the door is wide open for complex experiments
  Example on ID10: Using AI/ML to close the loop with the running experiment
L.Pithan - Closing the loop: Autonomous experiments enabled by machine-learning-based online data analysis in synchrotron beamline environments

## Slide 19: FAIR Data

## Slide 20: Why Bliss?
Integration within the ESRF Ecosystem
Sample changers, automation
Experiment GUIs

## Slide 21: conclusion
BLISS
      Ready to push-up the data acquisition frequency
      Easy integration of user software
      High flexibility to prepare complex experiments
      Online data visualization
      HDF5 saving structure, following the ESRF data policy, for all experiments
      Transparent online and offline data access for data analysis
      Decoupled data producers and data consumers. The BLISS data API can easily filled other data producers to use the same data analysis tools
EWOKS
      Workflow definitions for different science domains
      Easy automation of data reduction and online processing
      Result feedback to the running acquisition

## Slide 22: Thank You
Acknowledgements to
      The members of the software group for the development of all the different software tools
      Our colleagues from the Technical Infrastructure Division for their work on the network and data storage infrastructure
      All the beamline scientists for their feedback, patience and bug reports since the EBS start-up