## Slide 1: Concept for “ModCR” (Modular CR model for EIRENE)
D. Borodin et al.
Task status overview for internal discussion inside Thrust 2

## Slide 2
treating non-stationary effects
improving performance for simulations on ITER and DEMO scales
metastables (MS) in atoms (e.g. He)
vibrational (and rotational) states in molecules
isotopes: D2, T2, H2, DT, HD, …, Be-H/D/T, N-xxx, …
control the exploding amounts of data
EIRENE: collisional-radiative model (CRM) challenges

## Slide 3: Collisional-Radiative Models (CRM)
Grotrian diagram for atomic H (D, T)
Ry=13.6eV
Balance equations:
. . .
j, k, l, m, z, … states can be fine-superfine resolved or, opposite, bundled into few quasi-metastables (MS)
CRM = list of states + transition data
Often used:
- effective Maxwellian averaged rates

## Slide 4: CRM solvers available
CRM (technically) = reaction data + SOLVER
Most solvers solve algebraic stationary system of equations
in such cases the solver is much less valuable than the A&M data collection
this statement is underlined even by the developers of the very well established and mostly up-to-date YACORA model
CRM containing molecular species is even more complex, e.g. one needs to track more processes and more states (vibrational, rotational).
Tracking all the states as separate species demands enormous CPU and memory resources.
EIRENE pre-calculates rates for each volume cell. It also allows to pre-calculate values for various Ti/Te ratios.
D.Wünderlich and U.Fantz,
Atoms 2016, 4(4), 26

## Slide 5: New CRM Solver for EIRENE concepted
This CRM is aimed to precompute rate coefficients accounting for all parametric dependences (ne, Te, but also Ti, …) in contrast with currently used polynomial fits (AMJUEL, …) + add a number of levels/processes not accounted for at this time
The internal states (e.g. rovibrational states in molecular species) are to be tracked with a flexible a flexible control over this resolution (as separate specie or variable).
The nonstationary solution for balance equations should be the default one
(with the stationary only as a useful option).
The solver should be modular, thus usable standalone or even in various codes.
The improved A&M data input should be readable and structured (for starters JSON, potentially also HDF5). It should be pre-processed mostly automatic and easily exchanged with other codes and tools. We need tools for visualisation and testing.
  The only way to meet the exploding amounts of data from RMPS and CCC for molecules (with resolution by rovibrational states)
  IAEA GNAMPP assists, but also reveals the challenges
Not only performance and reliability to be improved, but additional physics can be provided!

## Slide 6: MS-effect for BeI (“generalised” MS 10-4s)
Effective rates:
1,2) transitions <Ex..> between "GS" and "MS"
3,4) ionizations <Iz..> from "GS" and "MS"
5,6) line intensity (PEC – photon emission coefficient), contributions from "GS" and "MS"
ADAS, Te=1eV, ne=2*1012cm-3
The system of 2 balance equations can be solved analytically . . .
MS-population tracking was introduced into ERO and demonstrated to be of significance by applications to PISCES-B, PSI-2 and JET-ILW (neutral Be, He, W)
For WI dedicated ADAS dataset was developed; various lower states bundling options (~10) tested etc.

## Slide 7: MS-effect for WI (PSI-2 linear plasma device, JET)
A.Eksaeva PhD-thesis, 2020
Ar  W
line Intensity [a.u.]
target
W0
(PSI-2)
Test in tokamak (JET ITER-like Wall): MS tracking reduces simulated line intensity by x1.7!
ERO:
λ = 400, 429, 522 nm
(PSI-2)
Ar  W
line Intensity [a.u.]
target
(PSI-2)
Multiple options for state bundling are worth considering
Dedicated ADAS’18 dataset

## Slide 8
CRM underestimates excited state population at large temperature
Standalone CRM vs EIRENE – 1 (statistic issues)
Simulations: SOURCE v=0
CRM overestimates excited state population at low temperature
EIRENE: 793’300 histories
EIRENEx10: 7’933’000 histories
EIRENEx100: 79’330’000 histories

## Slide 9
PLOUTOS (web-based) can be used to
to import/export data (JSON, tabular, etc.)
to produce input data for EIRENE and for other codes with CRMs
   load/improve/save the developed configuration (selected reactions and parameters) including starting from the standard pre-sets
to check data for consistency and abnormal features
do sensitivity studies:
   understand A&M side of the problem and identify the most significant processes (among the selected ones)
Both statues are at
Glyptothek, Munich.
www.eirene.de
EIRENE

## Slide 10
New code (also library for EIRENE): “ModCR”
Should provide BOTH standalone and build-in CRM for EIRENE
  Therefore written in modern Fortran
  Linked with Ploutos (uses the same JSON files for I/O)
    (AMJuel, HydHel, H2Vibr, etc are already inside, moreover under flexible web-powered control)
  Non-stationary approach utilising up-to-date Sundails solver (CVODE) for stiff ODE systems
    (algebraic stationary option also available for control)
The whole specie-state and reaction basis is inside, however the code should form the list of “active states”
  Determined by user in JSON parameter file (for few simulations)
  Provide different resolution on states being tracked
  Provide flexible border for tracking of MC species and internal state populations as variables
This
is unique and justifies creation of the new code

## Slide 11: ODE Solver for ModCR
SUNDIALS: SUite of Nonlinear and DIfferential/ALgebraic Equation Solvers
Developed at LLNL - awarded the 2023 SIAM/ACM Prize in Computational Science and Engineering
repository: https://github.com/LLNL/sundials
Modern, powerful and flexible – still it is available in FORTRAN (so suits to EIRENE)

## Slide 12: ModCR interaction with EIRENE and other tools
ModCR
EIRENE
CRM condensing (“ColRad”)
EIRENE
Main loop (“folneout”)
EIRENE
Post-processing (spectroscopy, etc)
Data sources
MCCC, R-matrix, …
Ploutos
YACORA
ModCR
Standalone
Interface
Flexible input files (JSON)

## Slide 13
ModCR and ColRad
Hardcoded data preparation: H_COLRAD, He_COLRAD and H2_COLRAD
ModCR is supposed to:
generalize the CRM use preparatory step for all species
link it to PLOUTOS and provide standalone simulations
take as much as possible from the ColRad development
photon tracing and other features are to be taken over into EIRENE with ModCR
We need an action plan to transform COLRAD to ModCR (code  input files…)
First species to start with in ModCR: H2 and He, next to come is D2 (and T2?..)
Be (incl. molecules) CRM in ModCR is developed for JET and testing purposes as well.
• Reads in 𝑇𝑒, 𝑛𝑒 (𝑇𝑖, 𝑛𝑖)
• Gives out 𝑆ion, Srec, Rpop
• stationary (!..) CRM

## Slide 14
ModCR and the EIRENE Main loop
ModCR is supposed to provide:
“abstract reaction“ approach and this way reduce branching
tracking of internal states as variables
user-defined “border” between states tracked as variables and as species
reverse compatibility with earlier simulations
high performance, seamless interface (so, FORTRAN)

## Slide 15
ModCR flow chat (standalone)
Input file (JSON)
CRMs
Tasks
CRM
Species
States
Transitions
Settings
Task
Manipulate CRM
Analyse CRM
Solve (set of) case(s)
Produce output
Output file1
(JSON)
Solver(s)
Output file X
Stationary
Dynamic
Analysis
New input
file (JSON)
Ploutos

## Slide 16
ModCR flow chat
Reading Input file (CRM + tasks, JSON)
Reading CRMs + extra data
Creating total list of species-rates-reactions
 sorting out and consistency checks
Performing data manipulation tasks
solver task
Sorting out the “active states” and the reduced reaction data, index abstractisation
Analysis, sorting, postprocessing tasks
ModCR output (mostly JSON, HDF5?..)
What is done by now?
reading JSON
reading PLOUTOS CRM (JSON)
reading ADAS (adf11, adf15)
incorporating of solver (CVODE++)
started with sorting of states and reactions…
Some positive implications for EIRENE already: reorganisation of external libs
ModCR interfaces to EIRENE in pre-calculation phase should be very much alike to COLRAD

## Slide 17: Thanks for the attention!

## Slide 18
background
H2+
H2 + H+ → H2++H
H2 + e → H2++ 2e
H
H2 + e → 2H + e
H2 + e → H + H+ + 2e
H2+ + e → 2H
H2+ + e → H + H+ + e
H2+ + e → 2H+ + 2e
H2(X)
ν = 0
ν = 1
ν = 2
ν = 3
ν = 4
ν = 5
SOURCE
H2(ν) + e → H2(ν±1) + e
H + e → H+ + 2e
Te=Ti=0.2÷30eV.
ne=ni=1019m-3
ne=ni=1021m-3
Plasma parameters:
AMJUEL, H2VIBR
Databases:
EU-DEMO
JET
CRM FOR MOLECULES : vibral resolution

## Slide 19: CRM FOR MOLECULES: leading reactions
low temperature (T < 2eV) leading reaction chains:
H2+H+→ H2++H H2++e → H+H++e
MAR/MAD competition at very low temperature
MAD
MAR
H2+H+→ H2++H H2++e → H+H
EU-DEMO

## Slide 20: Resolved vs. unresolved on vibrostates CRM in EIRENE
Larger molecular density (factor≃2∸3) along the separatrix with vibr. resolution.
AMJUEL: unresolved
H2VIBR: resolved

## Slide 21
New (or updated) modelling tools :
Ploutos
ModCR
Special thanks to
ADAS (M.O’Mullane et al.) for constant support
YACORA developers (U.Fanz, D.Wunderlich, et al.)
MCCC developers (D.V.Fursa et al.) for providing the database
CRM tools development

## Slide 22
Standalone CRM Ploutos: what is inside?..
CRM solver (transport excluded, pure A&M side of the problem) with extensive features
  Stationary and non-stationary solution (assuming velocity and plasma pars)
  Any specie can be treated as “Reservoir”
  “Spectral analysis” based on eigenvalue approach (which reactions are most important?)
  Sensitivity analysis – vary the plasma parameters, solver settings, reactions, etc.
Plotting, solver results visualisation
  Useful for fast consistency checks and trivial analysis while constructing the CRMs
  Good for physics analysis in case one follows established routines
Flexible reaction tables interconnected with the solver and plotting
  Optimised for consistency checks and trivial analysis while constructing the CRMs
  Input/output in various formats (new: JSON) including directly for EIRENE
  Critical things are highlighted, level of information detail controlled by the user.
  Data is grouped by the reactions (even if from various sources).
  Standard or custom initial configurations
Earlier known as “HydKin”
Power of web-based
Interface!

## Slide 23
PLOUTOS – (H2 2022/23 case)
Buttons to adjust table content

## Slide 24
Summary – improved CRMs
CRMs are essential part of MC transport codes including EIRENE
Transport and A&M sides of MC transport codes are NOT separable, however using the standalone PLOUTOS approach is often extremely useful
  Gives insight into the A&M physics
  Allows more control, looking into details and straightforward answers
  Particular valuable if standalone and external CRM would be just the same
  Isotope (D vs. H) effect demonstrates the significance of vibro-resolved MCCC data
New CRM (ModCR) is concepted and under development
  The same model should be usable standalone and inside the EIRENE
  PLOUTOS will keep and even strengthen its role as data pre-processor
  It is aimed to provide flexible “border” between particles treated as MC species or variables characterising the internal state
  Opacity and other effects should be available in ModCR, but it is too early to talk about that at the current stage.
Further tools (e.g. EIRENE input editor python-based GUI “AMJ4EIR”) are under development
Further details at www.eirene.de

## Slide 25
ColRad – plans for 2023

## Slide 26
Transport code variations and commons: CRMs
Property | EIRENE | ERO, ERO2.0
Ab initio | Yes (iterations with fluid code, e.g. with B2.5  “SOLPS-ITER”) | No, test-particle approximation on a given plasma BG (e.g. from SOLPS)
Gyro-motion | Guiding centre approximation | Full-resolved, detailed 3D wall elements, surface sheath
Plasma-wall interaction | Less detailed locally, often no 3D | More detailed: 3D, sheath, etc.
PWI impact on plasma | Yes, also “advanced fluid neutrals”, “wall reservoirs” etc. | In general NO (certain effects were introduced…)
Both approaches have clear advantages and range of appropriate tasks, both packages are highly demanded by ITER, EU-DEMO and other fusion-relevant devices!
 Moreover, they often support each other (plasma BGs from various CFD-EIRENE used and tested in ERO)
However, the subtasks for treatment of atomic and molecular processes in plasma are very similar!
Break-up of the molecular species in plasma
Ionisation and other processes affecting charge and energy, thus transport
Synthetic spectroscopy for comparison with diagnostics
Similar A&M process treatment challenges!

## Slide 27
YACORA: inclusion molecular source term
Stationary run vibrationally resolved:
Particle species
Reactions
H2 source term
proton impact
electron impact
vibrational transitions
electron impact
F.Cianfrani,
EPS-2022
YACORA + Source term
adjustable to the Edge2D-EIRENE

## Slide 28: CRUMPET, YACORA simulations (standalone CRM)
Different CR processes cause up to 60% difference in dissociation rates
Impact strongest in the Te = 0.5–4 eV range, where molecular processes strongest
Electronic transitions affect Te > 4 eV
Vibrational transitions affect Te < 4 eV
Predicted isotope effect strongest for temperatures associated with detachment onset and detached conditions
MCCC data indicates weaker dissociation of both H2 and D2 for Te > 3 eV compared to EIRENE data (AMJUEL, HYDHEL, H2VIBR)

## Slide 29: Isotop effect in „full-scale“ EIRENE (M.Groth)
Higher div. densities for T than for H plasmas observed in
JET-ILW L-mode plasmas, both exp. and in EDGE2D-EIRENE
Generic density scan with identical transport coeffs., models
Strong reduction in ion current to outer plate not yet reproduced ⇒ likely to require changes to transport coefficients
Te,OT least affected by isotope species

## Slide 30
Standalone CRM vs EIRENE: Effective source (JET)
Gas puffing
divertor region:  novel physical conditions (dominance of CX reactions at low temperature)
CRM in each simulation cell: molecule density scales linearly with the source  effective source
with isotope rescaling
M Groth et al. NF 2013
Based on
EDGE2D-EIRENE simulations
JET shot 81472

## Slide 31
The deviations from CRM are determined by molecular sources:
=
negative deviations at sources
positive deviations at sinks
X
ν = 0
ν = 1
ν = 2
ν = 3
ν = 4
ν = 5
diss./ ion.
Sout
Sref
X
ν = 0
ν = 1
ν = 2
ν = 3
ν = 4
ν = 5
diss./ion./transp.
Sin
transp.
EIRENE:
CRM:
: excitation/de-
excitation rate
Standalone CRM vs EIRENE - 2
Sin+ SEIR

## Slide 32: Standalone CRM vs EIRENE - 3
The deviations from CRM are determined by molecular sources:
=
negative deviations at sources
positive deviations at sinks
X
ν = 0
ν = 1
ν = 2
ν = 3
ν = 4
ν = 5
diss./ ion.
Sout
Sref
X
ν = 0
ν = 1
ν = 2
ν = 3
ν = 4
ν = 5
diss./ion./transp.
Sin
transp.
EIRENE:
CRM:
Sin+ SEIR
: excitation/de-
excitation rate