## Slide 1
Status of radiation transport in EIRENE
Ray Chandra
20 November 2023

## Slide 2
Several outstanding issues with code runs and physics models currently investigated
N. Horsten et al.
Separatrix location → ne,sep,omp
Fixing ne,sep,omp vs fuelling/pumping
Impact of vibrationally resolved molecules (c.f., U. Fantz, JNM 2001)
Increase of Idiv due to inclusion of Ly-a opacity (c.f., B. Lomanowski, PPCF 2020)
Transport of molecular ions
Necessary grid resolution for detached conditions
M. Groth, IAEA-TM CR Properties W & H, Vienna, Austria (2021)

## Slide 3
Ly-a opacity experimentally observed with KT1 in JET D L-mode
Constant in the optically thin case
94-98% absorption at high densities
Ad-hoc opacity factors in the model (constant, not self-consistent):
Photon transport using EIRENE!
B Lomanowski et al., Plasma Physics and Controlled Fusion 62, 6:065006 (2020)

## Slide 4
Line radiation trapping in EIRENE by including Line photons as test-particles
Analog description  D. Reiter et al., Plasma Physics and Controlled Fusion 44, 8:1723–37 (2002)
Requirements:
  Photon sources – for line radiation, excited species of atoms
  Rate coefficients – spont. Emission, absorption: line shape
  Reflections – simple specular model
Result  line absorption tallies Qext

## Slide 5
Solving the population of H excited states with collisional-radiative model within EIRENE – h_colrad.f
Based on K. Sawada et al., Journal of Applied Physics 78, 2913 (1995)
In steady-state:
M, C, F are ne,te dependent rate coefficients, explicitly coded in h_colrad.f up to n=34
Qext inserted as

## Slide 6
New plasma ionization balance and neutral H mfp from modified effective ionization rate coefficient, Seff
‘Extra’ ionization contribution from photon re-absorption, Seff,ph
Seff,cr normally read from AMJUEL or ADAS files, in this case Seff calculated internally

## Slide 7
Individual test cases for photon tracing and h_colrad
Testing h_colrad:
EIRENE 2D grid with ne and Te varied along x and y dimensions
Ne, 20 points, ~1e8 – 1e16 cm3
Te, 200 points, ~0.5 – 1e4 eV
Testing photon tracing:
EIRENE 1D cylindrical grid with 20 radial points
Homogeneous TH = 1 eV, nH = 1014 cm-3 , R = 5 cm
Simulated Ly-a and Ly-b photons (2e6) with volumetric sources (H(n=2,3) as bulk ions)
Line shape only doppler broadening

## Slide 8
Individual test cases for photon tracing and h_colrad
Testing h_colrad:
Testing photon tracing:
TSVV-5 Code Camp 21-25 November 2022

## Slide 9
Photon-gas coupling for self-consistent Qext  Seff  nH
EIRENE provides Qext to CRM, CRM provides Seff and nD* (photon sources) to EIRENE
First implementation in EIRENE version coupled to EDGE2D
(March 2023)

## Slide 10
Radiation transport applied to static plasma solutions from JET81472 D+Be EDGE2D-Eirene runs1
ne,sep = 0.6e19 – 2.2e19
Ly-alpha and Ly-beta as test-particles
Shown for low-recycling, high-recycling and detached
(ne,sep = 0.7e19, 1.2e19, 2.0e19)
1M. Groth et al., Journal of Nuclear Materials 463 (August 2015): 471–76, https://doi.org/10.1016/j.jnucmat.2014.12.030.

## Slide 11
Expected high Ly-alpha absorption rate at high neutral D density
S-1

## Slide 12
Photon absorption adds up to ~20% of total CR ionization rate in detached conditions
Ionization rate integrated over the whole plasma volume
No effect in low recycling regimes
EPS 2023 poster contribution
(July 2023)

## Slide 13
Population escape factors from EIRENE 
S-1

## Slide 14
Opacity-reduced CRM using population escape factors from EIRENE
Applied to SAWADA95 CRM
Ionization rate matches ‘exactly’ to EIRENE values

## Slide 15
Radiation transport applied to static plasma solutions from JET81472 D SOLPS-ITER runs
ne,sep = 0.6e19 – 2.2e19
Ly-alpha and Ly-beta as test-particles
Photon-gas implementation functional – tested for ne,sep = 9e18 - 12 iterations

## Slide 16
To-do lists:
Comparison with EDGE2D-EIRENE photon solutions – JET81472 static plasma opacity study (paper)
Opacity effect on electron cooling rate
Expanding h_colrad for H2 and H2+ contribution to H*
Full SOLPS-ITER simulation for new predictions of JET81472
Grid parallelization for future large CRM calculations
  - For H Lyman lines, MC part still the dominant cpu time

## Slide 17
Solving the population of H excited states with collisional-radiative model within EIRENE – h_colrad.f
Based on K. Sawada et al., Journal of Applied Physics 78, 2913 (1995)
In steady-state:
M, C, F are ne,te dependent rate coefficients, explicitly coded in h_colrad.f up to n=34
Qext inserted as

## Slide 18
Next2: Plasma-photon-gas coupling
Self-consistent ne,Te  new high-recycling, detached dynamics (hopefully better Idiv prediction)
Connect with EIRENE input parallelization work (Yannick, next code camp?)
Plasma code