## Slide 1: Update on integrated modelling of burning plasmas
C. Bourdelle et al
20/11/2023

## Slide 2: Fast particles and el-mag impacts in reduced models (recalling, Sept 2023)
effect | QuaLiKiz | TGLF
Thermal ion dilution | yes | yes
Shafranov shift stabilization by increase of through suprathermal pressure fraction | Yes (s-alpha equi only) | Yes (Miller equi)
Electrostatic stabilization by resonant ICRH fast ions | Yes | Yes (Bilato)
EM-stabilization (enhanced by fast-ions) | No electrostatic | Yes linearly only
Increased nonlinear EM-stabilization (zonal flow coupling) | No, ad-hoc trick | No, ad hoc trick
with and w/o FP |  | 
Direct Alfven modes impact on equilibrium | no | no
effect | QuaLiKiz | TGLF
Thermal ion dilution | yes | yes
 | Yes (s-alpha equi only) | Yes (Miller equi)
Electrostatic stabilization by resonant ICRH fast ions | Yes | Yes (Bilato)
EM-stabilization (enhanced by fast-ions) | No electrostatic | Yes linearly only
Increased nonlinear EM-stabilization (zonal flow coupling) | No, ad-hoc trick | No, ad hoc trick
with and w/o FP |  | 
Direct Alfven modes impact on equilibrium | no | no

## Slide 3: Ad hoc tricks to mimic NL stabilization (recalling, Sept 2023)
Input local decreased by local [Casson NF 2020]
For JET NBI+ICRH heated discharges, both thermal + fast-ion-enhanced EM-stabilization correlates with fast ion content
Simple mock-up works surprisingly well across multiple regimes.
  Particularly important in hybrid scenarios
  Critical for successful reproduction of D-reference discharges for DT campaign
  Used in successful DT predictions of in high-performance discharges
Similar in practice to ASTRA-TGLF ad-hoc model [Reisner NF 2020]: Fictious (
Neither approach is rigorously physics based
  Extrapolation to electron-heated reactor conditions more than questionable! Rather impossible!

## Slide 4: Nonetheless project to explore ad-hoc trick interplay with EP redistribution model, to look at non-linearities (C. Bourdelle, Ph Lauber et al)
Since HFPS is an ITER tool, we propose to debug and test the workflow on an ITER Q=10 case (Florian’s case in Mantica's paper). Also modelled using GENE-QLNN Citrin NF2023
  Modify the transport model used so far, including turbulent transport of heat and particle using QLK ad-hoc EP stabilization.
  Make sure the proper IDS are read/written btw the workflows: (https://jira.iter.org/browse/IMAS-4297 )
    output produce alpha particle density and pressure,
    input allow for EP modified diffusion coefficients
  run at least a 10 s time frame with the QLK+ad-hoc model for heat and particle and the FP workflow computing the linear stability and modifying the FP diffusion
  study the potential non-linearity and identify some actuators (for example initial q profile? ECCD deposition? )
Start a DEMO scenario advised by Florian Koechl then switch on the FP workflow as done on ITER case
(recalling, Sept 2023)

## Slide 5: A parte, this ITER Q=10 case was also modelled using JETTO + GENE-QLNN (electrostatic without EP!) Citrin PoP2023
proof-of-principle of a heat and particle transport GENE quasilinear (QL) NN transport model.
Linear GENE runs on input parameters taken from the final state of the integrated modeling JETTO-QuaLiKiz
Dedicated nonlinear runs at midradius to validate a custom saturation rule
QL transport flux database fit with NN models.
GENE-QLNN in JETTO
NB: at this stage no plan to do local el-magnetic GENE NN, since global effects matter for burning plasmas, therefore stand by on this approach for higher fidelity integrated modeling

## Slide 6: JETTO-QuaLiKiz ITER Q=10 modelling
Ref case JETTO-QuaLiKiz
Adding ad-hoc Casson stabilization i.e. local decreased by local [Casson NF 2020]
To avoid unphysical peaked pressure on-axis, leading to unphysical bootstrap current, adding ad-hoc ceff,e on-axis transport (0.5 m2/s Gaussian width r=0.15 instead of min value= 0.1 m2/s) and core fast P smoothing

## Slide 7: Impact of ad-hoc Casson on ITER Q=10 with JETTO-QuaLiKiz on Pfus +8.6% and Energy +2.9%
Ref case JETTO-QuaLiKiz
Adding ad-hoc Casson stabilization and P smoothing on-axis
646 MW
595 MW
388 MJ
377 MJ
+8.6%
+2.9%

## Slide 8: What’s next?
When EP IDS saved, we will start iteration ATEP and HFPS-QuaLiKiz+ad-hoc EP stab
To improve ad-hoc stabilization would need guidance from higher fidelity models
btot
bfast/btot
EPM need global codes
TAE, local codes OK (KBAE?)
Driving large fluxes
50%
0%
100%
ITG-TEM
KBM/AITG
Marginally unstable TAE
Stabilized ITG, reduced fluxes
?
Tf/Te=100
Tf/Te=10
guidance from domain mapping (as sketched below ?)
with global ORB5/GENE on when one can switch on ad-hoc stabilization
in integrated modelling framework