## Slide 1: Advanced fluid atom models for plasma boundary simulations
W. Van Uytven, W. Dekeyser, N. Horsten, M. Blommaert, M. Baelmans
TSVV-3: 6/3/2024

## Slide 2: Scope of current development work
Current scope
steady state
mean-field plasma model (SOLPS-ITER)
single species (all results deuterium)
no neutral-neutral collisions
no fluid molecules
Advanced fluid neutral models (AFN): fluid model for H/D/T atoms consistently derived from kinetic description for dominant CX

## Slide 3: References
Articles
  original derivation and implementation in MATLAB
    Horsten, N. et al. NF 57.11 (2017): 116043. ( + references therein)
  implementation in SOLPS and improvements for realistic cases
    Blommaert, M., et al. CtPP 58.6-8 (2018): 718-724.
    Van Uytven, W. et al. CtPP 60, 5-6 (2020), e201900147.
    Van Uytven, W. et al. NF (2022), 086023.
    Van Uytven, W. et al. NME (2022), 101255.
PhD manuscripts
    PhD N. Horsten, KU Leuven, 2019
    PhD W. Van Uytven, KU Leuven, 2023

## Slide 4: Transport model

## Slide 5: Transport model for the atoms
Continuity
atom density
atom particle source
atom particle flux density
recombination
ionization
  [PhD N. Horsten, KU Leuven, 2019]

## Slide 6: Transport model for the atoms
Momentum
stress tensor
atom viscosity
momentum source
pressure gradient
Momentum-linearized CX rate coeff.

## Slide 7: Transport model for the atoms
Perpendicular momentum
pressure-diffusion
drift-advective term
implemented and tested for first time [Van Uytven, W. et al. NME (2022), 101255]
Particle fluxes
Used for all non-drift simulations
Tested for first time on C-mod case

## Slide 8: Transport model for the atoms
Parallel momentum
First elaborate fully, then keep first-order terms assuming:
small pitch
small gradients metric coefficients
small gradients pitch
see Chapter 3 PhD N. Horsten or Appendix B PhD W. Van Uytven

## Slide 9: Transport model for the atoms
Energy equation
assume : effect of this assumption not yet investigated
See Chapter 3 PhD N. Horsten or Appendix B PhD W. Van Uytven which terms are kept

## Slide 10: Transport model for the atoms
Energy equation
In SOLPS-ITER: internal energy equation instead of total one
Combined ion-neutral energy equation
sum fluxes and sources for all ions and fluid neutrals
→ solve for common
Separate ion and neutral energy equation
sum fluxes and source for all ions & impurity neutrals
→ solve for
sum fluxes and sources for all hydrogenic neutrals
  → solve for
  [Van Uytven, W. et al. CtPP 60, 5-6 (2020), e201900147]
Pure ion energy equation
solve pure ion energy equation
assume =
not frequently used
energy convervation?

## Slide 11: Ion-neutral current
momentum exchange leads to the ion-neutral current
we denote i-n current as j(s) as in SOLPS
Assumptions for
ExB and diamagnetic ion drift
Only CX (→ no molecules in EIRENE!)
B2.5: everything from fluid side
EIRENE: mix! Va from post-processed kinetic neutrals but KCX from B2.5 (because sources are not yet scored, they will in the future)
[Van Uytven, W. et al. NME (2022), 101255]

## Slide 12: Flux limiters
Smoothly limit conductive fluxes to fraction of sound speed flux
CX-based transport coefficients undefined for low plasma density

## Slide 13: Flux limiters

## Slide 14: Boundary conditions

## Slide 15: Neutral boundary conditions
ions (D+ )
atoms (D)
ion recycling
atom reflection
atoms (D)
atoms (D)
molecules (D2)
atom-only models:
Immediate Franck-Condon dissociation
D2
D
D
Notes: TODO: trim toevoegen

## Slide 16: EIRENE sheath model
AFN recycling based on EIRENE sheath model
truncated drifting Maxwellian at sheath entrance
sheath acceleration to target
no collisions in sheath
AFN reflection of atoms
no sheath acceleration
no collisions in sheath

## Slide 17: EIRENE kinetic BCs: TRIM
For a given
incident particle
surface material
incident energy
incident polar angle
TRIM database
Probability fast reflection
PDF reflected energy
PDF reflected polar angle
PDF reflected azimuth angle
Shorthand notation: and

## Slide 18: Advanced fluid neutral boundary conditions
Incorporate TRIM reflection kernel in fluid BCs
probability fast reflection
reflection kernel
sheath-accelerated ion Maxwellian
Estimated incident atom distribution

## Slide 19: Incident atom distributions
Diffusion approximation (inspired by neutron modeling in fission)
  assume that every atom hitting the wall comes from CX with ions
  most accurate model for CX rate → ∞
  less robust if CX rate not high enough

## Slide 20: Incident atom distributions
Drifting Maxwellian
  based on fluid properties at guard cell
  for
  less rigorous
  more robust for lower CX rate
Mixed
  linear interpolation between and based on local Knudsen number

## Slide 21: Net fluid boundary fluxes

## Slide 22: Advanced fluid neutral boundary conditions
Macroscopic fast reflected+recycled fluxes
What is not fast reflected/recycled and not pumped
If we assume molecules dissociate at targets:
Velocity associated with energy of atoms from dissociation

## Slide 23: Practical implementation
write out integrals in full to get lovely expressions

## Slide 24: Practical implementation
check what can be pulled outside of integrals
numerically integrate remainder in pre-processing and store in database
What can be pulled from under integral
e.g. , …
Pre-computed databases as a function of

## Slide 25: Results

## Slide 26: Simplified ITER case

## Slide 27: ITER case with beryllium targets
Plasma profiles along outer target
With kinetic atoms
With fluid atoms + separate atom temperature
With fluid atoms

## Slide 28: ITER case with tungsten targets
Plasma profiles along outer target
Ion-atom collisionality too low

## Slide 29: Density scan: Be-Be

## Slide 30: Density scan: W-Be

## Slide 31
All previous cases with ‘mixed’ approach for incident atom assumption
Using Maxwellian everywhere gives similar results
Using Diffusion approach everywhere leads to code crash

## Slide 32: Neutral velocities C-mod case
[Van Uytven, W. et al. NME (2022), 101255]

## Slide 33: Conclusions
AFN: agreement with EIRENE much better than ever shown before
All physics based, no tuning paramters
Separate atom energy equation
  generally more accurate
  improvements often modest
    very high CX → , limited accuracy gain
    low CX → fluid model not valid
  transition cases with substantial benefit

## Slide 34: Future work
role of neutral bulk velocities in BCs, energy equation, …?
  possibly lot of additional complexity for small gain?
extend physics processes
  neutral-neutral collisions
  multi-species (D-T most urgent)
  fluid molecules
Extending BCs much easier when assuming truncated drifting Maxwellian for incident atoms

## Slide 35: References
Articles
  original derivation and implementation in MATLAB
    Horsten, N. et al. NF 57.11 (2017): 116043. ( + references therein)
  implementation in SOLPS and improvements for realistic cases
    Blommaert, M., et al. CtPP 58.6-8 (2018): 718-724.
    Van Uytven, W. et al. CtPP 60, 5-6 (2020), e201900147.
    Van Uytven, W. et al. NF (2022), 086023.
    Van Uytven, W. et al. NME (2022), 101255.
PhD manuscripts
    PhD N. Horsten, KU Leuven, 2019
    PhD W. Van Uytven, KU Leuven, 2023

## Slide 36: Back-up slides

## Slide 37: Effect of drifts on kinetic neutral solution
Standard approach → “MC-D”
Drifts in plasma model, but remove drifts from background for EIRENE → “MC-ND”
Comparing “MC-D” and “MC-ND” allows to separate effect of drifts on the neutral solution from effect of drifts on the plasma itself
[Van Uytven, W. et al. NME (2022), 101255]
Notes: Next, we will zoom in on the effect of drifts on the neutral solution itself. For kinetic neutrals, this can be done as follows:
In the standard case, we calculate the neutral solution with a high number of MC particles on a plasma background which includes the drift velocities.
We can now do the same, but remove the drift velocities from the plasma background.
By comparing these two results, we can separate the effect of the drifts on the neutrals, from the effect of the drifts on the plasma itself.

## Slide 38: i-n current in C-mod case
Qualitative agreement
Effect of i-n current on solution was very small for C-mod case
  → should be tested on other cases as well
[Van Uytven, W. et al. NME (2022), 101255]

## Slide 39: Coupled solution
inner target
20 mm before
inner target
→ with new transport term, fluid-kinetic discrepancies are no larger than they were without drifts
Full effect of drifts on kinetic neutral solution
Partial effect of drifts on fluid neutral solution
due to new advection term
Notes: The same conclusions follows when we look at the coupled plasma-neutral solution. With the new transport term included, the fluid-kinetic discrepancies are no larger than they were without drifts.

## Slide 40: Alcator C-mod case with drifts
Plasma profiles along inner target
With unadapted AFN model
[Van Uytven, W. et al. NME (2022), 101255]