## Slide 1
V. Quadri, B. McGibbon, D. S. Oliveira, P. Tamain, H. Bufferand, N. Rivals, R. Düll, G. Ciraolo, S. Sureshkumar, N. Varadarajan and the SOLEDGE3X team.
Update on status of SOLEDGE3X simulations for TCVX23

## Slide 2: Fluid neutrals in SOLEDGE3X
Reminder: EIRENE usage in 3D with turbulence – relevant resolutions not possible (memory limit)
  Circumvented recently by forcing 2D coupling to EIRENE (Diego’s presentation next time)
Using here fluid neutrals model model level 1 of Horsten et al.
Wall pumping:
neutrals flux limiter

## Slide 3: Some caveats with the fluid neutrals model as implemented
Boundary conditions: no effort to make fluid neutrals consistent with sheath and wall recycling models used in kinetic models
Some inconsistencies in source terms applied to the plasma:
-
Assumes
Assumes
“energy recycling coefficient”

## Slide 4: Status of TCVX23 simulations
2D / 3D | Neutrals model | B direction | Status
2D | Fluid and kinetic | forward | Density scan run by Virginia, published in NME, analysed in PhD thesis, data lost, currently being re-run by Bridget
3D | Fluid | forward | One attached case, one detached case, partially published in NME, analysed in PhD thesis, data lost, currently being re-run by Bridget
2D | Fluid and kinetic | reversed | Density scan run by Bridget, partially analysed in Master thesis, data lost
3D | Fluid | reversed | Initial runs performed by Bridget for 2 densities, not analysed as not converged, data lost, to be re-run (Diego)
3D | Kinetic 2D | reversed | Simulations for 2 densities on-going (Diego)

## Slide 5: TCVX23 cases: partially converged attached and detached cases (1)
Low ne, 30%
High ne, 30%
Attached
Detached

## Slide 6: TCVX23 cases: partially converged attached and detached cases (2)

## Slide 7: Reminder: change in profiles and turbulence properties
Mid-plane
Divertor
ne (m-3)
Te (eV)
Mid-plane
Divertor

## Slide 8: Detachment leads to an increase of the SOL width
Both attached and detached case show inflexion point => double exponential fit
SOL width increases both in near SOL (x1,7) and in the far SOL (x2,7) in detached case
  Due to flattening of both n (mainly in near SOL) and T profiles (mainly in far SOL)
Position of inflexion point similar for both cases

## Slide 9: A link with density shoulders?
Investigating link between profiles inflection point and effective collisionality [Carralero et al., Wynne et al.]
Effective collisionality larger than 1 in both cases all along radial profile
  Would need a lower density case to see if inflexion point disappears when
  No clear correlation between collisionality profile and location of inflexion point (crtical for ITER)

## Slide 10: Impact on classic mean-field transport coefficients
Transport coefficients reconstructed from ExB fluctuations:
Effect of detachment:
  x5 increase in
  gets negative in the divertor!
Attached
Detached

## Slide 11: Alternate mean-field transport models: heuristic
Heuristic model driven by :
Effect of detachment:
  No significant area with negative values
  ~x10 on all transport coefficients
Attached
Detached

## Slide 12: Alternate mean-field transport models: from quasi-linear theory
Model inspired from quasi-linear theory:
Attached
Detached
Effect of detachment:
  No significant area with negative values
  Diffusion x2 away from divertor, but drops to zero in divertor
  Thermodiffusion / heat pinch x2 away from divertor, x5 in divertor

## Slide 13: Reversed field: strong impact on mean-field simulations (1)

## Slide 14: Reversed field: strong impact on mean-field simulations (2)
Forward field
Reversed field

## Slide 15: Reversed field: status of turbulence cases
3D simulations restarted from 2D steady-state solutions:
  High density simulation running smoothly: ~1ms since transition => pseudo-steady-state
  Low density one difficult: crashing due to divergence of potential profile in the center (issue with matrix conditioning?) => restarted at artificially increased resistivity (factor of 4) and seems to work
Time (ms)

## Slide 16: Outlook
Virginia’s work to be presented at EPS, based on what could be scavenged from the Marconi crash (ie, not much, only figures)
  Simulations being re-run in parallel to serve at least as references for future cases
Near term priorities:
  Run 3D turbulence simulations with 2D axisymmetric kinetic neutrals (Diego)
    Compare with fluid neutrals
    Compare 3D fluid neutrals with 2D axisymmetric fluid neutrals
  Improve fluid neutrals model with by decreasing priority:
    Solve consistency issues in sources
    Move to 3-moment model
    Improve boundary conditions to mimic kinetic ones (following Horsten et al)
  Investigate impact of detachment on turbulence with improved fluid neutrals model

## Slide 17
Backup Slides

## Slide 18: Modeling TCV-X23 experiments with Soledge3x
Fig. 1 Measurements for line integrated average density passing through the magnetic axis (NEL #6) in time, target ion flux w/r NEL #6 and TCV-X23 magnetic equilibrium [courtesy of D. Sales de Oliveira et SPC team].
Why TCV-X23? Configuration which extends the scenario for turbulent codes validation up to detachment.
LSN deuterium L- Ohmic plasma discharges
longer and stable outer leg.
A specific shot in direct magnetic field (#761886) is modeled:
Two levels of density: (attached case), (detached case).

## Slide 19: Modeling TCV-X23 experiments with Soledge3x
Outlook: closer to a proper plasma background for particle balance, w/r to evolve it from scratch [V. Quadri et al, https://doi.org/10.1002/ctpp.202300146].
Convergence (~75%) still challenging, due to
  Increased resolution in 3D
  Neutrals recycling
Very slow transient phase for both plasma backgrounds, where turbulence properties are not going to evolve.
Strategy: 2D simulations served as a starter for 3D.
2D mean field simulations used to obtain the two density plasma backgrounds.
From 2D convergence, restart in 3D at higher resolution w/ turbulence.
Fig. 2 The SOLEDGE3X meshes used for 2D mean field transport (left) and 3D turbulent transport (right) [P. Tamain].
Z
R
2D
3D

## Slide 20: Plasma conditions provided by 2D mean field cases
Attached
Converged
Detached
Converged

## Slide 21: FN vs EIRENE: testing FN assumptions
1. Estimation of collisionality via
FN
EIR
same range w/ and w/out EIRENE
FN seems to rollover before EIRENE
FN fluxes amplitude much lower
2. Realistic localization of the ionization source
FN
EIRENE
FN
EIRENE
fluid neutrals model in Soledge3X will need refinements
However, still far from being perfect
Qualitative OK, quantitative NOK

## Slide 22: From 2D convergence, restart in 3D at higher resolution w/ turbulence.
Outlook: closer to a proper plasma background for particle balance, w/r to evolve it from scratch [V. Quadri et al, https://doi.org/10.1002/ctpp.202300146].
Convergence (~75%) still challenging, due to
  Increased resolution in 3D
  Neutrals recycling
Very slow transient phase for both plasma backgrounds, where turbulence properties are not going to evolve.
Transit to 3D turbulence
Statistical analysis on turbulence
2D
mean field
Transit to 3D turbulence
Statistical analysis on turbulence
2D
mean field
Fig. 3 Time traces of particle influx given by the ionization source and particle outflux for the two density cases, (left) and (right).

## Slide 23
From 2D  3D: two different densities at the sep with turbulence
Puff:
Puff:

## Slide 24: Different plasma conditions for the two density cases
Inner target
Outer target
Outer mid-plane
Fig 5. Poloidal profile at the first SOL flux surface of the time and toroidal averaged for and . Time and toroidal averaged maps of for (left) and (right).
~ 1eV!

## Slide 25: Different plasma conditions for the two density cases
Fig. 4 Time and toroidal average ionization source for (left) and (right).
High density case is detached!

## Slide 26: Different plasma conditions for the two density cases
Commonly, turbulent transport dominates transverse fluxes both in the main SOL and in the divertor.
Specific turbulent activity all along the outer divertor leg up to the target.
Turbulence structures immediately exhibit qualitatively differences depending on the density level.

## Slide 27: Time-averaged radial profiles
Fig 6. Radial profiles of the time and toroidal averaged electron density (upper) and temperature (bottom) for the two density cases, and at the outer midplane (left), outer target (cent) and mid divertor (right).
The density is globally higher where we aimed for the simulation to have higher values.
At the midplane, the profiles match the values imposed by the experiments but are still evolving.
The temperature is higher for the low-density case in the edge, and slightly higher in the near SOL.
Temperature profiles flatten in the far SOL around 10 eV.
1. Plasma properties
PFR
SOL
PFR
SOL
OMP
Outer target
Mid-divertor
PFR
SOL
PFR
SOL

## Slide 28: Impact on turbulence properties
Density fluctuations appear to increase with density itself.
However, fluctuations rate is globally larger for the low density case in the whole SOL (except some specific locations)
Relative fluctuations level of ()
2. Turbulence properties

## Slide 29: Impact on turbulence properties
The relative fluctuations are higher in the SOL, while they decrease at the separatrix where the increase in density is faster than the increase in absolute fluctuation level.
Globally, density fluctuations rate seems not so impacted: the amplitude of the fluctuations is not varying so much.
Skewness is strongly poloidal asymmetric.
Negative inside the separatrix; increasing positively for the ttached case [consistent w/ Zweben, MAST experimental dataset]
Flat and not skewed for the high density case at the MP

## Slide 30
Impact on turbulence properties
Near SOL
Far SOL

## Slide 31: Heat flux channel width
Single exponential fit
2D mean-field
3D turbulence
Fig. 8 MF & turbulence comparison of parallel heat fluxes peaks at the mid-plane for and via single exponential fit.
Single exponential fit
In turbulence simulations, the “average” in detachment has increased by a factor of 2.5.
3. Transport properties
Clear change in the profiles for MF vs turbulence.

## Slide 32: Heat flux shoulder appearance in high density case
 | [mm] |  | [mm] | 
Double exponential fit
log
3D turbulence
Appearance of a far SOL shoulder in the heat flux decay
linear fit 5E18

## Slide 33: Exctrating the diffusion maps for 2D mean field
Clear change in transport due to density regimes, with very different amplitudes.
Larger transport coefficients in the high density cases with respect to the low density case.
Particle transport is indeed strongly enhanced.

## Slide 34: Summary
Restarting from mean field simulations helps to establish turbulence on the desired plasma background.
Turbulence simulations can adequately access high-density regimes; even if not fully converged, the turbulence properties will not change significantly during a very long transient period.
Significant changes in global and local properties of both plasma and turbulence are observed transiting from low to high density regimes.
By increasing the density, a significant volume of plasma is migrating along the divertor region leading to a broadening of the SOL.
The appearance of a far SOL shoulder is observed in the detached case.
Outlook: All the data for comparison with experiments are available. What is next?

## Slide 35: mid divertor

## Slide 36: inner target

## Slide 37: absolute vs relative fluctuations 3 poloidal positions

## Slide 38: absolute + relative fluctuations 3 poloidal positions

## Slide 39: turbulence properties different poloidal locations

## Slide 40: OMP and mid divertor

## Slide 41: turb properties OMP and mid divertor

## Slide 42: OMP and mid diverto

## Slide 43: Ti turb properties

## Slide 44: Density fluc time evolution
OMP
Mid divertor
Outer strike point

## Slide 45: Different plasma conditions for the two density cases
Commonly, turbulent transport dominates transverse fluxes both in the main SOL and in the divertor.
Specific turbulent activity all along the outer divertor leg up to the target.
Turbulence structures exhibit already qualitatively differences depending on the density level.
Z

## Slide 46: Diffusion map

## Slide 47: Diffusion map

## Slide 49: Strong drop of the heat fluxes at the targets
inner target
outer target
Not possible to perform an Eich fit there