## Slide 2: Nonlinearities in plasma-neutrals interactions
Alexander S. Thrysøe, Anders H. Nielsen

## Slide 3: Nonlinearities in plasma-neutrals interactions

## Slide 4: Input vs. System Nonlinearity
Two main instances of non-linearities
Nonlinear source coupling:
  Neutral source terms (e.g., ionization, recombination, charge exchange) depend nonlinearly on local plasma and neutral particle fields such as and .
    Example:
Nonlinear plasma response:
  Even if the source perturbation is known, the plasma’s transport equations are themselves nonlinear (e.g., due to , , etc.).
    A small change in a field from neutral interaction source can lead to a disproportionate change in the plasma transport.

## Slide 5: The mean-field approximation
The mean-field approximation is applied in, e.g., multifluid codes or GPI to reduce the complexity of the system of equations from the form
  to an equation of the form
  where a temporal averaging of the fields
Due to the strong nonlinearity of transport quantities, using average values can misrepresent the dynamics between them, influenced by the statistics of fluctuating cross-field source terms*
*Havlíčková E et al 2011 J. Nucl. Mater. 415 S471–4, Thrysøe et al 2016 Plasma Phys. Control Fusion 58 044010

## Slide 6: The mean-field approximation for the source term
For the neutral interaction source term the form is typically
  where is mostly a function of
Writing as we have

## Slide 7: Input vs. System Nonlinearity
Two main instances of non-linearities
Nonlinear source coupling:
  Neutral source terms (e.g., ionization, recombination, charge exchange) depend nonlinearly on local plasma and neutral particle fields such as and .
    Compare (dynamic neutrals) to (static neutrals)
Nonlinear plasma response:
  Even if the source perturbation is known, the plasma’s transport equations are themselves nonlinear (e.g., due to , , etc.).
    Compare low and high fuelling cases

## Slide 8: nHESEL equations
nHESEL equations
  Drift-reduced Braginskii equations in 2D outer midplane domain
  Use TCVX23 profiles for plasma forcing profiles
  Synthetic high-resolution probe signals
normalized electron density

## Slide 9: nHESEL equations
nHESEL neutral equations
  Convective distinct interacting isothermal neutral molecule and atom species
normalized electron density

## Slide 10: Sources from neutral interactions
Assume two-fluid neutral atoms model (reaction rate >> thermalization rate) and fluid molecules
Assumption supported by MC neutral simulations*
atomic ionization
atomic ionization
charge exchange
charge exchange
molecular ionization
molecular dissociation
*K. Kvist, A.S. Thrysøe, T. Haugbølle, A.H. Nielsen, Phys. Plasmas 31, 032302 (2024)

## Slide 11: nHESEL simulation

## Slide 12: Electron density profile
Increasing fuelling rate from low to high leads to slightly elevated SOL electron density
No significant impact to density from dynamic vs. static neutrals

## Slide 13: Electron density profile
Increasing fuelling rate from low to high leads to elevated SOL electron density
No significant impact to density from dynamic vs. static neutrals

## Slide 14: Electron density variance
Larger variance in density signal further out in SOL for higher fuelling

## Slide 15: Electron density variance profile
Larger variance in density signal further out in SOL for higher fuelling
Mainly caused by local ionization, i.e., no reason to point to nonlinear transport effects observed

## Slide 16: Neutral density profiles
Only small increase in SOL electron density despite order of magnitude increase in neutral density

## Slide 17: Neutral density variance
Significant variance in neutral densities in response to SOL filaments

## Slide 18: Electron density source
Similar response to electron density source from increased neutral fuelling rate
No distinct difference between dynamic and static neutrals, despite large variance in neutral density
  related to anti-correlation between molecular and atomic fields in the SOL region

## Slide 19: Electron density source
Similar response to electron density source from increased neutral fuelling rate
No distinct difference between dynamic and static neutrals, despite large variance in neutral density
  related to anti-correlation between molecular and atomic fields in the SOL region
  sign of is determined by:
  Where depicts a correlation between and , and an anti-correlation

## Slide 20: Electron density source

## Slide 21: Input vs. System Nonlinearity
Nonlinear source coupling:
  Compare (dynamic neutrals) to (static neutrals) for TCVX23
  Despite fluctuations in the neutral density fields from neutral-blob interactions, the impact on electron density source is relatively small and is in this case a good approximation
  Not the case for mono-atomic neutrals or different temperature regimes

## Slide 22: Input vs. System Nonlinearity
Nonlinear source coupling:
  Compare (dynamic neutrals) to (static neutrals) for TCVX23
  Despite fluctuations in the neutral density fields from neutral-blob interactions, the impact on electron density source is relatively small and is in this case a good approximation
  Not the case for mono-atomic neutrals or different temperature regimes
Nonlinear plasma response:
  Compare low and high fuelling cases
  Higher fuelling elevates the SOL density, resulting in larger blobs and increased radial SOL particle flux
  No drastic non-linear response in probed regime in TCVX23